## Slide 1: IRL CPUs
Erik Hagersten
Uppsala University

## Slide 2
A new module Wed (Deadline Thu)
  Exceptions, x86 + vector instr, Out-of-order (also today)
One module next week (Deadline Thu)
  VLIW, Itanium, SMT, (Multicore)
Reading instructions, X-tenta etc.
www.it.uu.se/edu/course/homepage/avdark/ht13/
PhD student?

## Slide 3: Discussion & Quizzes

## Slide 4: Architectural assumptions
From To Latency
FP ALU FP ALU 3
FP ALU SD 2
LD FP ALU 1
Latency=number of cycles between the two adjacent instructions
Delayed branch: one branch delay slot
INT ALU produces the results the next cycle
FPU ALU produces the results 3 cycles later

## Slide 5
for (i=1; i<=1000; i=i+1)
x[i] = x[i] + y[i];
loop: 1.LD F0, 0(R1) ; F0 = array element x[i]
2.LD F4, 0(R2) ; F4 = array element y[i]
3.ADDD F2, F4, F0
4.SD 0(R1), F2 ; Store result
5.SUBI R2, R2, #8 ; decrement array ptr x
6.SUBI R1, R1, #8 ; decrement array ptr y
7.BNEZ R1, loop ; loop if R1 != 0
; x[i] stored ”backwards”
RAW
RAW
Where are the RAW dependencies?
I2I3; I3I4
There are none
I1I3; I2I3; I3I4
(RAW)
Q: Why stored backwards?

## Slide 6
for (i=1; i<=1000; i=i+1)
x[i] = x[i] + y[i];
loop: 1.LD F0, 0(R1) ; F0 = array element y[i]
2.LD F4, 0(R2) ; F4 = array element x[i]
stall
3.ADDD F2, F4, F0
stall
stall
4.SD 0(R1), F2 ; Store result
5.SUBI R2, R2, #8 ; decrement array ptr x
6.SUBI R1, R1, #8 ; decrement array ptr y
7.BNEZ R1, loop ; loop if R1 != 0
stall
RAW
RAW
How many cycles to execute this loop?
(if it is not optimized)
10 c
11 c
12 c
Q: Why not stall here?
Q: Why not stall between ADDDs?
ADDD F4, F0, F2
ADDD F10, F6, F2

## Slide 7: Software pipelining 1(3) Symbolic loop unrolling
LD
ADD
ST
SUB
BNEQ
LD
ADD
ST
SUB
BNEQ
LD
ADD
ST
SUB
BNEQ
LD
ADD
ST
SUB
BNEQ
LD
ADD
ST
SUB
BNEQ
Iteration 0
Iteration 1
Iteration 2
Iteration 3
Iteration 4
  Stagger the start of each iteration in the instruction scheduling
Software
Pipelined
Loop 1:
BNEQ SUB ST ADD LD
BNEQ SUB ST ADD LD
Software
Pipelined
Loop 2

## Slide 8: Software pipelining 2(3)
Example:
loop: LD F0,0(R1)
ADDD F4,F0,F2
SD 0(R1),F4
SUBI R1,R1,#8
BNEZ R1,loop
Looking at three rolled-out iterations of the loop body:
LD F0,0(R1) ; Iteration i
ADDD F4,F0,F2
SD 0(R1),F4
LD F0,0(R1) ; Iteration i+1
ADDD F4,F0,F2
SD 0(R1),F4
LD F0,0(R1) ; Iteration i+2
ADDD F4,F0,F2
SD 0(R1),F4
l
Execute in the same loop!!
SD 0(R1), F4
ADDD F4,F0,F2
LD F0, -16(R1)

## Slide 9: Software pipelining 3(3)
  Instructions from three consecutive iterations form the loop body:
  < prologue code >
loop: 1.SD 0(R1),F4 ; from iteration i
2.ADDD F4,F0,F2 ; from iteration i+1
3.LD F0, -16(R1) ; from iteration i+2
4.SUBI R1,R1,#8
5.BNEZ R1,loop
        < prologue code >
  No RAW data dependencies within a loop
  WAR ( ) hazard elimination may be needed to increase ILP
  6c / iteration, but only uses 2 FP regs (instead of 8 for unrolled)
RAW dependence to next loop
Where are the RAW
dependencies within this
loop?
I1I2
There are none
I1I2; I2I3
Q: Is this harder to parallelize?
A: Loop-carried dependencies

## Slide 10
This code write ones to a
matrix (N is large)
for (i = 0; i < N)
for (j = 0; j < N) {
x[i,j] = 1
}
Roughly how many times will the
branch prediction be wrong?
Always correct
4 times
8 times
N
2N
Initialized to
00 (not taken)
10
00
11
11
11
10
01
10
11
10
00
11
11
11
01
11
index
PC
How many misses with 1-bit
predictor?
Always correct
4 times
8 times
N
2N

## Slide 11
This code write zeroes to the
rightmost diagonal of a matrix (N is larger than 1000)
for (i = 0; i < N)
for (j = 0; j < N) {
if (j > i)
x[i,j] = 1
else
x[i,j] = 0
}
Roughly how many times will the
branch prediction be wrong?
Always correct
6 times
N times
2N
3N
4N
5N
0 1 1 1 1 1 1
0 0 1 1 1 1 1
0 0 0 1 1 1 1
0 0 0 0 ? 1 1
0 0 0 0 0 1 1
0 0 0 0 0 0 1
0 0 0 0 0 0 0
Initialized to
00 (not taken)
10
00
11
11
11
10
01
00
11
10
00
11
11
11
01
11
index
PC
How many misses with 1-bit
predictor?
Always correct
6 times
N times
2N
3N
4N
5N

## Slide 12: Adding Global History
LD
ADD
SUB
ST
>=0?
LD
ADD
SUB
ST
>1?
LD
ADD
SUB
ST
>2?
LD
ADD
SUB
ST
=0?
Y
Y
Y

## Slide 13
This code write zeroes to the
rightmost diagonal of a matrix (N is larger than 1000)
for (i = 0; i < N)
for (j = 0; j < N) {
if (j > i)
x[i,j] = 1
else
x[i,j] = 0
}
0 1 1 1 1 1 1
0 0 1 1 1 1 1
0 0 0 1 1 1 1
0 0 0 0 ? 1 1
0 0 0 0 0 1 1
0 0 0 0 0 0 1
0 0 0 0 0 0 0
Initialized to
00 (not taken)
10
00
11
11
00
10
01
10
11
index
”hash”
PC
0
0
0
Last 3 branches:

## Slide 14
This code writes zeroes to the
rightmost diagonal of a matrix (N is larger than 1000)
for (i = 0; i < N)
for (j = 0; j < N) {
if (j > i)
x[i,j] = 1
else
x[i,j] = 0
}
0 1 1 1 1 1 1
0 0 1 1 1 1 1
0 0 0 1 1 1 1
0 0 0 0 1 ? 1
0 0 0 0 0 1 1
0 0 0 0 0 0 1
0 0 0 0 0 0 0
Initialized to
00 (not taken)
10
00
11
11
00
10
01
10
11
index
”hash”
PC
0
0
1
Last 3 branches:

## Slide 15: Unrolled twice
for (i=1; i<=1000; i=i+1)
x[i] = x[i] + 10;
loop: 1.LD F0, 0(R1) ; F0 = array element x[i]
2.ADDD F4, F0, F2 ; Scalar constant “10” in F2
3.SD 0(R1), F4 ; Store result x[i]
4.LD F6, -8(R1) ; F6 = array element x[i+1]
5.ADDD F10, F6, F2 ; Scalar constant “10” in F2
6.SD -8(R1), F10 ; Store result x[i+1]
7.SUBI R1, R1, #16 ; decrement array ptr.
8.BNEZ R1, loop ; loop if R1 != 0
RAW
RAW
RAW
RAW

## Slide 16: Scheduling example
k = …
…
for (i=1; i<=1000; i=i+1) {
x[i] = x[i] + 10;
y[k] = y[k] + 10;
}
loop: 1.LD F0, 0(R1) ; F0 = array element x[i]
2.ADDD F4, F0, F2 ; Scalar constant “10” in F2
3.SD 0(R1), F4 ; Store result x[i]
4.LD F6, 0(R2) ; F6 = array element y[k]
5.ADDD F10, F6, F2 ; Scalar constant “10” in F2
6.SD 0(R2), F10 ; Store result y[k]
7.SUBI R1, R1, #8 ; decrement array ptr.
8.BNEZ R1, loop ; loop if R1 != 0
RAW
RAW
RAW
RAW

## Slide 17: Scheduling example
1.LD F0, 0(R1) ; F0 = array element x[i]
2.ADDD F4, F0, F2 ; Scalar constant “10” in F2
3.SD 0(R1), F4 ; Store result x[i]
4.SUBI R1, R1, #8 ; decrement array ptr.
5.BEQZ R1, foo ; Goto foo if R1 == 0
4.LD F6, 0(R1) ; F0 = array element x[i+1]
5.ADDD F10, F6, F2 ; Scalar constant “10” in F2
6.SD -8(R1), F10 ; Store result x[i+1]
…

## Slide 18: A 5-stage superscalar pipeline
IF
ID
EX
M
WB
IF
ID
EX
M
WB
Reg
ALU
ALU
D
B
C
A
E
One sequential
program:
L1$

## Slide 19: A 2-way superscalar 5-stage pipeline Need 2x ILP!
ALU
ALU
Mem
4/8
Can fetch up to two consecutive instr /cycle.
If deamed to be OK.
Only top pipeline may execute branches
2x reads & writes to the shared register file
Reg
2x reads & writes to the L1 cache

## Slide 20: Performance estimates for three simple ”loops”

## Slide 21: A more complicated example
DIV F0,F2,F4
ADDD F6,F0,F8
SUBD F8,F10,F14
MULD F6,F10,F8
RAW
WAR
RAW
WAW
//delayed a long time
Note: WAR and WAW (”name dependencies”) can be avoided through
”register renaming”
Register Renaming:
DIV F0,F2,F4
ADDD F6,F0,F8
SUBD tmp1,F10,F14 ;can be executed right away
MULD tmp2,F10,tmp1 ;delayed a few cycles

## Slide 22: Simple Tomasulo’s Algorithm
Order
R
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
Op:div
D:F0
S1:F2
S2:F4
#3
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Op:div
D:F0
S1:b
S2:f
#3
Write
Stage
Reg. Write
Path
#3 DIV F0,F2,F4
#4 ADDD F6,F0,F8
#5 SUBD F8,F10,F14
#6 MULD F6,F10,F8
D:F0
V:b/c
#3
F0
D:F0
V:b/c
#3
Op:div
D:F0
S1:b
S2:c
#3
Register
renaming!
#3
b/c
IF
X
W

## Slide 23: Tomasulo’s: What is going on?
Read Register:
  Rename DestReg to the Res. Station location
Wait for all RAW dependencies at Res. Station
After Execution
  Put result in Reorder Buffer (ROB)
  Broadcast result on CDB to all waiting instructions
  Rename DestReg to the ROB location
When all preceeding instr. have arrived at ROB:
  Write value to DestReg (called Commit)
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Write
Stage
Reg. Write
Path
1
2
3a
3b
3c
4

## Slide 24: Simple Tomasulo’s Algorithm
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
Op
D
S1
S2
#
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Op
D:F0
S1:v
S2:v
#
Op
D
S1:v/ptr
S2:v/ptr
#
Write
Stage
Reg. Write
Path
#3 DIV F0,F2,F4
#4 ADDD F6,F0,F8
#5 SUBD F8,F10,F14
#6 MULD F6,F10,F8
D
answ
#
D
D
answ
#

## Slide 25: Simple Tomasulo’s Algorithm
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Write
Stage
Reg. Write
Path
#3 DIV F0,F2,F4
#4 ADDD F6,F0,F8
#5 SUBD F8,F10,F14
#6 MULD F6,F10,F8
#
D
Op
D
S1
S2
#
Op
D:F0
S1:v
S2:v
#
Op
D
S1:v/ptr
S2:v/ptr
#
D
answ
D
answ
#

## Slide 26: Simple Tomasulo’s Algorithm
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Write
Stage
Reg. Write
Path
#3 DIV F0,F2,F4
#4 ADDD F6,F0,F8
#5 SUBD F8,F10,F14
#6 MULD F6,F10,F8
#
D
#5
Op
D
S1
S2
#
Op
D:F0
S1:v
S2:v
#
Op
D
S1:v/ptr
S2:v/ptr
#
D
answ
D
answ
#

## Slide 27: Simple Tomasulo’s Algorithm
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Write
Stage
Reg. Write
Path
#3 DIV F0,F2,F4
#4 ADDD F6,F0,F8
#5 SUBD F8,F10,F14
#6 MULD F6,F10,F8
#
D
#5
Op
D
S1
S2
#
Op
D:F0
S1:v
S2:v
#
Op
D
S1:v/ptr
S2:v/ptr
#
D
answ
D
answ
#
#6

## Slide 28: Simple Tomasulo’s Algorithm
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Write
Stage
Reg. Write
Path
#3 DIV F0,F2,F4
#4 ADDD F6,F0,F8
#5 SUBD F8,F10,F14
#6 MULD F6,F10,F8
#
D
#5
Op
D
S1
S2
#
Op
D:F0
S1:v
S2:v
#
Op
D
S1:v/ptr
S2:v/ptr
#
D
answ
D
answ
#
#6
#3

## Slide 29: Simple Tomasulo’s Algorithm
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Write
Stage
Reg. Write
Path
#3 DIV F0,F2,F4
#4 ADDD F6,F0,F8
#5 SUBD F8,F10,F14
#6 MULD F6,F10,F8
#
D
#5
Op
D
S1
S2
#
Op
D:F0
S1:v
S2:v
#
Op
D
S1:v/ptr
S2:v/ptr
#
D
answ
D
answ
#
#6
b/c

## Slide 30: Simple Tomasulo’s Algorithm
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Write
Stage
Reg. Write
Path
#3 DIV F0,F2,F4
#4 ADDD F6,F0,F8
#5 SUBD F8,F10,F14
#6 MULD F6,F10,F8
#
D
#5
Op
D
S1
S2
#
Op
D:F0
S1:v
S2:v
#
Op
D
S1:v/ptr
S2:v/ptr
#
D
answ
D
answ
#
#6
b/c

## Slide 31: Tomasulo’s: What is going on?
Read Register:
  Rename DestReg to the Res. Station location
Wait for all RAW dependencies at Res. Station
After Execution
  Put result in Reorder Buffer (ROB)
  Broadcast result on CDB to all waiting instructions
  Rename DestReg to the ROB location
When all preceeding instr. have arrived at ROB:
  Write value to DestReg (called Commit)
IF
Read operands
Issue
Mem
Issue
Int
Mem
FP
Add
FP
Mul1
FP
Mul2
FP
Div
Mem
IF
Res.
Station
0:a
1:
2:b
3:
4:c
5:
6:d
7:
8:e
9:
Common
Data Bus (CDB)
9 8 7 6 5 4 3 2 1
ReOrder
Buffer (ROB)
Write
Stage
Reg. Write
Path
1
2
3a
3b
3c
4

## Slide 32: A 5-stage superscalar pipeline
IF
ID
EX
M
WB
IF
ID
EX
M
WB
Reg
ALU
ALU
D
B
C
A
E
One sequential
program:
L1$

## Slide 33: A 2-way superscalar 5-stage pipeline Need 2x ILP!
ALU
ALU
Mem
4/8
Can fetch up to two consecutive instr /cycle.
If deamed to be OK.
Only top pipeline may execute branches
2x reads & writes to the shared register file
Reg
2x reads & writes to the L1 cache

## Slide 34: Superscalars
Mem
I
X
W
Regs
I
X
W
I
X
W
I
R
X
W
I
I
I
I
Issue
logic
£
€
SEK
150cycles
35 cycles
14 cycles
4 cycles
4GB
8MB
256kB
16kB
Thread 1
…
PC
res
rob

## Slide 35: HW prefetching
...a little green man that anticipates your next memory access and prefetches the data to the cache.
Improves MLP (memory-level parallelism)
Sequential prefetching: Sequential streams [to a page]. Some number of prefetch streams supported. Often only for L2 and L3.
PC-based prefetching: Detects strides from the same PC. Often for L1 caches.
Adjacent prefetching: On a miss, also bring in the “neighbouring” cache line. Often only for L2 and L3.

## Slide 36: Architectural assumptions
From To Latency
LD FP/INT ALU 3 (cache hit)
200 (cache miss)
“Load-use extra latency: 3 cycles for all loads”
Branches: Adds 3 cycles, unless correctly predicted
No branch delay slot
64 bit architecture/application
32kB cache, CL = 64B. HWP=strides+adjacent
Superscalar: 2-way issue of any instruction type
OoO small: ROB=32, single-issue, commits 2i/c
OoO large: ROB=128, 2-way Superscalar, 4i/c
All other resources are infinite

## Slide 37
for (i =0, i < HUGE, i++) {
sum += s[i].val1;
}
Translated into pseudo-ASM :
LOOP:
1: LDD F0, 8(R1) // R2 = a[i].val1
2: ADDD F2, F2, F0 // sum += …
3: SUBI R1, R1, #32 // i++
4: BEQZ R1, #LOOP // last time?
How many cycles per loop?
In-order, single-issue, no BP, no HWP
Cache adds 3 cycles LDD  FP ALU
Cache miss adds 200 cycles
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[i]
s[i+1]

## Slide 38
for (i =0, i < HUGE, i++) {
sum += s[i].val1;
}
Translated into pseudo-ASM :
LOOP:
1: LDD F0, 8(R1) // R2 = a[i].val1
50%: 3 stalls; 50%200 stalls
2: ADDD F2, F2, F0 // sum += …
3: SUBI R1, R1, #32 // i++
4: BEQZ R1, #LOOP // last time?
3 stalls
How many cycles per loop?
4 [instr] + (200 + 3)/2 [stall] + 3 [stall]
IN ORDER +BP +BP+HWP +BP+SWP
108 105 7 ~7 (HOW?)
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[i]
s[i+1]

## Slide 39
for (i =0, i < HUGE, i++) {
sum += s[i].val1;
}
Translated into pseudo-ASM :
LOOP:
0: PREF 896(R1) //Staying ahead 28 loops @ 32B stride
1: LDD F0, 8(R1) // R2 = a[i].val1
3 stalls
2: ADDD F2, F2, F0 // sum += …
3: SUBI R1, R1, #32 // i++
4: BEQZ R1, #LOOP // last time?
How many cycles per loop? 5 [instr] + 3 [stall] + 3 [stall]
Base +BP +BP+HWP +BP+SWP (how)
In order 108 105 7 8
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[i]
s[i+1]

## Slide 40
for (i =0, i < HUGE, i++) {
sum += s[i].val1;
}
Translated into pseudo-ASM :
LOOP:
1: LDD F0, 8(R1) // R2 = a[i].val1
2: ADDD F2, F2, F0 // sum += …
3: SUBI R1, R1, #32 // i++
4: BEQZ R1, #LOOP // last time?
How many cycles per loop? 5 [instr] + 3 [stall] + 3 [stall]
Base +BP +BP+HWP +BP+SWP (how)
In order 108 105 7 8
Superscalar?
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[i]
s[i+1]

## Slide 41
for (i =0, i < HUGE, i++) {
sum += s[i].val1;
}
Translated into pseudo-ASM :
LOOP:
1: LDD F0, 8(R1) // R2 = a[i].val1
3 stalls or 200 stalls
2: ADDD F2, F2, F0 // sum += …
3: SUBI R1, R1, #32 // i++
4: BEQZ R1, #LOOP // last time?
3 stalls
How many cycles per loop? 5 [instr] + 3 [stall] + 3 [stall]
Base +BP +BP+HWP +BP+SWP (how)
In order 108 105 7 8
Superscalar 107 104 6 7
OoO small? ??? ???
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[i]
s[i+1]

## Slide 42
for (i =0, i < HUGE, i++) {
sum += s[i].val1;
}
LOOP:
1: LDD F0, 8(R1) // R2 = a[i].val1
2: ADDD F2, F2, F0 // sum += …
3: SUBI R1, R1, #32 // i++
4: BEQZ R1, #LOOP // last time?
How many cycles per loop? 5 [instr] + 3 [stall] + 3 [stall]
Base +BP +BP+HWP +BP+SWP (how)
In order 108 105 7 8
Superscalar 107 104 6 7
OoO small ??? ???
First LDD = cache miss
Issue another 31 instructions (8 loops). Takes 32 cycles
Wait another 168 cycles (4 outstanding cache misses: MLP=4)
Repeat 1-3
 8 loops in 201 cycles  25 cycles/loop
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[i]
s[i+1]

## Slide 43
for (i =0, i < HUGE, i++) {
sum += s[i].val1;
}
LOOP:
1: LDD F0, 8(R1) // R2 = a[i].val1
2: ADDD F2, F2, F0 // sum += …
3: SUBI R1, R1, #32 // i++
4: BEQZ R1, #LOOP // last time?
How many cycles per loop?
Base +BP +BP+HWP +BP+SWP (how)
In order 108 105 7 8
Superscalar 107 104 6 7
OoO small 25 4
OoO large ??? ???
First LDD = cache miss
Issue another 131 instructions (32 loops). Takes 64 cycles
Wait another 136 cycles (MLP=16)
Repeat 1-3
 32 loops in 201 cycles  6 cycles/loop
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[i]
s[i+1]

## Slide 44
for (i =0, i < HUGE, i++) {
sum += s[i].val1;
}
LOOP:
1: LDD F0, 8(R1) // R2 = a[i].val1
2: ADDD F2, F2, F0 // sum += …
3: SUBI R1, R1, #32 // i++
4: BEQZ R1, #LOOP // last time?
How many cycles per loop?
Base +BP +BP+HWP +BP+SWP (how)
In order 108 105 7 8
Superscalar 107 104 6 7
OoO small 25 4
OoO large 6 2
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[i]
s[i+1]

## Slide 45
for (i =0, i < HUGE, i++) {
sum += s[a[i]].val3;
}
Translated into pseudo-ASM :
LOOP:
1: LD R2, 0(R1) // R2 = a[i]
2: LDD F0, 8(R2) // R3 = s[a[i]].val1
3: ADDD F2, F2, F0 // sum += …
4: SUBI R1, R1, #4 // i++
5: BEQZ R1, #LOOP // last time?
How many cycles per loop?
Base +BP +BP+HWP +BP+SWP
In order ?? ?? ??
Superscalar ?? ?? ?? ??
OoO small ?? ??
OoO large ?? ??
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[0]
s[1]
a[0], a[1], a[2], …

## Slide 46
for (i =0, i < HUGE, i++) {
sum += s[a[i]].val3;
}
Translated into pseudo-ASM :
LOOP:
1: LD R2, 0(R1) // R2 = a[i]
3 stalls 94%; 200 stalls 6%  15 stalls avg
2: LDD F0, 8(R2) // R3 = s[a[i]].val1
200 stalls ~100%
3: ADDD F2, F2, F0 // sum += …
4: SUBI R1, R1, #4 // i++
5: BEQZ R1, #LOOP // last time?
3 stalls
How many cycles per loop?
Base +BP +BP+HWP +BP+SWP
In order 223 ?? ??
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[0]
s[1]
a[0], a[1], a[2], …

## Slide 47
for (i =0, i < HUGE, i++) {
sum += s[a[i]].val3;
}
Translated into pseudo-ASM :
LOOP:
1: LD R2, 0(R1) // R2 = a[i]
1a: PREF 224(R1) //Pref dist: 2 * 28 loops @ 4B
1b: LD R3, 112(R1) //R3 = a[i+28]
1c: PREF 8(R3) //Prefetch s[a[i+28]]
2: LDD F0, 8(R2) // R3 = s[a[i]].val1
3 stalls
3: ADDD F2, F2, F0 // sum += …
4: SUBI R1, R1, #4 // i++
5: BEQZ R1, #LOOP // last time?
How many cycles per loop?
Base +BP +BP+HWP +BP+SWP
In order 223 208 11
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[0]
s[1]
a[0], a[1], a[2], …
How?

## Slide 48
for (i =0, i < HUGE, i++) {
sum += s[a[i]].val3;
}
LOOP:
1: LD R2, 0(R1) // R2 = a[i]
2: LDD F0, 8(R2) // R3 = s[a[i]].val1
3: ADDD F2, F2, F0 // sum += …
4: SUBI R1, R1, #4 // i++
5: BEQZ R1, #LOOP // last time?
How many cycles per loop?
Base +BP +BP+HWP +BP+SWP
In order 223 208 11
OoO small 33
LD = cache hit (thanks to HWP)
LD = cache miss
Issue another 31 instructions (~6 loops). Takes 32 cycles
Wait another 168 cycles; MLP = 6)
Repeat 1-4
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[0]
s[1]
a[0], a[1], a[2], …
???

## Slide 49
for (i =0, i < HUGE, i++) {
sum += s[a[i]].val3;
}
LOOP:
1: LD R2, 0(R1) // R2 = a[i]
2: LDD F0, 8(R2) // R3 = s[a[i]].val1
3: ADDD F2, F2, F0 // sum += …
4: SUBI R1, R1, #4 // i++
5: BEQZ R1, #LOOP // last time?
How many cycles per loop?
Base +BP +BP+HWP +BP+SWP
In order 223 208 11
OoO small 33
OoO Large 8
LD = cache hit (thanks to HWP)
LD = cache miss
Issue another 127 instructions (~24 loops). Takes 64 cycles
Wait another 136 cycles; MLP = 24)
Repeat 1-4
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
s[0]
s[1]
a[0], a[1], a[2], …
???

## Slide 50
while (ptr->next){
sum += ptr->val1;
ptr = ptr->next
}
Translated into pseudo-ASM:
LOOP:
1: LDD F0, 8(R3) // R1=val1
2: ADD F2, F2, F0 //sum1 += ...
3: LD R3 32(R3) //ptr = ...
4: BNEZ R3, #LOOP
How many cycles per loop?
Base +BP +BP+HWP +BP+SWP
In order ?? ?? ??
Superscalar ?? ?? ?? ??
OoO small ?? ??
OoO large ?? ??
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
ptr

## Slide 51
while (ptr->next){
sum += ptr->val1;
ptr = ptr->next
}
Translated into pseudo-ASM:
LOOP:
1: LDD F0, 8(R3) // R1=val1
Stall 200
2: ADD F2, F2, F0 //sum1 += ...
3: LD R3 32(R3) //ptr = ...
50% Stall 200, 50% stall 3
4: BNEZ R3, #LOOP
Stall 3
IN ORDER
Base: 307
+BP: 304
+BP + HWP: 204 (adjacent prefetching)
Which architecture would be the fastest and how fast would it run?
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
ptr

## Slide 52: Problems from previous IRL

## Slide 53
while (ptr->next){
sum += ptr->val1;
ptr = ptr->next
}
Translated into pseudo-ASM:
LOOP:
0: LD R4, 32(R3) // R4 = ptr->next
0b PREF 8(R4) //PREF min usage of ptr->next object
0c: PREF 32(R4) //PREF max usage of ptr->next object
1: LDD F0, 8(R3) // R1=val1
2: ADD F2, F2, F0 //sum1 += ...
3: LD R3, 32(R3) //ptr = ...
4: BNEZ R3, #LOOP
IN ORDER
Base: 307
+BP: 304
+BP + HWP: 204 (adjacent prefetching)
Which architecture would be the fastest and fast would it run?
val0
val1
val2
val3
Struct:
8B
val0
val1
val2
val3
ptr

## Slide 54
Directory representation
  Fully mapped
  DIRiB
  DIRiNB
  DIRiCV
Protocols
  MSI
  MOSI
  MESI

## Slide 55: Fully mapped directory
• k Nodes
• Dir entry per cacheline in home memory: k presence-bits + 1 dirty-bit
Memory
Cacheline (this is its ”home”)
Directory
…
1
2
3
k
d
k presense bits
Interconnect
$
$
$
$
k ”nodes”

## Slide 56: Broadcast DiriB (e.g. Dir3B)
• Broadcast (DiriB)
  A limited number of log(k) bit pointers (here i)
  Typically, i is small  Fewer bits needed in the directory
  Overflow bit turned on if more sharers than pointers
  Turns into ”broadcast mode” and send invalidates to all
  Changes back to pointers after invalidate
  Bad for widely shared invalidated data
Memory
Cacheline (this is its ”home”)
Directory
…
1
2
i
O
i log(k) bit pointers
Interconnect
$
$
$
$
k ”nodes”
$
Overflow bit
d

## Slide 57: No Broadcast: DiriNB (e.g. Dir3NB)
• (DiriNB)
  If more sharers than pointers, force eviction and reuse pointer
  Bad for widely shared data
Memory
Cacheline (this is its ”home”)
Directory
…
1
2
i
i log(k) pointers
Interconnect
$
$
$
$
k ”nodes”
$
d

## Slide 58: Course-grain Vector: DiriCV (Dir3CV)
• DiriCV
  Overflow bit turned on if more sharers than pointers
Memory
Cacheline (this is its ”home”)
Directory
…
1
2
i
O
i log(k) pointers
Interconnect
$
$
$
$
k ”nodes”
$
Overflow bit
d

## Slide 59: Overflow Broadcast: DiriCV (e.g. Dir3CV)
• Broadcast (DiriCV)
  Overflow bit turned on if more sharers than pointers
  Directory changed to (e.g., k/2) course presence bits
  Each bit indicates presence in a group of nodes (here 2)
  Invalidates sent to all in the group if bit is set
  Change back to pointers on invalidates
  Potentially less traffic than DIRiB due to limited broadcast
Memory
Cacheline (this is its ”home”)
Directory
Interconnect
$
$
$
$
k ”nodes”
$
Overflow bit
…
1
2
3
K
/2
O
k/2 presense bits
d

## Slide 60: What is a good implementation? (Space/efficiency/complexity)
 | MSI | MESI | MOSI
DIRiB |  |  | 
DIRiNB |  |  | 
DIRiCV |  |  | 
Fully mapped |  |  | 
UMA: Mem access latency = 2x latency of cache-to-cache accesses
16 caches
128 caches
Migratory sharing: (ALL: x = x + 1)
Producer consumer, P1: x := …, P2: … := x
One writer, 8 readers (writes are 0,2% of all mem accesses)
Massive read-only sharing
Many independent applications

## Slide 61: What is a good implementation? (Space/efficiency/complexity)
 | MSI | MESI | MOSI
DIRiB |  |  | 
DIRiNB |  |  | 
DIRiCV |  |  | 
Fully mapped |  | A4,A5 | A3, A2, A1
UMA: Mem access latency = 2x latency of cache-to-cache accesses
16 caches
128 caches
Migratory sharing: (ALL: x = x + 1)
Producer consumer, P1: x := …, P2: … := x
One writer, 8 readers (writes are 0,2% of all mem accesses)
Massive read-only sharing
Many independent applications

## Slide 62: What is a good implementation? (Space/efficiency/complexity)
 | MSI | MESI | MOSI
DIRiB |  | B4, B5 | B2, B1
DIRiNB |  |  | 
DIRiCV |  |  | B3
Fully mapped |  | A4,A5 | A3, A2, A1
UMA: Mem access latency = 2x latency of cache-to-cache accesses
16 caches
128 caches
Migratory sharing: (ALL: x = x + 1)
Producer consumer, P1: x := …, P2: … := x
One writer, 8 readers (writes are 0,2% of all mem accesses)
Massive read-only sharing
Many independent applications

## Slide 63: What is a good implementation? (Space/efficiency/complexity)
 | MSI | MESI | MOSI
DIRiB |  |  | 
DIRiNB |  |  | 
DIRiCV |  |  | 
Fully mapped |  |  | 
NUMA: Clean@home latency = ½ latency to dirty in remote cache
16 nodes
128 nodes
Migratory sharing: (ALL: x = x + 1)
Producer consumer, P1: x := …, P2: … := x
One writer, 8 readers (writes are 0,2% of all mem accesses)
Massive read-only sharing
Many independent applications

## Slide 64: What is a good implementation? (Space/efficiency/complexity)
 | MSI | MESI | MOSI
DIRiB |  |  | 
DIRiNB |  |  | 
DIRiCV |  |  | 
Fully mapped |  |  | 
UMA with LLC
16 nodes
128 nodes
Migratory sharing: (ALL: x = x + 1)
Producer consumer, P1: x := …, P2: … := x
One writer, 8 readers (writes are 0,2% of all mem accesses)
Massive read-only sharing
Many independent applications