## Slide 1: CENG/CSCI 3420 Computer Organization and Design Spring 2014 Lecture 02: Performance and ISA
XU, Qiang 徐強
[Adapted from UC Berkeley’s D. Patterson’s and
from PSU’s Mary J. Irwin’s slides with additional credits to Y. Xie]

## Slide 2: Review: Major Components of a Computer
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.
Workstation Design Target: 25% of cost on Processor, 25% of cost on Memory (minimum memory size), rest on I/O devices, power supplies, box

## Slide 3: Review: The Instruction Set Architecture (ISA)
instruction set architecture
software
hardware
The interface description separating the software and hardware

## Slide 4: Performance Metrics
Purchasing perspective
  given a collection of machines, which has the
    best performance ?
    least cost ?
    best cost/performance?
Design perspective
  faced with design options, which has the
    best performance improvement ?
    least cost ?
    best cost/performance?
Both require
  basis for comparison
  metric for evaluation
Our goal is to understand what factors in the architecture contribute to overall system performance and the relative importance (and cost) of these factors
Notes: Or smallest/lightest
Longest battery life
Most reliable/durable (in space)

## Slide 5: Throughput versus Response Time
Response time (execution time) – the time between the start and the completion of a task
  Important to individual users
Throughput (bandwidth) – the total amount of work done in a given time
  Important to data center managers
Will need different performance metrics as well as a different set of applications to benchmark embedded and desktop computers, which are more focused on response time, versus servers, which are more focused on throughput

## Slide 6: Response Time Matters
Justin Rattner’s ISCA’08 Keynote (VP and CTO of Intel)

## Slide 7: Defining (Speed) Performance
To maximize performance, need to minimize execution time
performanceX = 1 / execution_timeX
  If X is n times faster than Y, then
performanceX execution_timeY
-------------------- = --------------------- = n
performanceY execution_timeX
Decreasing response time almost always improves throughput
Notes: Increasing performance requires decreasing execution time

## Slide 8: A Relative Performance Example
If computer A runs a program in 10 seconds and computer B runs the same program in 15 seconds, how much faster is A than B?

## Slide 9: Relative Performance Example
If computer A runs a program in 10 seconds and computer B runs the same program in 15 seconds, how much faster is A than B?
We know that A is n times faster than B if
performanceA execution_timeB
-------------------- = --------------------- = n
performanceB execution_timeA
15
------ = 1.5
10
The performance ratio is
So A is 1.5 times faster than B

## Slide 10: Performance Factors
CPU execution time (CPU time) – time the CPU spends working on a task
  Does not include time waiting for I/O or running other programs
CPU execution time # CPU clock cycles
for a program for a program
= x clock cycle time
CPU execution time # CPU clock cycles for a program
for a program clock rate
= -------------------------------------------
Can improve performance by reducing either the length of the clock cycle or the number of clock cycles required for a program
or
Notes: Many techniques that decrease the number of clock cycles also increase the clock cycle time

## Slide 11: Review: Machine Clock Rate
Clock rate (clock cycles per second in MHz or GHz) is inverse of clock cycle time (clock period)
CC = 1 / CR
one clock period
10 nsec clock cycle => 100 MHz clock rate
5 nsec clock cycle => 200 MHz clock rate
2 nsec clock cycle => 500 MHz clock rate
1 nsec (10-9) clock cycle => 1 GHz (109) clock rate
500 psec clock cycle => 2 GHz clock rate
250 psec clock cycle => 4 GHz clock rate
200 psec clock cycle => 5 GHz clock rate
Notes: A clock cycle is the basic unit of time to execute one operation/pipeline stage/etc.

## Slide 12: Improving Performance Example
A program runs on computer A with a 2 GHz clock in 10 seconds. What clock rate must a computer B run at to run this program in 6 seconds? Unfortunately, to accomplish this, computer B will require 1.2 times as many clock cycles as computer A to run the program.
Notes: For class handout

## Slide 13: Improving Performance Example
A program runs on computer A with a 2 GHz clock in 10 seconds. What clock rate must computer B run at to run this program in 6 seconds? Unfortunately, to accomplish this, computer B will require 1.2 times as many clock cycles as computer A to run the program.
CPU timeA CPU clock cyclesA
clock rateA
= -------------------------------
CPU clock cyclesA = 10 sec x 2 x 109 cycles/sec = 20 x 109 cycles
CPU timeB 1.2 x 20 x 109 cycles
clock rateB
= -------------------------------
clock rateB 1.2 x 20 x 109 cycles
6 seconds
= ------------------------------- = 4 GHz
Notes: For lecture

## Slide 14: Clock Cycles per Instruction
Not all instructions take the same amount of time to execute
  One way to think about execution time is that it equals the number of instructions executed multiplied by the average time per instruction
Clock cycles per instruction (CPI) – the average number of clock cycles each instruction takes to execute
  A way to compare two different implementations of the same ISA
# CPU clock cycles # Instructions Average clock cycles
for a program for a program per instruction
= x
 | CPI for this instruction class |  | 
 | A | B | C
CPI | 1 | 2 | 3

## Slide 15: Using the Performance Equation
Computers A and B implement the same ISA. Computer A has a clock cycle time of 250 ps and an effective CPI of 2.0 for some program and computer B has a clock cycle time of 500 ps and an effective CPI of 1.2 for the same program. Which computer is faster and by how much?
Notes: For class handout

## Slide 16: Using the Performance Equation
Computers A and B implement the same ISA. Computer A has a clock cycle time of 250 ps and an effective CPI of 2.0 for some program and computer B has a clock cycle time of 500 ps and an effective CPI of 1.2 for the same program. Which computer is faster and by how much?
Each computer executes the same number of instructions, I, so
CPU timeA = I x 2.0 x 250 ps = 500 x I ps
CPU timeB = I x 1.2 x 500 ps = 600 x I ps
Clearly, A is faster … by the ratio of execution times
performanceA execution_timeB 600 x I ps
------------------- = --------------------- = ---------------- = 1.2
performanceB execution_timeA 500 x I ps
Notes: For lecture

## Slide 17: Effective (Average) CPI
Computing the overall effective CPI is done by looking at the different types of instructions and their individual cycle counts and averaging
Overall effective CPI =
  Where ICi is the percentage of the number of instructions of class i executed
  CPIi is the (average) number of clock cycles per instruction for that instruction class
  n is the number of instruction classes
The overall effective CPI varies by instruction mix – a measure of the dynamic frequency of instructions across one or many programs

## Slide 18: THE Performance Equation
Our basic performance equation is then
CPU time = Instruction_count x CPI x clock_cycle
Instruction_count x CPI
clock_rate
CPU time = -----------------------------------------------
or
These equations separate the three key factors that affect performance
  Can measure the CPU execution time by running the program
  The clock rate is usually given
  Can measure overall instruction count by using profilers/ simulators without knowing all of the implementation details
  CPI varies by instruction type and ISA implementation for which we must know the implementation details
Notes: Note that instruction count is dynamic – i.e., its not the number of lines in the code, but THE NUMBER OF INSTRUCTIONS EXECUTED

## Slide 19: Determinates of CPU Performance
CPU time = Instruction_count x CPI x clock_cycle
 | Instruction_count | CPI | clock_cycle
Algorithm |  |  | 
Programming language |  |  | 
Compiler |  |  | 
ISA |  |  | 
Core organization |  |  | 
Technology |  |  | 
Notes: For class handout

## Slide 20: Determinates of CPU Performance
CPU time = Instruction_count x CPI x clock_cycle
 | Instruction_count | CPI | clock_cycle
Algorithm |  |  | 
Programming language |  |  | 
Compiler |  |  | 
ISA |  |  | 
Core organization |  |  | 
Technology |  |  | 
X
X
X
X
X
X
X
X
X
X
X
X
Notes: For lecture

## Slide 21: A Simple Example
How much faster would the machine be if a better data cache reduced the average load time to 2 cycles?
How does this compare with using branch prediction to shave a cycle off the branch time?
What if two ALU instructions could be executed at once?
Op | Freq | CPIi | Freq x CPIi
ALU | 50% | 1 | .
Load | 20% | 5 | 
Store | 10% | 3 | 
Branch | 20% | 2 | 
 |  |  | =

## Slide 22: A Simple Example
How much faster would the machine be if a better data cache reduced the average load time to 2 cycles?
How does this compare with using branch prediction to shave a cycle off the branch time?
What if two ALU instructions could be executed at once?
Op | Freq | CPIi | Freq x CPIi
ALU | 50% | 1 | 
Load | 20% | 5 | 
Store | 10% | 3 | 
Branch | 20% | 2 | 
 |  |  | =
.5
1.0
.3
.4
2.2
CPU time new = 1.6 x IC x CC so 2.2/1.6 means 37.5% faster
1.6
.5
.4
.3
.4
.5
1.0
.3
.2
2.0
CPU time new = 2.0 x IC x CC so 2.2/2.0 means 10% faster
.25
1.0
.3
.4
1.95
CPU time new = 1.95 x IC x CC so 2.2/1.95 means 12.8% faster
Notes: For lecture

## Slide 23: Workloads and Benchmarks
Benchmarks – a set of programs that form a “workload” specifically chosen to measure performance
SPEC (System Performance Evaluation Cooperative) creates standard sets of benchmarks starting with SPEC89. The latest is SPEC CPU2006 which consists of 12 integer benchmarks (CINT2006) and 17 floating-point benchmarks (CFP2006).
www.spec.org
There are also benchmark collections for power workloads (SPECpower_ssj2008), for mail workloads (SPECmail2008), for multimedia workloads (mediabench), …

## Slide 24: Old SPEC Benchmarks
Integer benchmarks |  | FP benchmarks | 
gzip | compression | wupwise | Quantum chromodynamics
vpr | FPGA place & route | swim | Shallow water model
gcc | GNU C compiler | mgrid | Multigrid solver in 3D fields
mcf | Combinatorial optimization | applu | Parabolic/elliptic pde
crafty | Chess program | mesa | 3D graphics library
parser | Word processing program | galgel | Computational fluid dynamics
eon | Computer visualization | art | Image recognition (NN)
perlbmk | perl application | equake | Seismic wave propagation simulation
gap | Group theory interpreter | facerec | Facial image recognition
vortex | Object oriented database | ammp | Computational chemistry
bzip2 | compression | lucas | Primality testing
twolf | Circuit place & route | fma3d | Crash simulation fem
 |  | sixtrack | Nuclear physics accel
 |  | apsi | Pollutant distribution

## Slide 25: SPEC CINT2006 on Barcelona (CC = 0.4 x 109)
Name | ICx109 | CPI | ExTime | RefTime | SPEC ratio
perl | 2,1118 | 0.75 | 637 | 9,770 | 15.3
bzip2 | 2,389 | 0.85 | 817 | 9,650 | 11.8
gcc | 1,050 | 1.72 | 724 | 8,050 | 11.1
mcf | 336 | 10.00 | 1,345 | 9,120 | 6.8
go | 1,658 | 1.09 | 721 | 10,490 | 14.6
hmmer | 2,783 | 0.80 | 890 | 9,330 | 10.5
sjeng | 2,176 | 0.96 | 837 | 12,100 | 14.5
libquantum | 1,623 | 1.61 | 1,047 | 20,720 | 19.8
h264avc | 3,102 | 0.80 | 993 | 22,130 | 22.3
omnetpp | 587 | 2.94 | 690 | 6,250 | 9.1
astar | 1,082 | 1.79 | 773 | 7,020 | 9.1
xalancbmk | 1,058 | 2.70 | 1,143 | 6,900 | 6.0
Geometric Mean |  |  |  |  | 11.7
Notes: Mcf has large CPI because it has high cache miss rate!
Perl – interpreted string processing
Bzip2 – block-sorting compression
Gcc – GNU C compiler
Mcf – combinatorial optimization
Go – Go came (AI)
Hmmer – search gene sequence
Sjeng – chess game (AI)
Libquantum – quantum computer simulation
H264avc – video compression
Omnetpp – discret event simulation library
Astar – games/path finding
Xalancbmk – XML parsing

## Slide 26: Comparing and Summarizing Performance
Guiding principle in reporting performance measurements is reproducibility – list everything another experimenter would need to duplicate the experiment (version of the operating system, compiler settings, input set used, specific computer configuration (clock rate, cache sizes and speed, memory size and speed, etc.))
How do we summarize the performance for benchmark set with a single number?
  First the execution times are normalized giving the “SPEC ratio” (bigger is faster, i.e., SPEC ratio is the inverse of execution time)
  The SPEC ratios are then “averaged” using the geometric mean (GM)
GM = n SPEC ratioi
i = 1
n

## Slide 27: Other Performance Metrics
Power consumption – especially in the embedded market where battery life is important
  For power-limited applications, the most important metric is energy efficiency
Notes: From Version 3 of the book – probably needs replaced or dropped (based on SPEC2000)

## Slide 28: Summary: Evaluating ISAs
Design-time metrics:
  Can it be implemented? With what performance, at what costs (design, fabrication, test, packaging), with what power, with what reliability?
  Can it be programmed? Ease of compilation?
Static Metrics:
  How many bytes does the program occupy in memory?
Dynamic Metrics:
  How many instructions are executed? How many bytes does the processor fetch to execute the program?
  How many clocks are required per instruction?
  How "lean" a clock is practical?
Best Metric: Time to execute the program!
CPI
Inst. Count
Cycle Time
depends on the instructions set, the processor organization, and compilation techniques.

## Slide 29: Two Key Principles of Machine Design
  Instructions are represented as numbers and, as such, are indistinguishable from data
  Programs are stored in alterable memory (that can be read or written to) just like data
Stored-program concept
  Programs can be shipped as files of binary numbers – binary compatibility
  Computers can inherit ready-made software provided they are compatible with an existing ISA – leads industry to align around a small number of ISAs
Accounting prg (machine code)
C compiler (machine code)
Payroll data
Source code in C for Acct prg
Memory

## Slide 30: MIPS-32 ISA
Instruction Categories
  Computational
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
Registers
op
op
op
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide
R format
I format
J format

## Slide 31: MIPS (RISC) Design Principles
Simplicity favors regularity
  fixed size instructions
  small number of instruction formats
  opcode always the first 6 bits
Smaller is faster
  limited instruction set
  limited number of registers in register file
  limited number of addressing modes
Make the common case fast
  arithmetic operands from the register file (load-store machine)
  allow instructions to contain immediate operands
Good design demands good compromises
  three instruction formats

## Slide 32: MIPS Arithmetic Instructions
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs one operation
Each specifies exactly three operands that are all contained in the datapath’s register file ($t0,$s1,$s2)
  destination = source1 op source2
Instruction Format (R format)
0 17 18 8 0 0x22
Notes: For class handout

## Slide 33: MIPS Arithmetic Instructions
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs one operation
Each specifies exactly three operands that are all contained in the datapath’s register file ($t0,$s1,$s2)
  destination = source1 op source2
Instruction Format (R format)
0 17 18 8 0 0x22
Notes: Register designators (numbers) in decimal
Op codes and function fields in hex (0x designation)

## Slide 34: MIPS Instruction Fields
MIPS fields are given names to make them easier to refer to
op rs rt rd shamt funct
op 6-bits opcode that specifies the operation
rs 5-bits register file address of the first source operand
rt 5-bits register file address of the second source operand
rd 5-bits register file address of the result’s destination
shamt 5-bits shift amount (for shift instructions)
funct 6-bits function code augmenting the opcode

## Slide 35: MIPS Register File
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
locations
32
5
32
5
5
32
Holds thirty-two 32-bit registers
  Two read ports and
  One write port
Registers are
  Faster than main memory
    But register files with more locations are slower (e.g., a 64 word file could be as much as 50% slower than a 32 word file)
    Read/write port increase impacts speed quadratically
  Easier for a compiler to use
    e.g., (A*B) – (C*D) – (E*F) can do multiplies in any order vs. stack
  Can hold variables so that
    code density improves (since register are named with fewer bits than a memory location)
write control
Notes: All machines (since 1975) have used general purpose registers

## Slide 36: Aside: MIPS Register Convention
Name | Register Number | Usage | Preserve on call?
$zero | 0 | constant 0 (hardware) | n.a.
$at | 1 | reserved for assembler | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return addr (hardware) | yes

## Slide 37: MIPS Memory Access Instructions
MIPS has two basic data transfer instructions for accessing memory
lw $t0, 4($s3) #load word from memory
sw $t0, 8($s3) #store word to memory
The data is loaded into (lw) or stored from (sw) a register in the register file – a 5 bit address
The memory address – a 32 bit address – is formed by adding the contents of the base address register to the offset value
  A 16-bit field meaning access is limited to memory locations within a region of 213 or 8,192 words ( 215 or 32,768 bytes) of the address in the base register
Notes: Note that the offset can be positive or negative.
Offsets must be able to access bytes as well, so word offsets will have two low-order zeros in them.

## Slide 38: Machine Language - Load Instruction
Load/Store Instruction Format (I format):
lw $t0, 24($s3)
35 19 8 2410
Memory
data
word address (hex)
0x00000000
0x00000004
0x00000008
0x0000000c
0xf f f f f f f f
$s3
0x12004094
2410 + $s3 =
. . . 0001 1000
+ . . . 1001 0100
. . . 1010 1100 =
0x120040ac
0x120040ac
$t0
Notes: destination address no longer in the rd field - now in the rt field
offset limited to 16 bits - so can’t get to every location in memory (with a fixed base address)

## Slide 39: Byte Addresses
Since 8-bit bytes are so useful, most architectures address individual bytes in memory
  Alignment restriction - the memory address of a word must be on natural word boundaries (a multiple of 4 in MIPS-32)
Big Endian: leftmost byte is word address
    IBM 360/370, Motorola 68k, MIPS, Sparc, HP PA
Little Endian: rightmost byte is word address
    Intel 80x86, DEC Vax, DEC Alpha (Windows NT)
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0
Notes: Talk about the reasons (performance) for the word/byte alignment restriction

## Slide 40: Aside: Loading and Storing Bytes
MIPS provides special instructions to move bytes
lb $t0, 1($s3) #load byte from memory
sb $t0, 6($s3) #store byte to memory
0x28 19 8 16 bit offset
What 8 bits get loaded and stored?
  load byte places the byte from memory in the rightmost 8 bits of the destination register
    what happens to the other bits in the register?
  store byte takes the byte from the rightmost 8 bits of a register and writes it to a byte in memory
    what happens to the other bits in the memory word?
Notes: load byte takes the contents of the byte at the memory address specified, zero-extends it, and loads it into the register
Store byte leaves the other bits in the memory word intact.

## Slide 41: Example of Loading and Storing Bytes
Given following code sequence and memory state what is the state of the memory after executing the code?
add $s3, $zero, $zero
lb $t0, 1($s3)
sb $t0, 6($s3)
Memory
0x 0 0 9 0 1 2 A 0
Data
Word
Address (Decimal)
0
4
8
12
16
20
24
0x F F F F F F F F
0x 0 1 0 0 0 4 0 2
0x 1 0 0 0 0 0 1 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
$t0 = 0x00000090
mem(4) = 0xFFFF90FF
mem(4) = 0xFF12FFFF
What value is left in $t0?
What if the machine was little Endian?
What word is changed in Memory and to what?
$t0 = 0x00000012
Notes: For lecture
Big Endian Little Endian
0 1 2 3 3 2 1 0
$t0 gets 90 $t0 gets 12
word 4 gets FFFF90FF word 4 gets FF12FFFF

## Slide 42: MIPS Immediate Instructions
addi $sp, $sp, 4 #$sp = $sp + 4
slti $t0, $s2, 15 #$t0 = 1 if $s2<15
Machine format (I format):
0x0A 18 8 0x0F
Small constants are used often in typical code
Possible approaches?
  put “typical constants” in memory and load them
  create hard-wired registers (like $zero) for constants like 1
  have special instructions that contain constants !
The constant is kept inside the instruction itself!
  Immediate format limits values to the range +215–1 to -215
Notes: in gcc 52% of arithmetic operations involve constants – in spice its 69%
have the students answer why not – speed and limited number of registers
much faster than if loaded from memory
addi and slti do sign extend of immediate operand into the leftmost bits of the destination register (ie., copies the leftmost bit of the 16-bit immediate value into the upper 16 bits)
by contrast, ori and andi loads zero’s into the upper 16 bits and so is usually used (instead of the addi) to build 32 bit constants

## Slide 43: Aside: How About Larger Constants?
We'd also like to be able to load a 32 bit constant into a register, for this we must use two instructions
a new "load upper immediate" instruction
lui $t0, 1010101010101010
Then must get the lower order bits right, use ori $t0, $t0, 1010101010101010
16 0 8 10101010101010102
1010101010101010
0000000000000000
1010101010101010
0000000000000000
1010101010101010 1010101010101010
Notes: For lecture
sets the upper 16 bits of a constant in a register, allowing the next instruction to specify the lower 16 bits of the constant
note that lui fills the lower 16 bits of the register with zero’s
why can’t addi be used as the second instruction for this 32 bit constant?
also note – the assembler lets me specify constants larger than 16 bits in one instruction and then expands the code into two instructions (lui and ori) automatically

## Slide 44: Review: Unsigned Binary Representation
Hex | Binary | Decimal
0x00000000 | 0…0000 | 0
0x00000001 | 0…0001 | 1
0x00000002 | 0…0010 | 2
0x00000003 | 0…0011 | 3
0x00000004 | 0…0100 | 4
0x00000005 | 0…0101 | 5
0x00000006 | 0…0110 | 6
0x00000007 | 0…0111 | 7
0x00000008 | 0…1000 | 8
0x00000009 | 0…1001 | 9
 | … | 
0xFFFFFFFC | 1…1100 | 
0xFFFFFFFD | 1…1101 | 
0xFFFFFFFE | 1…1110 | 
0xFFFFFFFF | 1…1111 | 
232 - 1
232 - 2
232 - 3
232 - 4
232 - 1
1 1 1 . . . 1 1 1 1 bit
31 30 29 . . . 3 2 1 0 bit position
231 230 229 . . . 23 22 21 20 bit weight
1 0 0 0 . . . 0 0 0 0 - 1
Notes: All positive numbers - no sign bit
last entry is most significant byte address
fourth from last entry is most significant word address

## Slide 45: Review: Signed Binary Representation
2’sc binary | decimal
1000 | -8
1001 | -7
1010 | -6
1011 | -5
1100 | -4
1101 | -3
1110 | -2
1111 | -1
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
23 - 1 =
-(23 - 1) =
-23 =
1010
complement all the bits
1011
and add a 1
complement all the bits
0101
and add a 1
0110
Notes: Signed numbers – assuming 2’s complement representation – for eight bits
Note that msb of 1 indicates a negative number, the bit string all 0’s is zero, that the largest positive number that can be represented is 7 (2**(n-1) –1 for n bits) whereas the largest negative number that can be represented is –8 (-2**(n-1) for n bits)

## Slide 46: MIPS Shift Operations
Need operations to pack and unpack 8-bit characters into 32-bit words
Shifts move all the bits in a word left or right
sll $t2, $s0, 8 #$t2 = $s0 << 8 bits
srl $t2, $s0, 8 #$t2 = $s0 >> 8 bits
Instruction Format (R format)
Such shifts are called logical because they fill with zeros
  Notice that a 5-bit shamt field is enough to shift a 32-bit value 25 – 1 or 31 bit positions
0 16 10 8 0x00
Notes: also have sllv, srlv, and srav

## Slide 47: MIPS Logical Operations
There are a number of bit-wise logical operations in the MIPS ISA
and $t0, $t1, $t2 #$t0 = $t1 & $t2
or $t0, $t1, $t2 #$t0 = $t1 | $t2
nor $t0, $t1, $t2 #$t0 = not($t1 | $t2)
Instruction Format (R format)
andi $t0, $t1, 0xFF00 #$t0 = $t1 & ff00
ori $t0, $t1, 0xFF00 #$t0 = $t1 | ff00
Instruction Format (I format)
0 9 10 8 0 0x24
0x0D 9 8 0xFF00

## Slide 48: MIPS Control Flow Instructions
MIPS conditional branch instructions:
bne $s0, $s1, Lbl #go to Lbl if $s0!=$s1 beq $s0, $s1, Lbl #go to Lbl if $s0=$s1
  Ex: if (i==j) h = i + j;
bne $s0, $s1, Lbl1 add $s3, $s0, $s1 Lbl1: ...
Instruction Format (I format):
0x05 16 17 16 bit offset
How is the branch destination address specified?

## Slide 49: Specifying Branch Destinations
Use a register (like in lw and sw) added to the 16-bit offset
  which register? Instruction Address Register (the PC)
    its use is automatically implied by instruction
    PC gets updated (PC+4) during the fetch cycle so that it holds the address of the next instruction
  limits the branch distance to -215 to +215-1 (word) instructions from the (instruction after the) branch instruction, but most branches are local anyway
PC
Add
32
32
32
32
32
offset
16
32
00
sign-extend
from the low order 16 bits of the branch instruction
branch dst
address
?
Add
4
32
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 50: In Support of Branch Instructions
We have beq, bne, but what about other kinds of branches (e.g., branch-if-less-than)? For this, we need yet another instruction, slt
Set on less than instruction:
slt $t0, $s0, $s1 # if $s0 < $s1 then # $t0 = 1 else # $t0 = 0
Instruction format (R format):
Alternate versions of slt
slti $t0, $s0, 25 # if $s0 < 25 then $t0=1 ...
sltu $t0, $s0, $s1 # if $s0 < $s1 then $t0=1 ...
sltiu $t0, $s0, 25 # if $s0 < 25 then $t0=1 ...
2
0 16 17 8 0x24
Notes: Unsigned (u) versus signed integer comparison

## Slide 51: Aside: More Branch Instructions
Can use slt, beq, bne, and the fixed value of 0 in register $zero to create other conditions
  less than blt $s1, $s2, Label
  less than or equal to ble $s1, $s2, Label
  greater than bgt $s1, $s2, Label
  great than or equal to bge $s1, $s2, Label
slt $at, $s1, $s2 #$at set to 1 if
bne $at, $zero, Label #$s1 < $s2
Such branches are included in the instruction set as pseudo instructions - recognized (and expanded) by the assembler
  Its why the assembler needs a reserved register ($at)
Notes: For lecture
blt $s1,$s2 Label =
slt $at,$s1,$s2 #at gets 1 if $s1 < $s2
bne $at,$zero,Label

## Slide 52: Bounds Check Shortcut
Treating signed numbers as if they were unsigned gives a low cost way of checking if 0 ≤ x < y (index out of bounds for arrays)
sltu $t0, $s1, $t2 # $t0 = 0 if # $s1 > $t2 (max) # or $s1 < 0 (min) beq $t0, $zero, IOOB # go to IOOB if # $t0 = 0
The key is that negative integers in two’s complement look like large numbers in unsigned notation. Thus, an unsigned comparison of x < y also checks if x is negative as well as if x is less than y.

## Slide 53: Other Control Flow Instructions
MIPS also has an unconditional branch instruction or jump instruction: j label #go to label
Instruction Format (J Format):
0x02 26-bit address
PC
4
32
26
32
00
from the low order 26 bits of the jump instruction
Notes: If-then-else code compilation

## Slide 54: Aside: Branching Far Away
What if the branch destination is further away than can be captured in 16 bits?
The assembler comes to the rescue – it inserts an unconditional jump to the branch target and inverts the condition
beq $s0, $s1, L1
becomes
bne $s0, $s1, L2
j L1
L2:

## Slide 55: Instructions for Accessing Procedures
MIPS procedure call instruction: jal ProcedureAddress #jump and link
Saves PC+4 in register $ra to have a link to the next instruction for the procedure return
Machine format (J format):
Then can do procedure return with a
jr $ra #return
Instruction format (R format):
0x03 26 bit address
0 31 0x08
Notes: jr jumps to the address stored in the register – in this case $ra – which is just what we want.

## Slide 56: Six Steps in Execution of a Procedure
Main routine (caller) places parameters in a place where the procedure (callee) can access them
  $a0 - $a3: four argument registers
Caller transfers control to the callee
Callee acquires the storage resources needed
Callee performs the desired task
Callee places the result value in a place where the caller can access it
  $v0 - $v1: two value registers for result values
Callee returns control to the caller
  $ra: one return address register to return to the point of origin

## Slide 57: Aside: Spilling Registers
What if the callee needs to use more registers than allocated to argument and return values?
  callee uses a stack – a last-in-first-out queue
low addr
high addr
$sp
One of the general registers, $sp ($29), is used to address the stack (which “grows” from high address to low address)
  add data onto the stack – push
    $sp = $sp – 4 data on stack at new $sp
  remove data from the stack – pop
    data from stack at $sp $sp = $sp + 4
top of stack
Notes: Note that temporary registers $t0 through $t9 can also be used as by MIPS convention they are not preserved by the callee (kept intact) across subroutine boundaries
However, saved registers $s0 through $s7 must be preserved by the calle - I.e., if the callee uses one, it must first save it and then restore it to its old value before returning control to the caller

## Slide 58: Aside: Allocating Space on the Stack
The segment of the stack containing a procedure’s saved registers and local variables is its procedure frame (aka activation record)
  The frame pointer ($fp) points to the first word of the frame of a procedure – providing a stable “base” register for the procedure
    $fp is initialized using $sp on a call and $sp is restored using $fp on a return
low addr
high addr
$sp
Saved argument regs (if any)
Saved return addr
Saved local regs (if any)
Local arrays & structures (if any)
$fp
Notes: On the other hand, the stack pointer (sp) might change during the procedure (not the case for all of our examples) so references to a local variable in memory might have different offsets wrt the sp depending on where they are in the procedure.

## Slide 59: Aside: Allocating Space on the Heap
Static data segment for constants and other static variables (e.g., arrays)
Dynamic data segment (aka heap) for structures that grow and shrink (e.g., linked lists)
  Allocate space on the heap with malloc() and free it with free() in C
Memory
0x 0000 0000
Text
(Your code)
Reserved
Static data
0x 0040 0000
0x 1000 0000
0x 1000 8000
0x 7f f f f f f c
Stack
Dynamic data
(heap)
$sp
$gp
PC
Notes: Stack and heap grow towards each other.
Malloc() allocates space on the heap and returns a pointer to it. Memory allocation is controlled by programs (in C) and is the source of many common and difficult bugs. Forgetting to free space leads to “memory leak” and the need for “garbage collection” and freeing space to early to “dangling pointers”.

## Slide 60: MIPS Instruction Classes Distribution
Frequency of MIPS instruction classes for SPEC2006
Instruction Class | Frequency | 
 | Integer | Ft. Pt.
Arithmetic | 16% | 48%
Data transfer | 35% | 36%
Logical | 12% | 4%
Cond. Branch | 34% | 8%
Jump | 2% | 0%

## Slide 61: Atomic Exchange Support
Need hardware support for synchronization mechanisms to avoid data races where the results of the program can change depending on how events happen to occur
  Two memory accesses from different threads to the same location, and at least one is a write
Atomic exchange (atomic swap) – interchanges a value in a register for a value in memory atomically, i.e., as one operation (instruction)
  Implementing an atomic exchange would require both a memory read and a memory write in a single, uninterruptable instruction. An alternative is to have a pair of specially configured instructions
ll $t1, 0($s1) #load linked
sc $t0, 0($s1) #store conditional

## Slide 62: Automic Exchange with ll and sc
If the contents of the memory location specified by the ll are changed before the sc to the same address occurs, the sc fails (returns a zero)
try: add $t0, $zero, $s4 #$t0=$s4 (exchange value)
ll $t1, 0($s1) #load memory value to $t1
sc $t0, 0($s1) #try to store exchange #value to memory, if fail #$t0 will be 0
beq $t0, $zero, try #try again on failure
add $s4, $zero, $t1 #load value in $s4
If the value in memory between the ll and the sc instructions changes, then sc returns a 0 in $t0 causing the code sequence to try again.
Notes: Use care when inserting instructions between the ll and sc. Only register-register instructions can be safely permitted, otherwise it is possible to create deadlock where the processor can never complete the sc because of repeated page faults.

## Slide 63: The C Code Translation Hierarchy
C program
compiler
assembly code
assembler
object code
library routines
executable
linker
loader
memory
machine code
Notes: Four logical phases all programs go through
C code – x.c or .TXT
assembly code – x.s or .ASM
object code – x.o or .OBJ
executable – a.out or .EXE

## Slide 64: Compiler Benefits
Comparing performance for bubble (exchange) sort
  To sort 100,000 words with the array initialized to random values on a Pentium 4 with a 3.06 clock rate, a 533 MHz system bus, with 2 GB of DDR SDRAM, using Linux version 2.4.20
gcc opt | Relative performance | Clock cycles (M) | Instr count (M) | CPI
None | 1.00 | 158,615 | 114,938 | 1.38
O1 (medium) | 2.37 | 66,990 | 37,470 | 1.79
O2 (full) | 2.38 | 66,521 | 39,993 | 1.66
O3 (proc mig) | 2.41 | 65,747 | 44,993 | 1.46
The unoptimized code has the best CPI, the O1 version has the lowest instruction count, but the O3 version is the fastest. Why?
Notes: In order to control compilation-time and compiler memory usage, and the trade-offs between speed and space for the resulting executable, GCC provides a range of general optimization levels, numbered from 0--3, as well as individual options for specific types of optimization.
An optimization level is chosen with the command line option -OLEVEL, where LEVEL is a number from 0 to 3. The effects of the different optimization levels are described below:
-O0 or no -O option (default)
At this optimization level GCC does not perform any optimization and compiles the source code in the most straightforward way possible. Each command in the source code is converted directly to the corresponding instructions in the executable file, without rearrangement. This is the best option to use when debugging a program and is the default if no optimization level option is specified.
-O1 or -O
This level turns on the most common forms of optimization that do not require any speed-space tradeoffs. With this option the resulting executables should be smaller and faster than with -O0. The more expensive optimizations, such as instruction scheduling, are not used at this level. Compiling with the option -O1 can often take less time than compiling with -O0, due to the reduced amounts of data that need to be processed after simple optimizations.
-O2
This option turns on further optimizations, in addition to those used by -O1. These additional optimizations include instruction scheduling. Only optimizations that do not require any speed-space tradeoffs are used, so the executable should not increase in size. The compiler will take longer to compile programs and require more memory than with -O1. This option is generally the best choice for deployment of a program, because it provides maximum optimization without increasing the executable size. It is the default optimization level for releases of GNU packages.
-O3
This option turns on more expensive optimizations, such as function inlining, in addition to all the optimizations of the lower levels -O2 and -O1. The -O3 optimization level may increase the speed of the resulting executable, but can also increase its size. Under some circumstances where these optimizations are not favorable, this option might actually make a program slower.
-funroll-loops
This option turns on loop-unrolling, and is independent of the other optimization options. It will increase the size of an executable. Whether or not this option produces a beneficial result has to be examined on a case-by-case basis.
-Os
This option selects optimizations which reduce the size of an executable. The aim of this option is to produce the smallest possible executable, for systems constrained by memory or disk space. In some cases a smaller executable will also run faster, due to better cache usage.
It is important to remember that the benefit of optimization at the highest levels must be weighed against the cost. The cost of optimization includes greater complexity in debugging, and increased time and memory requirements during compilation. For most purposes it is satisfactory to use -O0 for debugging, and -O2 for development and deployment.

## Slide 65: The Java Code Translation Hierarchy
Java program
compiler
Class files (Java bytecodes)
Just In Time (JIT) compiler
Compiled Java methods (machine code)
Java library routines (machine code)
Java Virtual Machine

## Slide 66: Sorting in C versus Java
Comparing performance for two sort algorithms in C and Java
  The JVM/JIT is Sun/Hotspot version 1.3.1/1.3.1
 | Method | Opt | Bubble | Quick | Speedup quick vs bubble
 |  |  | Relative performance |  | 
C | Compiler | None | 1.00 | 1.00 | 2468
C | Compiler | O1 | 2.37 | 1.50 | 1562
C | Compiler | O2 | 2.38 | 1.50 | 1555
C | Compiler | O3 | 2.41 | 1.91 | 1955
Java | Interpreted |  | 0.12 | 0.05 | 1050
Java | JIT compiler |  | 2.13 | 0.29 | 338
Observations?
Notes: Unoptimized C prgram is 8.3 times faster than the interpreted Java code for bubble.
Using JIT makes Java 2.1 times faster than the unoptimized C and within a factor of 1.13 of the highest optimized C code.
Ratio’s aren’t as close for quick, presumably because it is harder to amortize the cost of runtime compilation over the shorter execution time.
The last column demonstrates the impact of a better algorithm

## Slide 67: Addressing Modes Illustrated
1. Register addressing
op rs rt rd funct
Register
word operand
op rs rt offset
2. Base (displacement) addressing
base register
Memory
word or byte operand
3. Immediate addressing
op rs rt operand
4. PC-relative addressing
op rs rt offset
Program Counter (PC)
Memory
branch destination instruction
5. Pseudo-direct addressing
op jump address
Program Counter (PC)
Memory
jump destination instruction
||

## Slide 68: MIPS Organization So Far
Processor
Memory
32 bits
230
words
read/write
addr
read data
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
registers
($zero - $ra)
32
32
32
32
32
32
5
5
5
PC
ALU
32
32
32
32
32
0
1
2
3
7
6
5
4
byte address
(big Endian)
Fetch
PC = PC+4
Decode
Exec
Add
32
32
4
Add
32
32
branch offset

## Slide 69: Next Lecture and Reminders
Next lecture
  MIPS ALU design and single-cycle implementation
    Reading assignment – PH, Chapter 3
Reminders
  HW1 will be online tmr and due next Thursday noon time, Jan. 23.
  Look for your project partner