## Slide 1: Ping and Traceroute by Aleisa A. Drivere Supervisor Graciela Perera

## Slide 2: Ping and Traceroute lab
Active measurement : adds traffic to a network.
Passive measurement: captures traffic generated by others.
Ping and Traceroute are active measurement methods.

## Slide 3: Ping
One of the oldest tools for network measurement
Uses Internet Control Message Protocol (ICMP) packets
Echo packet sent by source
Echo reply sent back to source by destination

## Slide 4: Ping
Very simple to use
Can use hostname (ex. www.google.com), or IP address (ex. 74.125.95.99).
At command prompt:
ping www.google.com
OR
ping 74.125.95.99

## Slide 5: Ping
To find IP addresses of known hostnames, at the Windows command prompt, type nslookup destination_hostname:
ex.) nslookup www.google.com

## Slide 6: Ping options
-w timeout : Timeout in milliseconds to wait for each reply.
-i TTL : Time To Live.
-a: resolve addresses to hostnames.
-n count : Number of echo requests to send.
-t : Ping the destination host until interrupted.
-r count: Record route for count hops.
-s count: Timestamp for count hops.

## Slide 7: Ping options
At command prompt:
Ping [options] destination_host
Example:
Ping –t www.yahoo.com
This will continue to ping the destination host until an interrupt is issued (in Windows, press ctrl_c).

## Slide 8: Traceroute
Traceroute sends a set of packets (default number in set is 3) with the target address as the destination. The first set has a Time To Live (TTL) of 1.
Traceroute increments the TTL by 1 on each successive set of packets (the second set has TTL of 2, third set TTL of 3, etc.)
Traceroute stops sending packet sets when it receives return packets from the original destination host.

## Slide 9: Traceroute
At command prompt:
traceroute destination_host
Windows version is tracert
Like ping, traceroute can use the hostname or IP address of the destination host.

## Slide 10: Traceroute
The most common type uses ICMP, just like ping.
Other types include UDP, TCP, Paris.
Windows tracert uses ICMP. Traceroute utilities in Unix-based operating systems (Mac OS, Linux) use UDP by default, with ICMP option available.

## Slide 11: Traceroute options
-w response_wait_time: default is 5 seconds.
-q number_of_queries: number of packets in each set. Default is 3.
-m maximum_hop_count: default is 30 for ICMP-based traceroute.

## Slide 12: Analyzing Traceroute Data
Each IP address that appears in a traceroute output can be looked up in a WHOIS database.
WHOIS will indicate the entity to which the IP address is registered.

## Slide 13: Analyzing Traceroute Data
In a packet switched network (like the Internet), packets can take different routes. This is why traceroutes issued at different times to the same target destination may show different intermediary routers.

## Slide 14: Request For Comments
ICMP: RFC 792
Ping: RFC 1739
Traceroute: RFC 1393
http://www.ietf.org

## Slide 15: References
Crovella, Mark, with Balachander Krishnamurthy, Internet Measurement: infrastructure, traffic & applications, 2006, John Wiley & Sons: New Jersey.
Kurose, James F., with Keith W. Ross, Computer Networking: A Top-Down Approach, Fifth Edition, 2010, Addison-Wesley: New York.
http://www.traceroute.org
http://en.wikipedia.org/wiki/Ping
http://en.wikipedia.org/wiki/Traceroute