## Slide 1: Units of Time, Storage, Throughput
Updated: 08/17/2014 AA
Morgan Kaufmann et al

## Slide 2: KHz, MHz, GHz, …My head hurtz!
    Hertz is a measure of the frequency of a periodic event.
    Named for German physicist Heinrich Rudolf Hertz
    One hertz means one time per second.
    Exercise:
    The average human heart beats 72 times per minute.
    What is frequency of the heart in hertz?
    72 beats per minute / 60 seconds per minute
    = 1.2 Hertz

## Slide 3: Cycle Time
A hummingbird can flap its wings up to 80 times per second.
The hummingbird flaps its wings at 80 Hertz.
How many seconds does it take for each flap?
  1 / 80 times/second = 1/80 second = 0.0125 seconds
The duration of time to complete one event is called the cycle time.

## Slide 4: Cycle Time and Frequency
A Chihuahua can do one wag of its tail in 0.1 seconds.
  0.1 seconds / wag
How many times does the dog wag its tail in one second?
1 / (0.1 seconds / wag) = 10 wags / second
What is the frequency of this dog’s tail wagging? 10 HZ
What is the relationship between cycle time and frequency?
  They are reciprocals

## Slide 5: Units of Frequency
1 Cycle per second = 1 Hertz = 1 Hz
  One operation per second
1,000 (10^3) Cycles per second = 1 Kilohertz = 1 KHz
  1,000 operations per second
1,000,000 (10^6) Cycles per second = 1 Megahertz = 1 MHz
1,000,000,000 (10^9) Cycles per second = 1 Gigahertz = 1 GHz
1 x 10^12 Cycles per second = 1 Terahertz

## Slide 6: Units of Time
Second
Millisecond = ms = 1/1000th of a second = 1 x 10^-3 seconds
Microsecond = µs = 1 x 10^-6 seconds
Nanosecond = ns = 1 x 10^-9 seconds

## Slide 7: Units of Time Exercises
Exercise: Convert 2.5 seconds to milliseconds
  Answer:
Exercise: Convert 0.00004 seconds into milliseconds
  Answer:
Exercise: Convert 0.04 ms to nanoseconds
  Answer:
Exercise: Convert 5 microseconds into seconds
Answer:

## Slide 8: Units of Time Exercises
Exercise: Convert 2.5 seconds to milliseconds
  Answer: 2.5 seconds x 1000 ms / second = 2500 ms
Exercise: Convert 0.00004 seconds into milliseconds
  Answer: 0.00004 seconds x 1000 ms/second = 0.04 ms
Exercise: Convert 0.04 ms to nanoseconds
  Answer: 0.04 ms x 1000000 ns/ms = 40000 ns
Exercise: Convert 5 microseconds into seconds
Answer: 5 x 10^-6 seconds = 0.000005 seconds

## Slide 9: Clock Cycle Exercises
A processor runs at 5 KHz, what is its cycle time?
Answer:
A processor runs at 100 MHz, what is its cycle time in ns?
Answer:
What is the clock speed in Hz of a processor whose cycle time is 2 x 10^-3 seconds?
Answer:
What is the clock speed in Mhz of a processor whose cycle time is 2 x 10^-6 seconds?
Answer

## Slide 10: Clock Cycle Exercises
A processor runs at 5 KHz, what is its cycle time?
Answer: 1/5000 = 1/(5x10^3) = 1/5 x 10^-3 = 0.2 x 10^-3 = 0.0002 seconds
A processor runs at 100 MHz, what is its cycle time in ns?
Answer: 1 / 100 x 10^6 = 1 / 1x10^8 = 1 x 10^-8 seconds
1 x 10^-8 seconds = 10 x 10^-9 seconds = 10 ns
What is the clock speed in Hz of a processor whose cycle time is 2 x 10^-3 seconds?
Answer: 1 / ( 2 x 10^-3) = ½ x 10^3 = 0.5 x 1000 = 500 Hz
What is the clock speed in Mhz of a processor whose cycle time is 2 x 10^-6 seconds?
Answer: 1 / (2 x 10^-6) = ½ x 10^6 = 0.5 x 1,000,000 = .5 Mhz

## Slide 11: Units of Memory or Storage
1 bit
1 byte = 8 bits
  Represent 1 character of text with 1 byte
1 kilobyte = 1 KB = 1024 bytes about 10^3 bytes
  Typical word processor file 100 KB
1 megabyte = 1024 KB = 1 MB about 10^6 bytes
  Digital photograph 1 to 4 MB
1 gigabyte = 1024 MB about 10^9 bytes
  Digital movie file 1 GB

## Slide 12: Exercise
Express 256,000,000 bytes as…
_________ Megabytes MB
_________ Gigabytes GB
_________ Kilobytes KB

## Slide 13: Exercise
Express 256,000,000 bytes as…
256 Megabytes MB
0.256 Gigabytes GB
256,000 Kilobytes KB

## Slide 14: Exercise
Express 3.0 x 10^6 bytes as…
____ Megabytes MB
____ Gigabytes GB
____ Kilobytes KB

## Slide 15: Exercise
Express 3.0 x 10^6 bytes as…
____ Megabytes MB
3.0 x 10^6 bytes / 10^6 bytes/MB = 3.0 MB
____ Gigabytes GB
3.0 x 10^6 bytes / 10^9 bytes/GB =
3.0 x 10^-3 GB =
0.003 GB
____ Kilobytes KB
3.0 x 10^6 bytes / 10^3 bytes/KB =
3.0 x 10^3 KB =
3000 KB

## Slide 16: Throughput
Throughput is a measure of the amount of work completed per unit of time.
Example:
Willy Wonka’s Chocolate Factory produces 600 everlasting gobstoppers every 4 hours.
What is the throughput in gobstoppers per hour? = 150 g / hr
Example:
Throughput of 100 gallons of chocolate / minute
How many gallons processed in 10 hours?
100 x 60 x 10 = 60,000 gallons

## Slide 17: Bus Bandwidth
Bandwidth is the speed which information can be moved along a bus
Bandwidth = amount of information (or stuff) moved / unit time
Bandwidth is measured in bytes, KB, or MB per second
Examples:
  100 KB per second
  2 GB per second
What factors determine the peak or maximum bandwidth of a bus?
Consider the tale of the fire-fighting gondoliers...

## Slide 18: Fire-fighting Gondoliers
There is a fire in Venice
The 16 fire fighters need to cross a canal to get to the fire
One gondola and its gondolier can ferry one fire fighter and his or her equipment in 10 minutes
How long will it take to move all 16 fire fighters?
  16 x 10 minutes = 160 minutes (ignore empty last return trip)
What is the bandwidth?
  16 / 160 = 0.1 fire fighter per minute
Source: Rick Russell from about.com

## Slide 19: Fire-fighting Gondoliers: Speedup #1
The gondolier realizes that more help is needed and so he calls 7 of his gondolier pals to bring their boats
Now 8 fire fighters can cross the canal at the same time
How long will it take to move all 16 fire fighters?
  2 x 10 minutes = 20 minutes
What is the bandwidth?
  16 / 20 = 0.8 fire fighter per minute (8 times faster)

## Slide 20: Fire-fighting Gondoliers: Speedup #2
The mayor runs up screaming that his cat is stuck in a burning building and must be saved in 5 minutes.
Is there any way to get a fire fighter across in time?
  Speed up the transfer speed
Suppose the 8 gondoliers had 8 motor boats that can ferry one fire fighter and his or her equipment in 4 minutes
How long will it take to move all 16 fire fighters?
  2 x 4 minutes = 8 minutes
What is the bandwidth?
  16 / 8 = 2.0 fire fighter per minute

## Slide 21: Bandwidth Summary
Increase bandwidth by increasing the “width” of the bus or the number of lanes of the highway to move more information at the same time
  Typical PC buses transport information in chunks of 8, 16, 32, 64, 128 or 256 bytes
Increase the speed of travel on the bus (“raise the speed limit”)
  Bus speed is rated in cycles per second
  One cycle represents one transfer of information
    (One gondola crossing)

## Slide 22: Bandwidth Questions
If a bus runs at 100 million clock cycles per second (100MHz) and it delivers 8 bytes on each clock cycle, what is its bandwidth?
  800 million bytes per second = 800 MB / second
If a bus runs at 150MHz and delivers 8 bytes per clock cycle, then what is its bandwidth?
  8 x 150 million = 1,200 MB / second = 1.2 GB / second

## Slide 23: Bandwidth Questions
(1) What is the bandwidth expressed in bytes/second of an 8-bit wide bus running at 10 MHz?
(2) What is the bandwidth expressed in MB/second of a 32-bit wide bus running at 10 MHz?
(3) What speed must an 8-bit wide bus have in order to equal the bandwidth of a 64-bit wide bus running at 800 MHz?

## Slide 24: Bandwidth Questions
(1) What is the bandwidth expressed in bytes/second of an 8-bit wide bus running at 10 MHz?
  1 bytes x 10,000,000 per second = 10,000,000 bytes/sec
(2) What is the bandwidth expressed in MB/second of a 32-bit wide bus running at 10 MHz?
  4 bytes x 10,000,000 per second = 40,000,000 bytes/sec = 40 MB/sec
(3) What speed must an 8-bit wide bus have in order to equal the bandwidth of a 64-bit wide bus running at 800 MHz?
  The 8-bit wide bus carries one-eight the data per transfer so it must run at a rate of eight times that of the 64-bit bus
   8 x 800 MHz = 6,400 MHz = 6.4 GHz

## Slide 25: Peak versus Sustained Bandwidth
The previous bandwidth calculations represent the theoretical or peak bandwidth assuming that a constant stream of data is always being pumped one-way through the bus
(1) In practice a bus services two-way traffic
  For example, send data from CPU to RAM or from RAM to CPU
(2) In practice there is some overhead involved in preparing to send and in receiving a chunk of data
  This overhead is called latency
Consequently, in practice the actual or sustained bandwidth of a bus is less than its theoretical or peak bandwidth

## Slide 26: Latency and Fire-fighting Gondoliers
Our estimate of 10 minutes to transmit one fire fighter from one side of the canal to the other was greatly simplified
Consider how that 10 minutes might be spent...
  Load fire fighter and gear: 1.5 minute
  Cross the canal with the fire fighter: 4 minutes
  Unload fire fighter and gear: 1.5 minute
  Empty boat returns to the fire station: 3 minutes
Only 4 of the 10 minutes is spent actually moving a fire fighter
  Two-way trip represents reality of bus needing to handle two-way transmissions of data; only one of which goes at a time
  Loading/unloading represents latency (overhead)

## Slide 27: Multiple Buses
Having a USB digital camera, hard drive, and video card sharing the same bus would be like having pedestrians, bicyclists, and automobiles sharing the same road
Modern PC motherboards include more than one bus to accommodate traffic flowing at vastly different speeds
Use a separate switch and bus line for each different type of traffic
  USB bus (slowest speed)
  Expansion device bus for hard drive, CD, DVD, network card
  Video bus (PCI-E 16x)
  Frontside bus – connects CPU & RAM

## Slide 28: PC Bus Bandwidths
USB 1.0 bus
  12 Mbits per second (megabits)
  How many Megabytes per second? 12/8 = 1.5 MB/sec
USB 2.0 bus
  480 Mbits per second (megabits)
  How many Megabytes per second? 480/8 = 60 MB/sec
PCI bus: 132 MB per second
AGP 8X: 2 GB per second
PCI Express: 250 MB per second
  Video slot is 16x or 4 GB per second
Frontside bus 3.16 GHZ Intel E8500 1.33GHZ FSB