## Slide 1: Overview of Instruction Set Architectures
Adapted from Ch. 4 of N. Carter’s Computer Architecture

## Slide 2: Variety of Instruction Sets
Number of operands for ALU instructions
Number and type of processor registers
How to refer to memory locations
Number of bits used to address memory
Number of bits needed to encode a machine language instruction

## Slide 3: Number of Operands
Zero operands for ALU instructions:
Stack architectures operate on data values held in a last-in-first-out (LIFO) stack.
Push a new value on top of stack.
Pop the topmost value(s) off the stack.
Computer Organization

## Slide 4: Stack Machine Instructions
Push operand value
Pop
MUL
ADD
SUB
DIV

## Slide 5: Multiplication with a Stack
10
Empty
Push #10
10
Push #20
20
200
MUL
Push two operands on top of stack
MUL: Pops two operands, pushes product
SP = -1
SP = 0
SP = 1
SP = 0
MUL instruction specifies no operands. Implicitly pop operands from stack.
Push #10
Push #20
MUL
Computer Organization

## Slide 6: Subtraction with a Stack
10
Empty
Push #10
10
Push #20
20
-10
SUB
Push two operands on top of stack
SUB: Pops two operands, pushes difference
SP = -1
SP = 0
SP = 1
SP = 0
Subtracts top value from next value down
Push #10
Push #20
SUB

## Slide 7: Stack Exercise
4.7 Write a stack program that computes
((5 + (3 x 7)) – 8)
First, express in Reverse Polish Notation
5 + (3 7 x) – 8
5 (3 7 x) + - 8
5 (3 7 x) + 8 -

## Slide 8: Stack Exercise: Solution
Write a stack program that computes
5 + (3 x 7) – 8
Trace the execution of the stack program to verify the result.
PUSH #5
PUSH #3
PUSH #7
MUL
ADD
PUSH #8
SUB

## Slide 9: Stack Machines in History
Example: Burroughs 5000 (B5000)
Originated in 1961
Designed for ALGOL language
Wanted ease of language compiler development
Topmost two words of stack held in two processor registers rest of stack in memory.

## Slide 10: Legacy of Stack Machines
Modern compilers still use RPN and a stack algorithm to compile arithmetic expressions
Function calls are implemented using a stack of activation records that hold function return addresses & local variables

## Slide 11: Summary of Stack Machines
Stack instructions take less memory to encode since 0 or 1 operand instructions.
Easier to write a stack machine assembler or compiler.
Stack does not support random access.
Bottleneck since all operations occur only with the few values atop the stack.

## Slide 12: Accumulator Architectures
1946 paper on “Stored program computer” proposed a single ALU register called the accumulator.
The EDSAC (1950) used its accumulator register to hold the result of the processor’s calculations (like our TOY-1 calculator)

## Slide 13: EDSAC
http://www.dcs.warwick.ac.uk/~edsac (c) Martin Campbell-Kelly
Photo of EDSAC just after its completion in 1949

## Slide 14: Accumulator Register
18 machine instructions each specified by a single letter mnemonic such as A = Add
Each mnemonic was translated by a simple “keyboard” into binary in the form of holes punched on a paper tape

## Slide 15: EDSAC Mnemonics
A Add
S Subtract
I Read
T Transfer information to storage
Z Stop the machine

## Slide 16: DEC PDP-8 (1965)
Single accumulator register
Each assembly instruction is encoded into 12 bits
8 different machine instructions

## Slide 17: PDP-8 Instruction Format
3 bits to encode one of 8 possible machine instructions
Remaining 9 bits used to specify either a constant, memory address, or I/O device parameter
Op-Code
Address / Data
3 bits
9 bits

## Slide 18: Example PDP-8 Program
// Computer C = A + B
// Clear accumulator to zero
CLA
// accumulator = accumulator + A
TAD A
// accumulator = accumulator + B
TAD B
// store accumulator value into memory location C
DCA C
Source: http://userpages.wittenberg.edu/bshelburne/Comp255S/PDP8Assembler.htm

## Slide 19: Accumulator & Registers
Some early personal computer processors such as the MOS 6502 had an accumulator plus two index registers
Examples: Apple II, Commodore 64, Atari 800, Nintendo NES 8-bit game console
Word size is 8-bits (1 byte)
Computer Organization

## Slide 20: 6502 Processor
8-bit Accumulator
X Index Register
Y Index Register
16-bit Program Counter
16-bit Stack Pointer
3 8-bit registers: accumulator, X index, and Y index
Stack is used for passing function parameters
8-bit Processor Status

## Slide 21: 6502 Addressing Modes
Addressing mode is the way in which operand values are specified
6502 provided...
  Immediate mode
  Absolute memory addressing
  Absolute indexed memory addressing

## Slide 22: Immediate Mode
Operand value is directly specified as a constant value
# designates operand as immediate value
Example:
  // Load accumulator with value 10
  LDA #10

## Slide 23: Immediate Mode
// Load accumulator with value 0
LDA #0
// Add value 10 to contents of accumulator
ADC #10
// Subtract value 5 from accumulator
SBC #5

## Slide 24: Immediate Mode Example
Show contents of accumulator after executing these instructions
LDA #7
ADC #10
SBC #3
Accum. = 7
Accum. = 17
Accum. = 14

## Slide 25: Absolute Memory Addressing
// Load accumulator with value at memory
// address 1000
LDA 1000
  Each addressable memory location is 8-bits
10
20
30
1000
1001
1002
60
1003
Accum. = 30

## Slide 26: Example
Example assembly code to compute C = A + B
// Load accumulator with A from address 1000
LDA 1000
// Add value of B from address 1001 to accumulator
ADC 1001
// Store contents of accumulator in C location 1002
STA 1002

## Slide 27: Absolute Indexed Addressing
  // Load accumulator with value at memory
  // address 1000 + value of X index register
  LDX #2
  LDA 1000,X
  Accumulator gets value of 10
  from address 1000+2 = 1002
  Accum. = Memory[1000 + 2] = 10
10
20
30
1000
1001
1002
60
1003
Accum. = 10
X = 2

## Slide 28: Indexing Array Elements
If we increment the X-index register we can use absolute indexing to step through the elements of an array
LDX instruction increments the value of the X-index register

## Slide 29: Sum of Array Elements
LDA #0
LDX #0
ADC 1000,X
INX
ADC 1000,X
INX
ADC 1000,X
STA 1003
3 8-bit integers in memory locations 1000-1002.
Store sum in location 1003.
Memory
10
20
30
1000
1001
1002
60
1003
Computer Organization

## Slide 30: Exercise
LDA #0
LDX #0
ADC 1000,X
INX
ADC 1000,X
INX
ADC 1000,X
STA 1003
Show contents of X-index and accumulator after each
instruction is executed.
Memory
10
20
30
1000
1001
1002
60
1003

## Slide 31: Exercise: Solution
LDA #0
LDX #0
ADC 1000,X
INX
ADC 1000,X
INX
ADC 1000,X
STA 1003
A = 0 X = ?
A = 0 X = 0
A = 30 X = 0
A = 30 X = 1
A = 50 X = 1
A = 50 X = 2
A = 60 X = 2
A = 60 X = 2
Memory
10
20
30
1000
1001
1002
60
1003

## Slide 32: 6502 In Perspective
“The 6502 was much superior to the Intel 8080. I had studied computer architecture as the primary interest of my life. The versatile addressing modes of the 6502 meant more than even if the 8080 had been a 16 bit machine.”
Steve Wozniak
Source: http://www.woz.org/letters/general/81.html

## Slide 33: Too Few Registers
Stack, accumulator, and accumulator + index registers must perform slower memory accesses whenever a program needs to use many different variables at the same time
Example:
  q = sqrt(x*x + y*y + z) / log(a - b)
Computer Organization

## Slide 34: General Purpose Register Machines
GPR machines make no distinction between accumulator and index registers.
Any register may be used to load/store memory and perform arithmetic or comparison operations.

## Slide 35: General Purpose Register Machines
Examples: MIPS R3000, Intel Pentium, Power PC, Sun SPARC
Processor Number of GPR’s
Intel 80386 8
MIPS R3000 31
Power PC G4 32
Not counting floating point or multimedia MMX registers

## Slide 36: GPR Assembly Example
Registers r0 - r7
Introduce 3 operand arithmetic operators
LOAD r0, 15 # r0 = 15
LOAD r1, 10 # r1 = 10
ADD r2, r0, r1 # r2 = r0 + r1
MUL r3, r0, r1 # r3 = r0 * r1

## Slide 37: GPR Exercise
4.11 Assume all registers contain 0, what is the value of R7 after these instructions?
MOV R7, #4
MOV R8, #3
ADD R9, R7, R7
SUB R7, R9, R8
MUL R9, R7, R7
Computer Organization

## Slide 38: GPR Exercise: Solution
4.11 Assume all registers contain 0, what is the value of R7 after these instructions?
MOV R7, #4 R7 = 4
MOV R8, #3 R7 = 4, R8 = 3
ADD R9, R7, R7 R7 = 4, R8 = 3 , R9 = 8
SUB R7, R9, R8 R7 = 8 – 3 = 5, R8 = 3, R9 = 8
MUL R9, R7, R7 R7 = 5, R8 = 3, R9 = 5 * 5 = 25
Register R7 contains 5 after execution of these instructions

## Slide 39: GPR versus Stack
Fast random access to values in registers.
Harder to write optimized compiler since must carefully decide how to allocate registers.
But a well-made compiler can produce faster code if it can keep all or most needed variables in fast registers.
GPR has displaced stack machines.

## Slide 40: GPR Exercise
4.12: Write a GPR assembly program to compute 5 + (3 x 7) – 8. Use any registers R0-R7.

## Slide 41: GPR Exercise: Solution
4.12: Compute: 5 + (3 x 7) – 8
MOV R1, #3 R1 = 3
MOV R2, #7 R1 = 3, R2 = 7
MUL R1, R1, R2 R1 = 21, R2 = 7
MOV R2, #5 R1 = 21, R2 = 5
ADD R1, R1, R2 R1 = 26
MOV R2, #8 R1 = 26, R2 = 8
SUB R1, R1, R2 R1 = 18, R2 = 8
There are other equivalent instruction sequences.

## Slide 42: GPR Exercise
4.13: Write GPR assembly instructions to compute ((10 x 8) + (4 – 7))2.

## Slide 43: GPR Exercise: Solution
4.13: compute ((10 x 8) + (4 – 7))2
MOV R1, #10 R1 = 10
MOV R2, #8 R1 = 10, R2= 8
MUL R1, R1, R2 R1 = 80, R2 = 8
MOV R2, #4 R1 = 80, R2 = 4
MOV R3, #7 R1 = 80, R2 =4, R3 = 7
SUB R2, R2, R3 R1 = 80, R2 = -3, R3 = 7
ADD R1, R1, R2 R1 = 77, R2 = -3, R3 = 7
MUL R1, R1, R1 R1 = 5929, R2 = -3, R3 = 7
Other instruction sequences are possible.