## Slide 1: MIPS Assembly Language Programming
Notes adapted from PPT files accompanying Bob Britton’s text
© 2004 Pearson|Prentice Hall
Updated: 10/01/2010

## Slide 2: Benefits of Studying Assembly Language Programming
Gain insights into writing more efficient code
Understand the behind-the-scenes work done by high-level language compilers
Open new opportunities in the field of embedded processors

## Slide 3: Why MIPS?
Easier to understand than Intel 80x86
Can focus more on methodology of assembly programming
MARS software simulator for MIPS R3000 32-bit RISC processor
Skills learned will benefit learning assembly (if needed) for latest processors

## Slide 4: Current Applications of MIPS
MIPS 32-bit and 64-bit processors are embedded in many electronic devices:
  Broadcom Sentry5 secured network gateway: embedded 200 MHz MIPS 32-bit
  Time Warner cable Pace DC-550 HD Digital Cable set-top box
  Toshiba licensed MIPS R3000A processor in Lexmark Optra laser printer
Source: Press releases at www.mips.com http://www.mips.com/content/PressRoom/PressReleases

## Slide 5: More Familiar MIPS Adopters
Sony PSOne
33 MHz MIPS R3000A
Sony Aibo Robot Dog
200 MHz MIPS
Nintendo 64
100 MHz MIPS R4300i
Sony PS2
295 MHz MIPS R5900 and MIPS R3000 for PsOne compatibility

## Slide 6: Sony PSP
Next-generation hand-held entertainment device
Video games,MP3 audio, MPEG4 video
Two 333 MHz MIPS R4000 processors
Projected U.S. launch in Q1 2005

## Slide 7: History of MIPS
Company founded in 1984 as outgrowth of John Hennessey’s research at Stanford University
MIPS RISC processors were used extensively in workstations produced by Silicon Graphics
MIPS = Microprocessor without Interlocked Pipeline Stages

## Slide 8: MIPS Computer Organization
Functional units
Data path diagram
Control logic
Registers

## Slide 9: Functional Units
Control unit
Register file
Arithmetic Logic Unit (ALU)
Program Counter (PC)
Instruction Register (IR)
Memory access

## Slide 10: DataPath Diagram

## Slide 11: Data buses
The lines in the data path diagram are buses.
A bus is a set of electrical lines capable of transmitting binary values.
The buses in the MIPS R3000 are 32-bits wide.
Thus MIPS bus transmits data in 32-bit chunks.

## Slide 12: Control Unit
The control unit transmits control signals to the various functional units indicating when each should perform a specified operation.
For example, the control unit sends a signal to a multiplexer to select an input signal to be transmitted.
For example, signal when a register should load a value from memory.

## Slide 13: MIPS Register File
A register is an electronic component located inside the processor that holds a value being used in a recent computation.
The processor can access and operate on values in registers much faster than it can do so with values in main memory.

## Slide 14: MIPS Load & Store
As we’ll soon see all MIPS computation instructions only operate on values held in registers.
Typical MIPS instruction sequence:
  Load values into registers from memory
  Perform computation instruction
  Store result to memory

## Slide 15: MIPS Registers
Thirty-two 32-bit registers
24 registers available for programmer use
8 registers are special purpose or reserved
In MIPS assembly a $ precedes the name of a register

## Slide 16: MIPS Registers
The 24 registers available for programmer use are given symbolic names that suggest their purpose according to convention.
  Main program variables
  Local variables inside functions
  Function parameters
  Function return values

## Slide 17: Main Program Registers
8 “Main program registers”
Registers $s0 through $s7 are used to hold program variables that persist after function calls are completed.
For example, use $s0 through $s7 for main program variables

## Slide 18: Local Variable Registers
10 “local variable registers”
Registers $t0 through $t9 are used to hold the local variables of a function.

## Slide 19: Function Parameter Registers
4 “function parameter registers”
Registers $a0 through $a3 are used to pass parameter values into functions.

## Slide 20: Function Return Registers
2 “function return value registers”
Registers $v0 and $v1 are used to return values from function calls.

## Slide 21: Special Purpose Registers
$sp The stack pointer register points to the top of a stack used to dynamically allocate memory while the program runs.
$ra This register is loaded with the return address when invoking a function call.
$fp The frame pointer gives the memory offset where function local variables and parameters are stored.

## Slide 22: Zero Register
Register zero $0 is reserved to always contain the frequently used constant 0.

## Slide 23: A Quick Look at MIPS
The MARS Simulator
MARS text editor
A first MIPS program

## Slide 24: MARS: A MIPS Simulator
Simulator for the MIPS R2000/R3000
MARS - MIPS Assembler and Runtime Simulator
Jointly developed by Pete Sanderson (programming) and Ken Vollmar (details and paperwork).
Available as a free download

## Slide 25: Where to Get MARS?
http://courses.missouristate.edu/KenVollmar/MARS/

## Slide 26: mars tutorials
http://courses.missouristate.edu/KenVollmar/MARS/tutorial.htm

## Slide 27: Run the MARS Editor

## Slide 28: Edit Hello World
# HELLO WORLD
.data
# Symbolic label Hello: data type is ASCII string
Hello: .asciiz "Hello World\n"
.text # Text segment is unused for now.
main: # Start of code section
# Load register $v0 with code 4 for OS print.
li $v0, 4
# Load address $a0 with address of string.
# Label names are case sensitive.
la $a0, Hello
# call operating system to perform print operation
syscall
# END OF PROGRAM - MUST LEAVE ONE BLANK LINE AT END.

## Slide 29: Load Immediate
Loads specified numeric value into the destination register
General format for LI
li <destination_reg>, <number>
Specific example: $v0 = 4
li $v0, 4

## Slide 30: Load Address
Load given memory address into destination register
General format for LA instruction
la <destination_reg>, <addr>
Specific example: $a0 = (hello)
la $a0, Hello

## Slide 31: Case Sensitivity
MIPS assembly language is case sensitive
Mnemonic commands must be expressed in lower case, for example:
  li
  la
  add
  sub

## Slide 32: Mars
Single-step using F7 key
Examine contents of:
  $v0
  $a0
  Memory contents of string shown in hex #s

## Slide 33: Arithmetic Logic Unit (ALU)
The ALU is a digital logic circuit that can perform binary integer arithmetic operations such as add, subtract, multiply, and divide.
The ALU also performs binary logical operations such as AND, OR, NOR, and Exclusive OR.

## Slide 34: Program Counter (PC)
The program counter holds the memory address of the next instruction to be executed.
When a new program is started, the operating system will initialize the PC to the address of the first instruction.

## Slide 35: Fetch-Execute Cycle
The processor accesses the instruction addressed by the program counter.
The current instruction is stored in the instruction register (IR).
Increment the program counter to point to the next instruction.

## Slide 36: Fetch-Execute Cycle
The processor decodes the instruction to determine its opcode and operands.
Optional, fetch operands from memory
The processor executes the instruction.
Memory and/or registers are updated to reflect the result of the instruction.

## Slide 37: Mars Exercise
Assemble the source code for the Hello world program
Single-step through the code by pressing the F7 key
Note how the PC increments by 4 after each instruction
Inspect the memory address where each instruction is stored

## Slide 38: MIPS Instruction Format
All MIPS instructions are 32-bits in length.
MIPS employs a fixed instruction size, which simplifies matters.
The program counter is incremented by 4 after each instruction.
Other processors such as the CISC Intel 80x86 have variable length instructions.

## Slide 39: MIPS Instruction Set
Arithmetic, Logic, and Shifting Instructions
Load and Store Instructions
Conditional Branch Instructions
Function Call Instructions

## Slide 40: Simplicity Favors Regularity
All arithmetic instructions have 3 operands
Operand order is fixed (destination first) C code: A = B + C;
# Let A = $s0, B = $s1, and C = $s2. add $s0, $s1, $s2

## Slide 41: Addition Example
# $t0 = 10 (base 10)
li $t0, 10
# $t1 = 20 (base 10)
li $t1, 20
# $t2 = $t0 + $t1
add $t2, $t0, $t1

## Slide 42: Use mars to Trace Addition
Examine register contents
$t0 = 0x0000000A = 10 (base 10)
$t1 = 0x00000014 = 20 (base 10)
$t2 = 0x0000001E = 30 (base 10)

## Slide 43: Subtraction Example
# $t0 = 10
li $t0, 10
# $t1 = 20
li $t1, 20
# $t2 = $t0 - $t1
sub $t2, $t0, $t1

## Slide 44: Use mars to Trace Subtraction
Examine register contents
$t0 = 0x0000000A = 10 (base 10)
$t1 = 0x00000014 = 20 (base 10)
$t2 = 0xFFFFFFF6 = -10 (base 10)
MARS shows 32-bit register and memory contents as a string of 8 hexadecimal digits

## Slide 45: Negative Integers
# Result of 10 – 20 = -10
$t2 = 0xFFFFFFF6
Can you determine how the MIPS processor represents negative integers such as -10?

## Slide 46: Programming Exercise
Compute (9 + 16) – (3 + 22)
Use two or more of the MIPS registers $t0, $t1, ...$t7 with the
li, add, and sub instructions.
You can do this using as few as two registers or as many as seven.

## Slide 47: Smaller is Faster
MIPS provides only 32 registers.
Many more registers would increase clock cycle time due to increased distance.
Large programs will use more data than can be held in 32 or even more registers.
Data is held in memory until needed for processing when required values are copied into faster accessible processor registers.

## Slide 48: Add Instruction
Pseudo code for an addition statement.
$t0 = $t1 + $t2;
Convert pseudo code statement into MIPS assembly language statement.
# Add contents of registers $t1 and $t2 store sum in register $t0.
add $t0, $t1, $t2

## Slide 49: Add Instruction Immediate Version
Pseudo code for an addition statement.
$t0 = $t1 + 15;
Convert pseudo code statement into MIPS assembly language statement.
# “i” signifies immediate format. The integer constant is a 16-bit value.
addi $t0, $t1, 15

## Slide 50: Subtract Instruction
Pseudo code for a subtraction statement.
$t0 = $t1 - $t2;
Convert pseudo code statement into MIPS assembly language statement.
sub $t0, $t1, $t2

## Slide 51: Subtract Instruction Immediate Version
Not provided by MIPS R2000/3000
Use addi with a negative value
# decrement value of $t0 by 1.
addi $t0, $t0, -1

## Slide 52: Immediate Values are 16-Bits
Immediate mode instructions can specify an integer constant that uses up to 16-bits
Since the 32-bit MIPS instruction must also encode the op-code (or command) and the register numbers, only 16-bits are left to encode the immediate constant

## Slide 53: Logical Bit-wise AND
Sets a bit 1 only if the corresponding pair of source bits are both 1; else the result bit is 0.
0 1
0 0 0
1 0 1
AND

## Slide 54: Exercise
Compute bitwise AND
  11001
  01011
  01001
Compute bitwise AND
  10110 10110
  11100 01100
  10100 00100
Intuitively what is the effect of bitwise AND?

## Slide 55: Logical Bit-wise AND Instruction
Pseudo code for a logical bit-wise AND statement.
// & is bit-wise AND using C or C++ notation
$t0 = $t1 & $t2;
Convert pseudo code statement into MIPS assembly language statement.
and $t0, $t1, $t2

## Slide 56: Bit-wise AND Example
Extract the least significant bit of $t1
Set low-order bit to 1 in $t2
What does the result tell us about $t1?
$t1 = 10101010 10101010 10101010 10101011
$t2 = 00000000 00000000 00000000 00000001
$t0 = 00000000 00000000 00000000 00000001
and $t0, $t1, $t2

## Slide 57: Logical Bit-wise AND -Immediate Format
Pseudo code for a logical bit-wise AND statement.
// & is bit-wise AND using C or C++ notation
$t0 = $t1 & 0xFF;
Convert pseudo code into MIPS assembly language
# “i” indicates immediate mode format
andi $t0, $t1, 0xFF

## Slide 58: Bit-wise AND Example
Extract the 8 least significant bits of $t1
Constant 0xFF has 8 low order bits set to 1
$t1 = 10101010 10101010 10101010 10101010
0xFF = 00000000 00000000 00000000 11111111
$t0 = 00000000 00000000 00000000 10101010
and $t0, $t1, 0xFF
Gray shaded bits indicate assumed 0’s since the immediate constant is only 16-bits

## Slide 59: Exercise
Given the 16-bits
  1100 1101 0010 1101
  And xxxx xxxx xxxx xxxx
  ----------------------------
  1100 000 0000 1101
  What are the 16-bits to mask off the four low and high order bits? Express the mask in hex.

## Slide 60: Logical Bit-wise OR
Sets a bit 1 if either of the corresponding pair of source bits is 1; else result bit is 0.
0 1
0 0 1
1 1 1
OR

## Slide 61: Exercise
Compute bitwise OR
  11001
  01011
  11011
Compute bitwise OR
  00111
  10001
  10111
Intuitively what is the effect of bitwise OR?

## Slide 62: Logical Bit-wise OR Instruction
Pseudo code for a logical bit-wise OR statement.
// | is bit-wise OR using C or C++ notation
$t0 = $t0 | $t1;
Convert pseudo code statement into MIPS assembly language statement.
or $t0, $t0, $t1

## Slide 63: Bit-Wise OR Example
Set the two low order bits of $t0 to 1 but leave all other bits of $t0 unchanged
$t0 = 10101010 10101010 10101010 10101010
$t1 = 00000000 00000000 00000000 00000011
$t0 = 10101010 10101010 10101010 10101011
or $t0, $t0, $t1

## Slide 64: Logical Bit-wise OR Instruction Immediate Format
Pseudo code for a logical bit-wise OR statement.
// | is bit-wise OR using C or C++ notation
$t0 = $t0 | 0xFF;
Convert pseudo code statement into MIPS assembly language statement.
ori $t0, $t0, 0xFF

## Slide 65: Bit-Wise OR Example
Set least significant 8 bits of $t0 to 1
$t0 = 10101010 10101010 10101010 10101010
0xFF = 00000000 00000000 00000000 11111111
$t0 = 10101010 10101010 10101010 11111111
ori $t0, $t0, 0xFF
Gray shaded bits indicate assumed 0’s since the immediate constant is only 16-bits

## Slide 66: Load Immediate Value
The immediate form of logical OR can also be used to load an immediate value into a register
0xFF = 00000000 00000000 00000000 11111111
$zero = 00000000 00000000 00000000 00000000
$t0 = 00000000 00000000 00000000 11111111
ori $t0, $zero, 0xFF
Gray shaded bits indicate assumed 0’s since the immediate constant is only 16-bits

## Slide 67: Load Immediate Value
The immediate form of logical OR can also be used to load an immediate value into a register
These two instructions are equivalent.
ori $t0, $zero, 0xFF
li $t0, 0xFF
The li is a pseudo-instruction

## Slide 68: Programming Exercise
Find a way to represent sets of fruit.
{ apple, banana, grape, lemon,
mango, orange, peach, strawberry }
Let set A = { apple, banana, lemon }
set B = { apple, mango, peach }
A union B = { apple, banana, lemon, mango, peach }
A intersect B = { apple }

## Slide 69: Solution
Assign a bit to represent each fruit
        SET A SET B
1 apple apple apple
2 banana banana
4 grape
8 lemon lemon
16 mango mango
32 orange
64 peach peach
128 strawberry
11 = 0x0B 81 = 0x51

## Slide 70: Solution
# Set bit pattern of 1’s for members of set A
li $t0, 0x0B
# Set bit pattern of 1’s for members of set B
li $t1, 0x51
# Use bitwise AND for intersection of sets
and $t2, $t0, $t1
# Use bitwise OR for union of sets
or $t3, $t0, $t1

## Slide 71: Programming Exercise
Can we add one more instruction that can tell us whether or not apple is a member of the intersection of sets A and B?
Can we add a second instruction that can tell us whether or not strawberry is a member of the union of sets A, B?
Result of operation != 0 means YES

## Slide 72: Solution
li $t0,
li $t1,
and $t2, $t0, $t1
or $t3, $t0, $t1
# Mask off bit for apple
andi $t2, $t2, 0x01
# Mask off bit for strawberry
andi $t3, $t3, 0x80

## Slide 73: Logical Bit-wise NOT
Inverts all bits
0 becomes 1 1010
1 becomes 0 NOT
0101

## Slide 74: Logical Bit-wise NOT
not $t1, $t0
Set $t1 to be the negation of $t0
Let
$t0 = 00000000 00000000 00000000 11111111
$t1 = 11111111 11111111 11111111 00000000

## Slide 75: Logical Bit-wise NOR
Computes the negation of OR.
0 1
0 0 1
1 1 1
OR
0 1
0 1 0
1 0 0
NOR

## Slide 76: Logical Bit-wise NOR
Pseudo code for a logical bit-wise NOR statement.
// ~ is bit-wise negation in C or C++
$t2 = ~($t0 | $t1);
Convert pseudo code statement into MIPS assembly language statement.
nor $t2, $t0, $t1

## Slide 77: Logical Bit-wise NOR
nor $t2, $t0, $t1
Let
$t0 = 00000000 00000000 00000000 11111111
$t1 = 00000000 00000000 11111111 11111111
$t2 = 11111111 11111111 00000000 00000000
MIPS R3000 does not provide a NAND instruction

## Slide 78: Logical Bit-wise Exclusive OR
Exclusive-OR abbreviated XOR sets a bit 1 only if the corresponding pair of source bits differ; else the result bit is 0.
0 1
0 0 1
1 1 0
XOR

## Slide 79: Exercise
Compute bitwise NOR
  11001
  01011
  00100
Compute bitwise NOR
  00110
  10101
  01000

## Slide 80: Logical Bit-wise XOR
Pseudo code for a logical bit-wise Exclusive-OR statement.
// ^ is bit-wise XOR using C or C++ notation
$t2 = $t0 ^ $t1;
Convert pseudo code statement into MIPS assembly language statement.
xor $t2, $t0, $t1

## Slide 81: Logical Bit-wise XOR
xor $t2, $t0, $t1
Let
$t0 = 00000000 11111111 00000000 11111111
$t1 = 00000000 11111111 11111111 00000000
$t2 = 00000000 00000000 11111111 11111111

## Slide 82: Logical Bit-wise XOR Immediate Format
Pseudo code for a logical bit-wise Exclusive-OR statement.
// ^ is bit-wise XOR using C or C++ notation
$t2 = $t0 ^ 0xF0F0;
Convert pseudo code statement into MIPS assembly language statement.
xori $t2, $t0, 0xF0F0

## Slide 83: Logical Bit-wise XOR Immediate Format
xori $t2, $t0, 0xF0F0
0xF0F0 = 0000 0000 0000 0000 1111 0000 1111 0000
$t0 = 0000 0000 1111 1111 1111 1111 0000 0000
$t2 = 0000 0000 1111 1111 0000 1111 1111 0000
Gray shaded bits indicate assumed 0’s since the immediate constant is only 16-bits

## Slide 84: Exercise
Compute bitwise XOR
  11001
  01011
  10010
Compute bitwise XOR
  10010
  01011
  11001
Intuitively what does XOR do?
Note that being able to detect differences is useful in detecting errors when transmitting data

## Slide 85: Useful Property of XOR
Compute bitwise XOR
  00110
  10101  Apply XOR bit pattern
  10011
Compute bitwise XOR
10011
10101  Apply XOR bit pattern AGAIN
00110  Get back the original bit pattern

## Slide 86: Side Note: XOR Animation
This property of XOR can be used to produce a simple animated graphics effect, e.g. moving cursors or rubber band rectangles
XOR the bit pattern of the moving image once to make the shape appear
XOR the bit pattern again to erase it leaving the background image intact

## Slide 87: Declaring 32-bit Constants
Overcome the limitation of 16-bit immediate constants by declaring 32-bit constants in memory
Then load the 32-bit constant value from its memory location into a register

## Slide 88: Declaring 32-bit Constants
.data
# Declare 32-bit constant to
# represent IEEE single precision
# floating point value -2000
FValue: .word 0xC4FA0000
main:
# Load 32-bit word from
# labeled memory location
# into register $t0
lw $t0, FValue

## Slide 89: Load Word Instruction
Load a 32-bit word value from the given memory address into destination register
lw <destination_register>, <address>
Use a symbolic label name so the assembler figures out the actual address
lw $t0, FValue

## Slide 90: masking
A common use of logical operations is isolating, or "masking" parts of words. Just like a mask covers your face and lets your eyes show through, a bit mask lets some bits show through, and hides others. Think of one operand as the "data" and the other as the "mask". For the different operations:
AND - for every 1 in the mask, the data bit shows. For every 0 in the mask, the result is 0, the data bit is hidden.
OR - for every 0 in the mask, the data bit shows. For every 1 in the mask, the result is 1, hiding the data bit.
XOR - for every 0 in the mask, the data bit is unchanged. For every 1 in the mask, the data bit is reversed. If you XOR twice, the original value is restored. This property is often used in graphic programming to show moving objects. If something is put into an image with XOR, another XOR will remove it. If you see something that changes colors to contrast with whatever background there is, XOR operations are being used.

## Slide 91: Programming Assignment
Set $t0 = 0xC4FA0000, which is the hexadecimal representation for the 32-bit IEEE single precision value -2000
Declare two 32-bit word values in memory for 0xC4FA0000 and the mask to isolate the value of the sign bit
Use bitwise logical AND to determine the value of the sign bit

## Slide 92: Programming Assignment
Load $t0 with an arbitrary IEEE single precision value such as 0xC4FA0000, which is the hexadecimal representation for -2000
Write a sequence of bitwise MIPS assembly instructions to invert the sign bit in $t0
The code should work with any 32-bit IEEE value positive or negative

## Slide 93: Programming Assignment
Example: Invert the high-order bit
1100 0100 1111 1010 0000 0000 0000 0000
0100 0100 1111 1010 0000 0000 0000 0000

## Slide 94: Programming Assignment
Test your code using one positive and one negative floating point value
Check your results using the IEEE floating point conversion Java applet at
http://babbage.cs.qc.cuny.edu/IEEE-754.old/32bit.html

## Slide 95: Logical Bit-wise Shift Left
Pseudo code for a bit-wise shift left statement.
// << is bit-wise shift left in C or C++ notation
$t0 = $t0 << 2;
# Shift bits two places to left same as multiply by 4.
# mnemonic is SLL expressed in lower case
sll $t0, $t0, 2

## Slide 96: Logical Bit-wise Shift Left
sll $t0, $t0, 2
The effect is a very fast multiply by a power of two.
Shifts in two 0 bits at the low-order end.
The two high-order bits are pushed off the left end.
$t0 = 00000000 00000000 00000000 11111111
$t0 = 00000000 00000000 00000011 11111100

## Slide 97: Example: Shift Left Logical
Let $t0 = 0xFFFFFFE8 = -24
$t0 = 1111 1111 1111 1111 1111 1111 1110 1000
sll $t1, $t0, 1
$t1 = 1111 1111 1111 1111 1111 1111 1101 0000 = -48

## Slide 98: Logical Bit-wise Shift Right
Pseudo code for a bit-wise shift right statement.
// << is bit-wise shift right in C or C++ notation
$t0 = $t0 >> 2;
Convert pseudo code statement into MIPS assembly language statement.
# Shift bits two places to right same as divide by 4.
srl $t0, $t0, 2

## Slide 99: Logical Bit-wise Shift Right
srl $t0, $t0, 2
The effect is a very fast division by a power of two.
Shift in 0 bits at high-order end and shift existing bits to right.
Low-order bits are lost as they are pushed off the far right end.
$t0 = 00000000 00000000 00000000 11111111
$t0 = 00000000 00000000 00000000 00111111

## Slide 100: Arithmetic Shift Right
Negative values are not maintained since logical shift right inserts 0 bits at the high-order end
MIPS provides the Arithmetic Shift Right that inserts a new bit at the high-order end that preserves the original sign bit

## Slide 101: Example 1: sra
Let $t0 = 0xFFFFFFE8 = -24
sra $t1, $t0, 1
$t1 = 0xFFFFFFF4
$t0 = 1111 1111 1111 1111 1111 1111 1110 1000
$t1 = 1111 1111 1111 1111 1111 1111 1111 0100 = -12

## Slide 102: Example 1 continued...
Let $t0 = 0xFFFFFFE8 = -24
sra $t2, $t0, 2
$t2 = 0xFFFFFFFA
$t0 = 1111 1111 1111 1111 1111 1111 1110 1000
$t2 = 1111 1111 1111 1111 1111 1111 1111 1010 = -6

## Slide 103: Example 1 continued.
Let $t0 = 0xFFFFFFE8 = -24
sra $t3, $t0, 3
$t3 = 0xFFFFFFFD
$t0 = 1111 1111 1111 1111 1111 1111 1110 1000
$t3 = 1111 1111 1111 1111 1111 1111 1111 1101 = -3

## Slide 104: Example 2: sra
Let $t0 = 0xFFFFFFEB = -21
sra $t1, $t0, 1
$t1 = 0xFFFFFFF5
$t0 = 1111 1111 1111 1111 1111 1111 1110 1011
$t1 = 1111 1111 1111 1111 1111 1111 1111 0101 = -11
-21 / 2 = -11? This is a “mathematical” result
-11 x 2 = -22 + 1 = -21 (Add remainder of 1)

## Slide 105: Example 2: continued.
Let $t0 = 0xFFFFFFEB = -21
sra $t2, $t0, 2
$t2 = 0xFFFFFFFA
$t0 = 1111 1111 1111 1111 1111 1111 1110 1011
$t1 = 1111 1111 1111 1111 1111 1111 1111 1010 = -6
-21 / 4 = -6? When there is an uneven division via a sra, then truncate in the negative direction!

## Slide 106: Example 3: sra
-38 = 111111111111111111111111 1101 1010
divide by 4 we would sra by 2 bit positions
gives
111111111111111111111111 1111 0110, which is -10
It makes mathematicians happy, because it agrees with the remainder of +2, that is, -10*4 +2 = -38. The answer has been truncated (rounded down) in the negative direction.
Reference: http://www.compapp.dcu.ie/~ray/CA225b.html

## Slide 107: Exercises
Assume binary numbers are 8-bit two’s complement
Logical shift left by 3 bits
  00001011
Logical shift left by 4 bits
  00001011
Logical shift right by 2 bits
  11001001
Arithmetic shift right by 3 bits
  11001001
Show the base 10 integer value before & after each shift.
Which of these results in a potentially undesirable change in sign?

## Slide 108: Programming Exercise
Let $t0 = 0xC4FA0000, which is the hexadecimal representation for IEEE single precision value -2000
Use bit-wise AND to mask out the 8 bits of the exponent (bits 23-30 out of bits 0..31)
Shift 8-bits of exponent to the right
Subtract bias of 127
What is the value of the unbiased exponent?

## Slide 109: Programming Exercise
Let $t0 = 0xC4FA0000
1100 0100 1111 1010 0000 0000 0000 0000
Let $t1 = mask off the 8-bits of the exponent
0100 0100 1000 0000 0000 0000 0000 0000
Let $t2 = shift right until rightmost bit of exponent occupies the low-order bit 0 position
0000 0000 0000 0000 0000 0000 1000 1001

## Slide 110: Programming Exercise
$t2 = Result after shifting bits of the exponent
0000 0000 0000 0000 0000 0000 1000 1001
Let $t3 = $t2 - 127
Subtract bias value of 127 (base 10)
Final result is the actual value of the power of 2 exponent

## Slide 111: EXTRA

## Slide 112: Programming Exercise
Given an arbitrary 32-bit IEEE single precision floating point number
Use bitwise logical AND to examine the contents of the sign bit
  A result of 0 indicates a positive value
  A non-zero result indicates a negative value

## Slide 113: Programming Exercise
Set $t0 = 0xC4FA, which is the hexadecimal representation for high-order 16-bits of the IEEE single precision value -2000
The actual 32-bit encoding for -2000 is 0xC4FA0000
This simplified example discards the least significant 16-bits of the mantissa so that the bit mask can be expressed as a 16-bit immediate mode constant

## Slide 114: IEEE Single Precision
IEEE single precision floating point value is encoded using 32-bits
The high order bit (index 31) represents the sign
1
8 bits
23 bits
mantissa
exponent
sign bit
0
22
31

## Slide 115: Simplified Example
For this example we arbitrarily truncate the mantissa to its 7 most significant bits
Later on we’ll see more instructions that will enable us to work with the full 32-bit encoded value
1
8 bits
7 bits
Truncated Mantissa
exponent
sign bit
0
6
16
This simplification is for example only

## Slide 116: Programming Exercise
Determine the hexadecimal value that represents the 16-bit mask
Use bit-wise andi to extract the high-order or sign bit (Assume to be in position 16 for now)
  Mask will have a single 1 bit in the high order position
  Express the mask as a 16-bit immediate constant
Leave the result in register $t1

## Slide 117: Programming Exercise
Set $t0 = 0x44FA, which is the hexadecimal representation for the high-order 16-bits of IEEE single precision value +2000
Repeat the previous exercise to examine the contents of the sign bit
Leave the result in register $t1

## Slide 118: Programming Exercise
A final value of 0x0000 indicates a positive sign
A non-zero value of 0x8000 indicates a negative sign (1 in the sign bit position)