## Slide 1: Branching & Loops
Updated 7/9/2013

## Slide 2: Branching & Loops
Making decisions and repeating instructions
  If-then
  If-then-else
  while loop
  for loop
  switch statement

## Slide 3: Branch if Equal
# Go to LABEL if value in
# $s0 equals value in $s1.
beq $s0, $s1, LABEL
See: page 105 of H&P: Computer Organization and Design

## Slide 4: Labels
Sections of code may be given labels which the assembler will interpret as the address of the instruction following the label.
Use of labels saves the programmer from having to calculate the address of the branch target instruction.
Tip: Use meaningful label names.

## Slide 5: Branch if Equal
# high-level language pseudo code
if ($t0 != $t1)
$t0 = $t0 – 1;
# Equivalent MIPS assembly code
beq $t0, $t1, endif
# then $t0 = $t0 - 1
addi $t0, $t0, -1
endif:

## Slide 6: Branch-Friendly Pseudo Code
# high-level language pseudo code
if ($t0 != $t1)
$t0 = $t0 – 1;
# MIPS branch-friendly pseudo code
if ($t0 == $t1)
goto endif;
$t0 = $t0 – 1;
endif:

## Slide 7: Branch if Not Equal
# Go to LABEL if value in
# $s0 not equal value in $s1.
bne $s0, $s1, LABEL
See: page 123 of H&P: Computer Organization and Design

## Slide 8: Branch if Not Equal
# high-level language pseudo code
if ($t0 == $t1)
$t0 = $t0 – 1;
# MIPS branch-friendly pseudo code
if ($t0 != $t1)
goto endif;
$t0 = $t0 – 1;
endif:

## Slide 9: Branch if Not Equal
# MIPS branch-friendly pseudo code
if ($t0 != $t1)
goto endif;
$t0 = $t0 – 1;
endif:
# Equivalent MIPS assembly code
bne $t0, $t1, endif
# then $t0 = $t0 - 1
addi $t0, $t0, -1
endif:

## Slide 10: Example If Statement
# high-level language pseudo code
if ( $s3 != $s4 )
$s0 = $s1 + $s2;
# MIPS branch-friendly pseudo code
if( $s3 == $s4 )
goto endif;
$s0 = $s1 + $s2;
endif:
See: page 123 of H&P: Computer Organization and Design

## Slide 11: Example If Statement
# MIPS branch-friendly pseudo code
if( $s3 == $s4 )
goto endif;
$s0 = $s1 + $s2;
endif:
# Equivalent MIPS assembly code
beq $s3, $s4, endif
add $s0, $s1, $s2 # f = g + h
endif:
remainder of the program...

## Slide 12: Exercise
Write the branch-friendly pseudo code
if ($t0 == $t1)
{
$t0 += 1;
$s0 += $t0;
}

## Slide 13: Exercise
Write the equivalent MIPS assembly code
if ($t0 != $t1)
goto END_IF;
$t0 += 1;
$s0 += $t0;
END_IF:

## Slide 14: Exercise: Solution
bne $t0, $t1, END_IF
# $t0 = $t0 + 1
addi $t0, $t0, 1
# $s0 = $s0 + $t0
add $s0, $s0, $t0
END_IF:

## Slide 15: Example
Write the equivalent MIPS assembly code
if ($t0 == 25)
{
$t0 = $t0 + 10;
}

## Slide 16: Example
First, the branch-friendly pseudo code
if ($t0 != 25)
goto END_IF
$t0 = $t0 + 10;
END_IF:

## Slide 17: Example
MIPS assembly code
li $t1, 25
bne $t0, $t1, END_IF
addi $t0, $t0, 10
END_IF:
# remainder of the program…

## Slide 18: Branch if Less Than or Equal
# Go to LABEL if value in
# $s0 is less than or equal
# to value in $s1.
ble $s0, $s1, LABEL

## Slide 19: Branch if Less Than or Equal
# high-level language pseudo code
if ($t0 > $t1)
$t0 = $t0 – 1;
# MIPS branch-friendly pseudo code
if ($t0 <= $t1)
goto endif;
$t0 = $t0 – 1;
endif:

## Slide 20: Branch if Less Than or Equal
# MIPS branch-friendly pseudo code
if ($t0 <= $t1)
goto endif;
$t0 = $t0 – 1;
endif:
# Equivalent MIPS assembly code
ble $t0, $t1, endif
# then $t0 = $t0 - 1
addi $t0, $t0, -1
endif:

## Slide 21: Branch if Greater Than or Equal
# MIPS branch-friendly pseudo code
if ($t0 >= $t1)
goto endif;
$t0 = $t0 – 1;
endif:
# Equivalent MIPS assembly code
bge $t0, $t1, endif
# then $t0 = $t0 - 1
addi $t0, $t0, -1
endif:

## Slide 22: Branch if Less Than
# MIPS branch-friendly pseudo code
if ($t0 < $t1)
goto endif;
$t0 = $t0 – 1;
endif:
# Equivalent MIPS assembly code
blt $t0, $t1, endif
# then $t0 = $t0 - 1
addi $t0, $t0, -1
endif:

## Slide 23: Branch if Greater Than
# MIPS branch-friendly pseudo code
if ($t0 > $t1)
goto endif;
$t0 = $t0 – 1;
endif:
# Equivalent MIPS assembly code
bgt $t0, $t1, endif
# then $t0 = $t0 - 1
addi $t0, $t0, -1
endif:

## Slide 24: Comparisons & Branch
Pseudo Code MIPS instruction
  if ($t0 == $t1) goto beq $t0, $t1, label
  if ($t0 != $t1) goto bne $t0, $t1, label
  if ($t0 < $t1) goto blt $t0, $t1, label
  if ($t0 > $t1) goto bgt $t0, $t1, label
  if ($t0 <= $t1) goto ble $t0, $t1, label
  if ($t0 >= $t1) goto bge $t0, $t1, label

## Slide 25: Exercises
Write branch-friendly pseudo code and MIPS assembly for each:
if($t0 > $t1)
$t0 = $t0 + 1;
if($t0 <= $t1)
$t0 = $t0 + 1;

## Slide 26: Comparisons with Zero
Branch comparisons will frequently be made with zero
  if (X == 0)
  if (X != 0)
  if (X > 0)
  if (X < 0)
  if (X >= 0)
  if (X <= 0)

## Slide 27: Comparisons with Zero
Pseudo Code MIPS instruction
  if ($t0 == 0) goto beqz $t0, label
  if ($t0 != 0) goto bnez $t0, label
  if ($t0 > 0) goto bgtz $t0, label
  if ($t0 < 0) goto bltz $t0, label
  if ($t0 >= 0) goto bgez $t0, label
  if (X <= 0) goto blez $t0, label

## Slide 28: Branch if Equal to Zero
# MIPS branch-friendly pseudo code
if ($t0 == 0) goto endif;
$t0 = $t0 – 1;
endif:
# Equivalent MIPS assembly code
beqz $t0, endif
# else $t0 = $t0 - 1
addi $t0, $t0, -1
endif:

## Slide 29: Branch if Not Equal to Zero
# MIPS branch-friendly pseudo code
if ($t0 != 0) goto endif;
$t0 = $t0 – 1;
endif:
# Equivalent MIPS assembly code
bnez $t0, endif
# then $t0 = $t0 - 1
addi $t0, $t0, -1
endif:

## Slide 30: Exercises
Write branch-friendly pseudo code and MIPS assembly for each:
if($t0 >= 0)
$t0 = $t0 + 1;
if($t0 < 0)
$t0 = $t0 + 1;

## Slide 31: Compound Boolean Expressions
Using the aforementioned compare & branch instructions, how might we implement this C / C++ statement?
if($t0 > $t1 && $t0 < $t2)
$t3 = $t3 + 1;

## Slide 32: Compound Boolean Expressions
C / C++ code
if($t0 > $t1 && $t0 < $t2)
$t3 = $t3 + 1;
Branch-friendly code
if($t0 <= $t1 || $t0 >= $t2) goto next;
$t3 = $t3 + 1;
next:
Apply DeMorgan’s Law to invert the compound Boolean expression

## Slide 33: Compound Boolean Expressions
Branch-friendly pseudo code
if($t0 <= $t1 || $t0 >= $t2) goto next;
$t3 = $t3 + 1;
next:
ble $t0, $t1, next
bge $t0, $t2, next
addi $t3, $t3, 1
next:

## Slide 34: Exercises
Write branch-friendly pseudo code and MIPS assembly for:
if($t0 >= 0 && $t0 <= $t1)
$t0 = $t0 + 1;

## Slide 35: Test and Set Instructions
Perform a comparison of values in two source registers and set the Boolean result 0 or 1 into the destination register
Example:
seq $dest, $src1, $src2
Sets $dest to 1 (true) if $src1 == $src2;
to 0 (false) otherwise.

## Slide 36: Test & Set Instructions
Pseudo Code MIPS instruction
  $t0 = ($s0 == $s1) seq $t0, $s0, $s1
  $t0 = ($s0 != $s1) sne $t0, $s0, $s1
  $t0 = ($s0 > $s1) sgt $t0, $s0, $s1
  $t0 = ($s0 < $s1) slt $t0, $s0, $s1
  $t0 = ($s0 >= $s1) sge $t0, $s0, $s1
  $t0 = ($s0 <= $s1) sle $t0, $s0, $s1

## Slide 37: Example
Evaluate this Boolean expression so that the result 0 (false) or 1 (true) is left in $t3.
$t3 = ($s0 != $s1) && ($s0 > $s2)
sne $t0, $s0, $s1 # $t0 = ($s0 != $s1)
sgt $t1, $s0, $s2 # $t1 = ($s0 > $s2)
and $t3, $t0, $t1 # $t3 = $t0 and $t1

## Slide 38: Exercise
Use test and set instructions along with the boolean and/or instructions to compute the following Boolean expression.
Leave the result 0 (false) or 1 (true) in $t0.
($s0 >= $s1 || $s0 <= $s2) && $s1 > $s3

## Slide 39: Exercise: Solution
($s0 >= $s1 || $s0 <= $s2) && $s1 > $s3
sge $t0, $s0, $s1
sle $t1, $s0, $s2
or $t0, $t0, $t1
sgt $t1, $s1, $s3
and $t0, $t0, $t1

## Slide 40: Exercise
Given this “C / C++” code
if($t0 >= $t1 || $t0 <= $t2)
$t3 = $t3 + 1;
Write the equivalent MIPS code using the test-and-set instructons, and/or, and one of the branch-zero instructions

## Slide 41: Exercise: Solution
Note: If we use the test-and-set instructions to obtain a Boolean 0 or 1 that represents the result of the original Boolean expression, we do NOT need to negate the expression as we did with the compare-branch instructions
MIPS Assembly code
sge $s0, $t0, $t1 # $s0 = ($t0 >= $t1)
sle $s1, $t0, $t2 # $s1 = ($t0 <= $t2)
or $s0, $s0, $s1 # $s0 = $s0 || $s1
beqz $s0, next # branch if 0 (false)
addi $t3, $t3, 1
next:

## Slide 42: Programming Exercise
Write a MIPS assembly program to read an integer from the keyboard and print the message “Between 1 and 10” if the value entered is between 1 and 10, inclusive.
No output is displayed otherwise.

## Slide 43: Unconditional Branch
Branch to instruction immediately following the specified symbolic label
This is the MIPS “Goto” statement
b LABEL

## Slide 44: Unconditional Branch
Branch to instruction immediately following the specified symbolic label
Label gives a 16-bit +/- displacement from the current instruction
b LABEL

## Slide 45: Unconditional Jump
Jump to instruction immediately following the specified symbolic label
Label gives a 26-bit +/- displacement from the current instruction
j LABEL

## Slide 46: Example if-then-else
# High-level language pseudo code
if ($s3 == $s4)
$s0 = $s1 + $s2;
else
$s0 = $s1 - $s2;
# MIPS branch-friendly pseudo code
if ($s3 != $s4) goto ELSE;
$s0 = $s1 + $s2;
goto END_ELSE; # Acts like “break” in a switch
ELSE:
$s0 = $s1 - $s2
END_ELSE:

## Slide 47: Example If-then-else
# pseudo code # MIPS Assembly
if($s3 != $s4)
goto ELSE; bne $s3, $s4, ELSE
$s0 = $s1 + $s2; add $s0, $s1, $s2
goto END_ELSE; b END_ELSE
ELSE: ELSE:
$s0 = $s1 - $s2; sub $s0, $s1, $s2
END_ELSE: END_ELSE:
See: page 124-125 of H&P: Computer Organization and Design

## Slide 48: Exercise
# High-level language pseudo code
if ($t0 >= 0)
{
$s0 += 1;
$s1 += $s0;
}
else
{
$s0 -= 1;
$s2 += $s0;
}

## Slide 49: Exercise – Part 1
Write the MIPS branch-friendly pseudo code for this if-then-else statement.
# High-level language pseudo code
if ($t0 >= 0)
{
$s0 += 1;
$s1 += $s0;
}
else
{
$s0 -= 1;
$s2 += $s0;
}

## Slide 50: Exercise – Part 2
Write the equivalent MIPS assembly code
if ($t0 < 0) goto ELSE;
$s0 += 1;
$s1 += $s0;
goto END_ELSE;
ELSE:
$s0 -= 1;
$s2 += $s0;
END_ELSE

## Slide 51: Exercise
Write MIPS assembly code for:
if ($t0 == 0)
$t0 = $t0 + 3;
else if($t0 == 1)
$t0 = $t0 + 2;
else
$t0 = $t0 + 1;

## Slide 52: Exercise: Solution
bnez $t0, else1
addi $t0, $t0, 3
b endif
else1:
li $t2, 1 # must load constant 1 in a register
bne $t0, $t2, else2
addi $t0, $t0, 2
b endif
else2:
$t0 = $t0 + 1;
endif:

## Slide 53: Exercise
Write MIPS code for this C/C++/Java…
if ($t0 > 0)
{
if ($t0 < $t1)
$t0 += 1;
else
$t0 += 2;
}

## Slide 54: Loops
Use test-and-set or compare-and-branch instructions to test the loop Boolean condition.
Pre-test loop: branch test at front of loop.
Post-test loop: branch test at end of loop.

## Slide 55: Example Do-While Loop
# C++ do-while loop
int i = 0;
do
{
i = i + 1;
}
while(i < 10);
# Branch-friendly
# pseudo code
int i = 0;
LOOP:
i = i + 1;
if(i < 10) goto LOOP;

## Slide 56: Example Do-While Loop
# Equivalent MIPS assembly code
li $t0, 0
li $t1, 10
LOOP:
# Increment $t0 by 1
addi $t0, $t0, 1
# if $t0 < 10 goto LOOP
blt $t0, $t1, LOOP

## Slide 57: Counting Down
Counting down to zero can be slightly more efficient if the direction of the counting loop does not matter
Avoids need for a second register to hold the upper bound of the loop index

## Slide 58: Example Do-While Loop
# Branch-friendly pseudo code
int i = 10;
LOOP:
i = i - 1;
if (i > 0) goto LOOP;

## Slide 59: Example Do-While Loop
# Equivalent MIPS assembly code
li $t0, 10
LOOP:
# Decrement $t0 by 1
addi $t0, $t0, -1
# if $t0 > 0 goto LOOP
bgtz $t0, LOOP

## Slide 60: Exercise
Write the MIPS assembly code for:
# User must enter an integer between 1-10
int x;
do
{
cin >> x;
}
while(x < 0 || x > 10);

## Slide 61: Exercise: Solution
# Load register with upper bound of 10.
li $s0, 10
LOOP:
# Load register $v0 with code 5 for read integer
li $v0, 5
# Read integer returns value in $v0 register
syscall
bltz $v0, LOOP
bgt $v0, $s0, LOOP

## Slide 62: While Loop
# High-level language pseudo code
int i = 0;
while (i < 10)
{
i = i + 1;
}
# MIPS branch-friendly pseudo code
int i = 0;
LOOP:
if (i >= 10) goto END_WHILE;
i = i + 1;
goto LOOP;
END_WHILE:

## Slide 63: While Loop
# MIPS branch-friendly pseudo code
int i = 0;
LOOP:
if (i >= 10) goto END_WHILE;
i = i + 1;
goto LOOP;
# Equivalent MIPS assembly code
li $t0, 0
li $t1, 10
LOOP: bge $t0, $t1, END_WHILE
addi $t0, $t0, 1
b LOOP
END_WHILE:

## Slide 64: Exercise
Write the branch-friendly pseudo code
while ($t0 > 0 || $t1 > 0)
{
  $t0 += $s0;
  $t1 += $s1;
}

## Slide 65: Exercise
Write the equivalent MIPS assembly code
WHILE:
if !($t0 > 0 || $t1 > 0) goto END_WHILE;
$t0 += $s0;
$t1 += $s1;
goto WHILE;
END_WHILE:

## Slide 66: Exercise Solution
# Branch-friendly pseudo code
WHILE:
if !($t0 > 0 || $t1 > 0) goto END_WHILE;
$t0 += $s0;
$t1 += $s1;
goto WHILE;
END_WHILE:
# Equivalent MIPS assembly code
WHILE: sgt $v0, $t0, $zero
sgt $v1, $t1, $zero
or $v0, $v0, $v1
beqz $v0, END_WHILE
add $t0, $t0, $s0
add $t1, $t1, $s1
b WHILE
END_WHILE:

## Slide 67: Exercise
Write the branch-friendly pseudo code
int i = 10;
int sum = 0;
while (i >= 0)
{
sum = sum + i;
  i = i – 1;
}

## Slide 68: Exercise
Write the equivalent MIPS assembly code
i = 10;
sum = 0;
WHILE:
if (i < 0) goto END_WHILE;
sum = sum + i;
i = i – 1;
goto WHILE;
END_WHILE:

## Slide 69: Exercise Solution
# Branch-friendly pseudo code
i = 10;
sum = 0;
WHILE:
if (i < 0) goto END_WHILE;
sum = sum + i;
i = i – 1;
goto WHILE;
# Equivalent MIPS assembly code
li $t0, 10
li $s0, 0
WHILE: bltz $t0, END_WHILE
add $s0, $s0, $t0
addi $t0, $t0, -1
b WHILE
END_WHILE:

## Slide 70: Nested Loop Exercise
int x = 0; # $t0 = x
while(x < 3) # $s0 = 3
{
int y = 0; # $t1 = y
while(y < 5) # $s1 = 5
{
y++;
}
x++;
}
Write the equivalent MIPS code