## Slide 1: Memory Addressing
Updated 7/9/2013

## Slide 2: Load & Store Instructions
MIPS is a “load-store” architecture meaning only load & store instructions access memory.
Since all MIPS arithmetic and logical instructions operate on registers, the load and store instructions are used to move data between the registers and memory.

## Slide 3: Data Stored in RAM
A typical real-world program will have more data than can be stored simultaneously in the 24-programmer usable MIPS registers.
Must store program data in main memory and move data currently processed into registers, process data, and store results back to main memory.

## Slide 4: Variables to Registers
Pascal or C, programmers use descriptive variable names such as: speed, volume, or size.
When the machine language code runs on the processor, the variables will be stored in memory locations and/or registers.
To efficiently execute code, a compiler will attempt to keep the variables that are referenced most often in processor registers because access to a variable in a processor register is much faster than access to memory.

## Slide 5: “Spilling” Registers
Put less commonly used data or variables needed later into memory.
Keep currently used data or variables in registers.
A compiler or assembly programmer must utilize registers well since register access is faster than memory access.

## Slide 6: Memory Organization
Viewed as a large, single-dimension array, with an address.
A memory address is an index into the array such as 0, 1, 2, 3...
"Byte addressing" means that the index refers to one byte or 8 bits of data.
0
1
2
3
4
5
6
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 7: Memory Organization
For MIPS, a word is 32 bits or 4 bytes.
232 bytes with byte addresses from 0 to 232-1
230 words with byte addresses 0, 4, 8, ... 230-4

## Slide 8: MIPS 32-bit Words
0
4
8
12
32 bits of data
32 bits of data
32 bits of data
32 bits of data
Words are aligned by chunks of 4-bytes (32-bits)
Words addresses at 0, 4, 8, 12, 16, 20, 24, ...
16
20
24
28
32 bits of data
32 bits of data
32 bits of data
32 bits of data

## Slide 9: Word Alignment for LW / SW
MIPS load and store instructions that move 32-bit word values between registers and memory
  lw: Load word instruction
  sw: Store word instruction
Load word & store word instructions require memory address to be a multiple of 4 such as 0, 4, 8, 12, 16, etc.

## Slide 10: Load from Memory Address
# Load register $t0 with contents
# of word at specified address
lw $t0, 0xB300
The address constant 0xB300 is expressed as a 16-bit immediate value

## Slide 11: Store to Memory Address
# Store contents of register $t0
# into word at specified address
sw $t0, 0xB300
The address constant 0xB300 is expressed as a 16-bit immediate value

## Slide 12: Example 16-bit Addressing
0xB300
0xFF00FF00
32 bits of data
32 bits of data
32 bits of data
32 bits of data
32 bits of data
32 bits of data
32 bits of data
0xB304
0xB308
0xB30C
0xB310
0xB314
0xB318
0xB31C
lw $t0, 0xB300
# Result is that register $t0 holds the # 32-bit value 0xFF00FF00

## Slide 13: Example 16-bit Addressing
0xB300
0xFF00FF00
32 bits of data
32 bits of data
32 bits of data
0xFF00FF00
32 bits of data
32 bits of data
32 bits of data
0xB304
0xB308
0xB30C
0xB310
0xB314
0xB318
0xB31C
lw $t0, 0xB300
sw $t0, 0xB310
# Result is that register memory # location 0xB310 is assigned
# the 32-bit value 0xFF00FF00

## Slide 14: Exercise
0xB300
Value of A
Value of B
Value of Temp
32 bits of data
32 bits of data
32 bits of data
32 bits of data
0xB304
0xB308
0xB30C
0xB310
0xB314
0xB318
0xB31C
Let A, B, and Temp be 32-bit integer variables with memory addresses:
A: 0xB300
B: 0xB304
Temp: 0xB308
32 bits of data

## Slide 15: Exercise
0xB300
Value of A
Value of B
Value of Temp
32 bits of data
32 bits of data
32 bits of data
32 bits of data
0xB304
0xB308
0xB30C
0xB310
0xB314
0xB318
0xB31C
Write 16-bit MIPS load/store word instructions to swap the values of A & B.
32 bits of data

## Slide 16: Exercise: Solution
0xB300
Value of A
Value of B
Value of C
32 bits of data
32 bits of data
32 bits of data
32 bits of data
0xB304
0xB308
0xB30C
0xB310
0xB314
0xB318
0xB31C
# C = A
lw $t0, 0xB300
sw $t0, 0xB308
# A = B
lw $t0, 0xB304
sw $t0, 0xB300
# B = C
lw $t0, 0xB308
sw $t0, 0xB304
32 bits of data

## Slide 17: Register Memory Addressing
An immediate constant can only specify a 16-bit address
A 16-bit address can only index up to 216 / 4 or 4,096 32-bit words
Overcome this limit by using a register to hold the memory address

## Slide 18: Memory Allocation
In general a programmer does not get to choose the address where a piece of data will be stored.
The programmer requests space to hold data and the Operating System provides the starting address of an unused block of memory.

## Slide 19: Request Space for Data
Use the “load address” la instruction to load a 32-bit register with the address of a given labeled datum.
Familiar example:
.data
Messg: .asciiz “Hello\n”
.text
main:
la $a0, Messg

## Slide 20: Request Space for Data
Use the “load address” la instruction to load a 32-bit register with the address of a given labeled datum.
Example:
.data
A: .word 100
B: .word 200
Temp: .word 0
.text
main:
la $a0, A

## Slide 21: Load from Memory Address
# Load register $t0 with contents
# of word whose 32-bit address is
# given by register $a0
lw $t0, ($a0)
The ()s are necessary to say interpret the contents of $a0 as an address

## Slide 22: Store to Memory Address
# Store contents of register $t0
# into word whose 32-bit address
# is given by register $a1
sw $t0, ($a1)

## Slide 23: Programming Exercise
Declare 32-bit data words A, B, and Temp having initial values of 100, 200, and 0, respectively.
Use the load address, load word, and store word instructions to swap the values of data variables A and B.

## Slide 24: Programming Exercise
.data
# Initialize variable A to 100
A: .word 100
# Initialize variable B to 200
B: .word 200
# Initialize variable Temp to 0
Temp: .word 0

## Slide 25: Solution
# $a0 = address of A
la $a0, A
# $a1 = address of B
la $a1, B
# $a2 = address of temp
la $a2, Temp
# Temp = A
lw $t0, ($a0)
sw $t0, ($a2)
# A = B
lw $t0, ($a1)
sw $t0, ($a0)
# B = Temp
lw $t0, ($a2)
sw $t0, ($a1)

## Slide 26: Compute Area of Two Rooms
.data
# Initialize variable widthA to 10
widthA: .word 10
# Initialize variable heightA to 20
heightA: .word 20
# Initialize variable widthB to 15
widthB: .word 15
# Initialize variable heightB to 25
heightB: .word 25
# Initialize variable area
area: .word 0

## Slide 27: Solution – Page 1 of 2
# $a0 = address of widthA
la $a0, widthA
# $a1 = address of heightA
la $a1, heightA
# Get width & height of room A into
# $t0 and $t1
lw $t0, ($a0)
lw $t1, ($a1)
# $s0 = $t0 x $t1 area of room A
mul $s0, $t0, $t1

## Slide 28: Solution – Page 2 of 2
# $a0 = address of widthB
la $a0, widthB
# $a1 = address of heightB
la $a1, heightB
# Get width & height of room B into
# $t0 and $t1
lw $t0, ($a0)
lw $t1, ($a1)
# $s1 = $t0 x $t1 area of room B
mul $s1, $t0, $t1
# $s2 = $s0 + $s1
add $s2, $s0, $s1
# Store total area into variable.
la $a2, area
sw $s2, ($a2)

## Slide 29: Addressing Bytes of Memory
MIPS provides instructions to load and store one byte of memory at a time
Load & store of bytes involves the low-order 8-bits of a processor register

## Slide 30: Load Byte
Load byte at specified 16-bit immediate address into the destination register
  Byte address can be 0, 1, 2, 3, ... and is not required to be a multiple of 4
The 8-bit value is sign-extended to fill the 32-bit register

## Slide 31: Load Byte
# Load byte at address 0x45EF into
# register $t0
lb $t0, 0x45EF
Byte at address 0x45EF: 0001 1100
$t0 = 0000 0000 0000 0000 0000 0000 0001 1100
Two’s complement sign extension fills 24 high-order bits with sign bit 0

## Slide 32: Load Byte
# Load byte at address 0x45EF into
# register $t0
lb $t0, 0x45EF
Byte at address 0x45EF: 1111 1100
$t0 = 1111 1111 1111 1111 1111 1111 1111 1100
Two’s complement sign extension fills 24 high-order bits with sign bit 1

## Slide 33: Load Byte Unsigned
Load byte at specified 16-bit immediate address into the destination register
  Byte address can be 0, 1, 2, 3, ... and is not required to be a multiple of 4
The 8-bit value is not sign extended
High-order bits of destination register are 0

## Slide 34: Load Byte Unsigned
# Load byte at address 0x45EF into
# register $t0
lbu $t0, 0x45EF
Byte at address 0x45EF: 0001 1100
$t0 = 0000 0000 0000 0000 0000 0000 0001 1100
lbu fills 24 high-order bits of register to 0

## Slide 35: Load Byte Unsigned
# Load byte at address 0x45EF into
# register $t0
lbu $t0, 0x45EF
Byte at address 0x45EF: 1111 1100
$t0 = 0000 0000 0000 0000 0000 0000 1111 1100
lbu fills 24 high-order bits of register to 0

## Slide 36: Store Byte
Store low-order 8-bits of register into byte specified 16-bit immediate address
  Byte address can be 0, 1, 2, 3, ... and is not required to be a multiple of 4

## Slide 37: Store Byte
# Store low-order 8-bits of register
# into byte at address 0x45EF
sb $t0, 0x45EF
Byte at address 0x45EF: 0001 1100
$t0 = 0000 0000 0000 0110 1100 1011 0001 1100

## Slide 38: Exercise
Declare 32-bit data bytes A, B, and Temp having initial values of 128, 7, and 0, respectively.
Use the load address, load byte or load byte unsigned, and store byte instructions to swap the values of data variables A and B.

## Slide 39: Exercise
.data
# Initialize variable A to 128
A: .byte 128
# Initialize variable B to 7
B: .byte 7
# Initialize variable Temp to 0
Temp: .byte 0

## Slide 40: Solution
# $a0 = address of A
la $a0, A
# $a1 = address of B
la $a1, B
# $a2 = address of temp
la $a2, Temp
# Temp = A
lbu $t0, ($a0)
sb $t0, ($a2)
# A = B
lbu $t0, ($a1)
sb $t0, ($a0)
# B = Temp
lbu $t0, ($a2)
sb $t0, ($a1)

## Slide 41: Base Plus Displacement
Programs will frequently access memory locations in sequence.
for(int i = 0; i < 10; i++)
{
C[i] = A[i] + B[i];
}

## Slide 42: Base Plus Displacement
Specify the effective (actual) address using two parts
Base: the fixed address marking the beginning of a “chunk” of memory
Displacement: an integer offset from the base address

## Slide 43: Base Plus Displacement
Effective Address =
  Base Address + Displacement
Suppose the first 32-bit word of an array is stored at address 1000
Let the base address be 1000
1000
7
1004
23
1008
32
1012
16
1016
4
1020
89
1024
120
1028
16
1032
8

## Slide 44: Base Plus Displacement
Effective Address =
  Base Address + Displacement
Use the displacement to index an element of the array
Since this is an array of 32-bit words the displacement must also be a multiple of 4
1000
7
1004
23
1008
32
1012
16
1016
4
1020
89
1024
120
1028
16
1032
8

## Slide 45: Base Plus Displacement
Effective Address =
  Base Address + Displacement
Access array[5] which is the 6th 32-bit word of the array
  Base address = 1000
  Displacement = 20 = 5 * 4
Effective address = 1000 + 20 = 1020
1000
7
1004
23
1008
32
1012
16
1016
9
1020
89
1024
120
1028
16
1032
8

## Slide 46: Base Displacement Exercise
Give the base address and offset to index the following elements of the array of 32-bit words.
1) A[3]
2) A[6]
2000
7
2004
23
2008
32
2012
16
2016
4
2020
89
2024
120
2028
16
2032
8

## Slide 47: Exercise Solution
1) A[3]
Base = 2000
Offset = 12
Effective address = 2012
2) A[6]
Base = 2000
Offset = 24
Effective address = 2024
2000
7
2004
23
2008
32
2012
16
2016
4
2020
89
2024
120
2028
16
2032
8

## Slide 48: MIPS Base Plus Displacement
The base address must be given in one of the MIPS registers
The MIPS displacement is a 16-bit integer ranging between -32,768 to +32,764
The effective address must be a multiple of four when using load/store word instructions

## Slide 49: Declaring Array Data
Declare three arrays of unsigned 8-bit integers
.data
X: .byte 1, 2, 4, 8
Y: .byte 3, 7, 2, 4
Z: .byte 0, 0, 0, 0

## Slide 50: Setting Base Address
Load the address of the array’s symbolic label into base register $a0
la $a0, X
la $a1, Y
la $a2, Z

## Slide 51: Exercise
Write MIPS assembly code to compute:
Z[0] = X[0] + Y[0];

## Slide 52: Solution
# compute Z[0] = X[0] + Y[0]
# Byte-sized chunks increment by 1
lbu $t0, 0($a0)
lbu $t1, 0($a1)
add $t2, $t0, $t1
sb $t2, 0($a2)

## Slide 53: Exercise
Write MIPS assembly code to compute:
Z[3] = X[3] + Y[3];

## Slide 54: Solution
# compute Z[3] = X[3] + Y[3]
# Byte-sized chunks increment by 1
lbu $t0, 3($a0)
lbu $t1, 3($a1)
add $t2, $t0, $t1
sb $t2, 3($a2)

## Slide 55: Declaring Array Data
Declare three arrays of unsigned 32-bit integers
.data
X: .word 1, 2, 4, 8
Y: .word 3, 7, 2, 4
Z: .word 0, 0, 0, 0

## Slide 56: Setting Base Address
Load the address of the array’s symbolic label into base register $a0
la $a0, X
la $a1, Y
la $a2, Z

## Slide 57: Exercise
Write MIPS assembly code to compute:
Z[3] = X[3] + Y[3];

## Slide 58: Solution
# compute Z[3] = X[3] + Y[3]
# word-sized chunks increment by 4
# Offset is 3 x 4 or 12
lw $t0, 12($a0)
lw $t1, 12($a1)
add $t2, $t0, $t1
sw $t2, 12($a2)

## Slide 59: Declaring an Empty Array
.data
# Allocate 32 bytes for Empty array.
Empty: .space 32
Specify the amount of space to allocate as a number of bytes.
To allocate a number of words multiply by 4 bytes per word.

## Slide 60: Filling an Array
.data
# Allocate 32 bytes for Empty array.
Empty: .space 32
main: la $a0, Empty
li $t0, 0
# Store $t0 into Empty[0]
sw $t0, 0($a0)
# Store $t0 into Empty[1] sw $t0, 4($a0)
# Store $t0 into Empty[2]
sw $t0, 8($a0)
# Store $t0 into Empty[3]
sw $t0, 12($a0)

## Slide 61: Filling an Array – Take Two
la $a0, Empty
li $t0, 0
# Store $t0 into Empty[0]
sw $t0, 0($a0)
# Addr = base+displacement
addi $a0, $a0, 4
# Store $t0 into Empty[1] sw $t0, 4($a0)
# Addr = base+displacement
addi $a0, $a0, 4
# Store $t0 into Empty[2]
sw $t0, 8($a0)
# Addr = base+displacement
addi $a0, $a0, 4
# Store $t0 into Empty[3]
sw $t0, 12($a0)

## Slide 62: Exercise
Declare Messg to be an array of 4 bytes
Use the li and sb instructions to fill this array with the characters “H”, “O”, “T”
    65 is the ASCII code for “A”
Store the value 0x00 into the last element of the array to null terminate the string
Use the print string system call to display the characters in the array Messg.

## Slide 63: Loops and Arrays
Since the MIPS displacement must be a constant, it is of little help when we want to use a loop to process an array.
Always fix the displacement to zero.
Increment or decrement the array base address to step through the array.
Increment or decrement by the size of each element in bytes.

## Slide 64: Filling an Array using Loop
.data
# Allocate 32 bytes for Empty array.
Empty: .space 32
.text
main:
la $a0, Empty
# Value to fill each element
li $v0, 0
# Count of elements to initialize
li $t0, 4
Loop:
# May omit offset of 0
sw $v0, 0($a0)
# Increment array pointer by element size
addi $a0, $a0, 4
addi $t0, $t0, -1
bgtz $t0, Loop

## Slide 65: Exercise: Array Sum
int i = 0;
int sum = 0;
int A[] = { 10, 15, 2, 7, 5, 8, 44, 89, 9, 77 };
while(i < 10)
{
sum += A[i];
i++;
}

## Slide 66: Exercise: Array Sum
.data
A: .byte 10, 15, 2, 7, 5, 8, 44, 89, 9, 77
Given the array of unsigned 8-bit integers
Accumulate the sum in $s0

## Slide 67: Sum of Array of Bytes
.data
A: .byte 10, 15, 2, 7, 5, 8, 44, 89, 9, 77
.text
main: la $a0, A # Base address
li $t0, 0 # Loop counter
li $t7, 10 # Loop limit
li $s0, 0 # Sum = 0
LOOP: lb $t1, 0($a0)
add $s0, $s0, $t1
# increment base+displacemnet
addi $a0, $a0, 1
addi $t0, $t0, 1
blt $t0, $t7, LOOP

## Slide 68: Loop Over Array of Words
To loop through an array of 32-bit words
Increment address register by 4 bytes to move on to the next array element

## Slide 69: Sum of Array of Words
.data
A: .word 10, 15, 2, 7, 5, 8, 44, 89, 9, 77
.text
main: la $a0, A # Base address
li $t0, 0 # Loop counter
li $t7, 10 # Loop limit
li $s0, 0 # Sum = 0
LOOP: lw $t1, 0($a0)
add $s0, $s0, $t1
# increment base address in register $a0
addi $a0, $a0, 4
addi $t0, $t0, 1
blt $t0, $t7, LOOP

## Slide 70: Exercise
.data
A: .word 10, 15, 2, 7, 5, 8, 44, 89, 9, 77
Write a loop to find the maximum value.
Leave the maximum value in register $A1.
Print out value of maximum.

## Slide 71: Reading a String from Keyboard
.data
# Declare buffer array of 80 bytes.
SBuf: .space 80
.text
main:
# Read string system call in register $v0
li $v0, 8
# Load address of string into register $a0
la $a0, SBuf
# Specify size of buffer in register $a1
li $a1, 80
syscall

## Slide 72: Exercise
Assume Letters is the label for an array of 80 bytes
Assume its contents have been initialized to contain only upper or lower case letters
The string ends with the ‘\0’ ASCII integer code value of zero
Write a loop to convert all lower case letters to their upper case equivalents
‘A’ = 65, ‘Z’ = 90, ‘a’ = 97, ‘z’ = 122

## Slide 73: Two-Dimensional Arrays
The elements of a multi-dimensional array are stored in consecutive locations in memory
Row major order: assign array elements to memory locations row-by-row
Column major order: assign array elements to memory locations column-by-column

## Slide 74: Row-Major 8-Bit Example
col
row 0 1 2
0 ‘A’ ‘B’ ‘C’
1 ‘D’ ‘E’ ‘F’
2 ‘G’ ‘H’ ‘I’
‘A’ ‘B’ ‘C’ ‘D’ ‘E’ ‘F’ ‘G’ ‘H’ ‘I’
0 1 2 3 4 5 6 7 8
----------- memory address of elements ------------>
FYI: C, C++, Java store array elements according to row-major order
Can you derive the equation to go from [row][col] to offset?

## Slide 75: Row Major Exercise
Given array A of 8-bit elements in row-major order.
8 rows and 10 columns
A[row][col], for 0 <= row < 8 and 0 <= col < 10
Find offset in bytes for elements:
  A[0][8] = (0 * 10) + 8 = 8
  A[1][0] = (1 * 10) + 0 = 10
  A[1][9] = (1 * 10) + 9 = 19
  A[6][6] = (6 * 10) + 6 = 66
  A[7][9] = (7 * 10) + 9 = 79
  A[r][c] = (r * num_columns) + c

## Slide 76: Row-Major 32-Bit Example
col
row 0 1 2
0 ‘A’ ‘B’ ‘C’
1 ‘D’ ‘E’ ‘F’
2 ‘G’ ‘H’ ‘I’
‘A’ ‘B’ ‘C’ ‘D’ ‘E’ ‘F’ ‘G’ ‘H’ ‘I’
0 4 8 12 16 20 24 28 32
----------- memory address of elements ------------>
FYI: C, C++, Java store array elements according to row-major order

## Slide 77: Row Major Exercise
Given array A of 32-bit elements in row-major order.
8 rows and 10 columns
A[row][col], for 0 <= row < 8 and 0 <= col < 10
Find offset in bytes for elements:
  A[0][8] = (0 * 10*4) + 8*4 = 0 + 32 = 32
  A[1][0] = (1 * 10*4) + 0*4 = 40 + 0 = 40
  A[1][9] = (1 * 10*4) + 9*4 = 40 + 36 = 76
  A[6][6] = (6 * 10*4) + 6*4 = 240 +24 = 264
  A[7][9] = (7 * 10*4) + 9*4 = 280 + 36 = 316
  A[r][c] = ((r * num_columns) + c) * element_size)

## Slide 78: Row Major Addressing Exercise
Assume row-major array of 32-bit integers
40 Rows and 80 columns
Assume all elements are initialized
Write MIPS code to compute:
A[16][12] = 32 * A[16][11]

## Slide 79: Row Major Addressing Solution
  A[r][c] = ((r * 80) + c) * element_size)
Write MIPS code to compute:
A[16][12] = 32 * A[16][11]
la $a0, A
li $s0, 80 # Num columns
li $t0, 16 # Row index
mul $t0, $t0, $s0 # r = r * 80
addi $t0, $t0, 11 # Add column index
sll $t0, $t0, 2 # multiply by 4
add $t0, $t0, $a0 # add base + offset
lw $v0, ($t0) # Get A[16][11]
sll $v0, $v0, 5 # 32 * A[16][11]
addi $t0, $t0, 4 # Add of A[16][12]
sw $v0, ($t0)

## Slide 80: Nested Loop Exercise
int row = 0; # $t0 = row
while(row < 5) # $s0 = 3
{
int col = 0; # $t1 = col
while(col < 4) # $s1 = 5
{
col++;
}
row++;
}
Write the equivalent MIPS code

## Slide 81: Two-D Array Exercise
.data
# 5 rows x 4 columns row-major order
A: .word 1, 2, 3, 4, 5, 6, 7, 8, 9,
10, 11, 12, 13, 14, 15, 16,
17, 18, 19, 20
# the data above must be on one line
NEW_LINE: .asciiz “\n”
Write a nested loop to print the 5x4 table

## Slide 82: Find the Treasure $
.data
# Five rows x 6 columns ASCII maze board
# Assume row major-order
# Find ROW and COL indices of treasure $
A: .byte ‘#’, ‘#’, ‘#’, ‘#’, ‘#’, ‘#’,
‘#’, ‘.’, ‘.’, ‘#’, ‘.’, ‘#’,
‘#’, ‘.’, ‘.’, ‘#’, ‘$’, ‘#’,
‘#’, ‘.’, ‘.’, ‘.’, ‘.’, ‘#’,
‘#’, ‘#’, ‘#’, ‘#’, ‘#’, ‘#’
Goal: .byte ‘$’

## Slide 83: Question
What’s the most efficient way to find the row and column indices where the treasure ‘$’ is found.
Solution: 1-D loop to count offset of ‘$’ element
  Row = offset / row_size
  Col = offset % row_size

## Slide 84: Column-Major 8-Bit Example
col
row 0 1 2
0 ‘A’ ‘B’ ‘C’
1 ‘D’ ‘E’ ‘F’
‘A’ ‘D’ ‘B’ ‘E’ ‘C’ ‘F’
0 1 2 3 4 5
----------- memory address of elements ------------>
FYI: FORTRAN stores array elements according to column-major order
Can you derive the equation to go from [row][col] to offset?

## Slide 85: Column Major Exercise
Given array A of 8-bit elements in column-major order.
8 rows and 10 columns
A[row][col], for 0 <= row < 8 and 0 <= col < 10
Find offset in bytes for elements:
  A[0][8] = (8 * 8) + 0 = 64 + 0 = 64
  A[1][0] = (0 * 8) + 1 = 1
  A[1][9] = (9 * 8) + 1 = 73
  A[6][6] = (6 * 8) + 8 = 56
  A[7][9] = (9 * 8) + 7 = 79
  A[r][c] = (c * num_rows) + r

## Slide 86: Column-Major 32-Bit Example
col
row 0 1 2
0 ‘A’ ‘B’ ‘C’
1 ‘D’ ‘E’ ‘F’
‘A’ ‘D’ ‘B’ ‘E’ ‘C’ ‘F’
0 4 8 12 16 20
----------- memory address of elements ------------>
FYI: FORTRAN stores array elements according to column-major order

## Slide 87: Column Major Exercise
Given array A of 32-bit elements in column-major order.
8 rows and 10 columns
A[row][col], for 0 <= row < 8 and 0 <= col < 10
Find offset in bytes for elements:
  A[0][8] = ((8 * 8) + 0)*4 = 64*4 = 256
  A[1][0] = ((0 * 8) + 1)*4 = 1*4 = 4
  A[1][9] = ((9 * 8) + 1)*4 = 73*4 = 292
  A[6][6] = ((6 * 8) + 8)*4 = 56*4 = 224
  A[7][9] = ((9 * 8) + 7)*4 = 79*4 = 316
  A[r][c] = ((c * num_rows) + r) * element_size

## Slide 88: Column Major Exercise
.data
# 3 rows, 4 columns stored in column-major order
A: .word 10, 8, 16, 15, 3, 5, 7, 2, 9, 4, 11, 6
.text
main:
Write a loop in MIPS code to find the sum of the four elements on the second (middle row).
15 7 4
3 2 11
16 5 9 6