## Slide 1: Switch Statement
Updated 7/11/2013
Pre-requisites: 1D array addressing

## Slide 2: Example Switch Statement
# high-level language pseudo code
int C = 2;
int X = 0;
switch(C)
{
case 0: X = X + 1; break;
case 1: X = X + 2; break;
case 2: X = X + 3; break;
}

## Slide 3: Example Switch Statement
JUMP_TABLE = { case0, case1, case2 }
# Default skips over switch if key value is out of range
if (C < 0) goto END_SWITCH;
if (C > 2) goto END_SWITCH;
goto JUMP_TABLE[C];
case0: $s0 = $s0 + 1; goto END_SWITCH;
case1: $s0 = $s0 + 2; goto END_SWITCH;
case2: $s0 = $s0 + 3; goto END_SWITCH;
END_SWITCH:

## Slide 4: MIPS Jump Table
Initialize an array of 32-bit words so each element holds the address of the first instruction of each switch case
.data
JUMP_TABLE: .word case0, case1, case2
...
case0: add $s0, $s0, 1
b END_SWITCH
case1: add $s0, $s0, 2
b END_SWITCH
case2: add $s0, $s0, 3
b END_SWITCH

## Slide 5: Jump Register Instruction
Jump to the 32-bit address contained in the specified register
jr $t1

## Slide 6: Using the Jump Table
The case variable value 0, 1, or 2 is used to index an element of the Jump Table
Must multiply case variable value by 4 since the Jump Table is an array of words
int C = 2; // C = 0, 1, or 2
$t1 = JumpTable[C*4];
jr $t1

## Slide 7: MIPS Switch Statement
.data
JUMP_TABLE: .word case0, case1, case2
.text
main:
# Let $t0 hold the switch value 0, 1, or 2
bltz $t0, END_SWITCH
li $t1, 2
bgt $t0, $t1, END_SWITCH
# Multiply switch value 0, 1, or 2 by 4
sll $t0, $t0, 2
la $a0, JUMP_TABLE
add $a0, $a0, $t0
lw $t2, 0($a0)
jr $t2
case0: add $s0, $s0, 1
b END_SWITCH
case1: add $s0, $s0, 2
b END_SWITCH
case2: add $s0, $s0, 3
b END_SWITCH
END_SWITCH: