## Slide 1: MIPS Instruction Encodings
Updated 7/12/2013

## Slide 2: Instruction Formats
The fixed 32-bit MIPS instruction may be encoded in one of three different formats depending on the number of operands, type of operands, and functionality of the instruction.
  Immediate format
  Register format
  Jump format

## Slide 3: Immediate Format
5-bits
5-bits
16-bits
6-bits
Op-Code
Source register
Destination register
Immediate Constant
Most instructions that involve a 16-bit immediate mode constant are encoded using the following format.
The 32-bit MIPS instruction word is divided as shown.

## Slide 4: Immediate Format: Example
5-bits
5-bits
16-bits
6-bits
Op-Code
Immediate Constant
# Load register $t0 with value 255.
ori $t0, $zero, 255
32 registers 0...31 with
register $zero represented by code 0
register $t0 represented by code 8
0
8
255
Source register
Destination register
13

## Slide 5: Immediate Format: Example
5-bits
5-bits
16-bits
6-bits
Op-Code
Immediate Constant
# Load register $t0 with value 255.
ori $t0, $zero, 255
Encode the bit-fields into a 32-bit hexadecimal number
0
8
255
Source register
Destination register
13
01000
0000 0000 1111 1111
001101
00000
0x340800FF

## Slide 6: Immediate Format: Example
5-bits
5-bits
16-bits
6-bits
Op-Code
Immediate Constant
# $t1 = $t0 + 1.
addi $t1, $t0, 1
register $t0 represented by code 8
register $t1 represented by code 9
8
9
1
Source register
Destination register
8

## Slide 7: Immediate Format: Example
5-bits
5-bits
16-bits
6-bits
Op-Code
Immediate Constant
# $t1 = $t0 + 1.
addi $t1, $t0, 1
Encode the bit-fields into a 32-bit hexadecimal number
8
9
1
Source register
Destination register
8
01001
0000 0000 0000 0001
001000
01000
0x21090001

## Slide 8: Immediate Format: Example
5-bits
5-bits
16-bits
6-bits
Op-Code
Immediate Constant
# $t1 = $t0 - 1.
addi $t1, $t0, -1
register $t0 represented by code 8
register $t1 represented by code 9
8
9
-1
Source register
Destination register
8

## Slide 9: Immediate Format: Example
5-bits
5-bits
16-bits
6-bits
Op-Code
Immediate Constant
# $t1 = $t0 - 1.
addi $t1, $t0, -1
Encode the bit-fields into a 32-bit hexadecimal number
8
9
1
Source register
Destination register
8
01001
1111 1111 1111 1111
001000
01000
0x2109FFFF

## Slide 10: Hacking Program Binaries
Suppose you locate the instruction that increments score in your favorite game
# Increment player’s score by 10 points
addi $t0, $t0, 10
Hexadecimal encoded instruction
0x2108000A

## Slide 11: Hacking Program Binaries
Use a Hexadecimal file editor to change...
Hexadecimal encoded instruction
0x21080064
# Increment player’s score by 100 points
addi $t0, $t0, 100

## Slide 12: Immediate OpCodes
addi 8
andi 12
ori 13
xori 14

## Slide 13: Load Word
.data
A: .word 1, 2, 3
la $a0, A
lw $t0, 4($a0)
register $t0 represented by code 8
register $a0 represented by code 4

## Slide 14: Load Word
5-bits
5-bits
16-bits
6-bits
Op-Code
Immediate Constant
lw $t0, 4($a0)
register $t0 represented by code 8
register $a0 represented by code 4
4
8
4
Source register
Destination register
35

## Slide 15: Load Word
5-bits
5-bits
16-bits
6-bits
Op-Code
Immediate Constant
lw $t0, 4($a0)
Encode the bit-fields into a 32-bit hexadecimal number
4
8
4
Source register
Destination register
35
01000
0000 0000 0000 0100
100011
00100
0x8C880004

## Slide 16: Decoding Machine Instructions
Given encoded machine instruction represented by a binary number
Divide 32-bits into bit fields
Decode opcode, register(s), and immediate constant

## Slide 17: Decoding Example
Given encoded instruction:
0x3108F0F0
If given in hex, express as binary
0011 0001 0000 1000 1111 0000 1111 0000

## Slide 18: Decoding Example
0011 0001 0000 1000 1111 0000 1111 0000
Divide 32-bits into four fields...
001100 01000 01000 1111 0000 1111 0000

## Slide 19: Decoding Example
0011 0001 0000 1000 1111 0000 1111 0000
Divide 32-bits into four fields...
001100 01000 01000 1111 0000 1111 0000
Opcode = 001100 = 12 (base 10) = andi

## Slide 20: Decoding Example
0011 0001 0000 1000 1111 0000 1111 0000
Divide 32-bits into four fields...
001100 01000 01000 1111 0000 1111 0000
Source Register = 01000 = 8 = $t0

## Slide 21: Decoding Example
0011 0001 0000 1000 1111 0000 1111 0000
Divide 32-bits into four fields...
001100 01000 01000 1111 0000 1111 0000
Dest. Register = 01000 = 8 = $t0

## Slide 22: Decoding Example
0011 0001 0000 1000 1111 0000 1111 0000
Divide 32-bits into four fields...
001100 01000 01000 1111 0000 1111 0000
Constant = 1111 0000 1111 0000 = 0xF0F0

## Slide 23: Exercise
Decode the machine instruction
  0x214A0014

## Slide 24: Register Format
# $t2 = $t0 + $t1
add $t2, $t0, $t1
# $t2 = result of shifting bits of
# $t0 left by 8 bit positions.
sll $t2, $t0, 8

## Slide 25: Register Format
ADD $t0, $t1, $t2
This MIPS assembly instruction adds the values in registers $t1 and $t2 then stores the sum in register $t0.
The 32-bit register instruction specifies the operation (ADD) using the 6-bit function code field instead of the op-code field (set ZERO).
Since there are 32 registers we require 5 bits to specify each register operand. Each register is indexed by a number between 0 - 31.
5-bits
5-bits
5-bits
5-bits
000000
6-bits
Op-Code
1st source register
2nd source register
Destination register
Shift amount
Function code

## Slide 26: Register Format
Op-code: Always set to zero for register format
rs: First register source operand
rt: Second register source operand
rd: Destination register operand
shift amount: used for bit-wise shift/rotate instructions
function code: specific variant of the op-code

## Slide 27: Assembly to Machine Language
The 32-bit instruction is divided into bit fields.
Number of bits assigned to each field for a register format instruction.
17
18
8
0
0
32
Op-Code
1st source register
2nd source register
Destination register
Shift amount
Function code
5-bits
5-bits
5-bits
5-bits
6-bits
6-bits
Op-Code
1st source register
2nd source register
Destination register
Shift amount
Function code
Fill-in bit fields with encoding of add $t0, $s1, $s2
$s1
$s2
$t0
unused
ADD

## Slide 28: Assembly to Machine Language
17
18
8
0
0
32
Op-Code
1st source register
2nd source register
Destination register
Shift amount
Function code
10001
10010
01000
00000
000000
100000
Op-Code
1st source register
2nd source register
Destination register
Shift amount
Function code
The bit fields can be interpreted as binary numbers
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
32-bit binary value is the encoded machine language instruction.
See: page 117 of H&P: Computer Organization and Design

## Slide 29: Encoded Instruction
10001
10010
01000
00000
000000
100000
Op-Code
1st source register
2nd source register
Destination register
Shift amount
Function code
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
Here is the encoding of the instruction: add $t0, $s1, $s2
MARS simulator displays the 32-bit binary number in hexadecimal
0x02324020 = add $t0, $s1, $s2

## Slide 30: Decoding Machine Language
Sometimes a programmer must reverse-engineer machine language to reconstruct the assembly language code.
Debugging a MIPS core dump of sequence of 32-bit hexadecimal or binary numbers showing the section of code involved in the crash.
See: page 154 of H&P: Computer Organization and Design

## Slide 31: Decoding Machine Language
What is the assembly language for this machine language instruction?
See: page 154 of H&P: Computer Organization and Design
0000 0000 1010 1111 1000 0000 0010 0000
31
0
Begin by examining the high order 6 bits of the op-code field.
Hexadecimal representation: 0x00AF8020

## Slide 32: Decoding Machine Language
See: page 154 of H&P: Computer Organization and Design
0000 0000 1010 1111 1000 0000 0010 0000
31
0
Op-code = 0 ---> Register format instruction
Op-code of 0 signifies register format.

## Slide 33: Decoding Machine Language
Examine low-order 6 bits of function code.
See: page 154 of H&P: Computer Organization and Design
0000 0000 1010 1111 1000 0000 0010 0000
31
0
Op-code = 100000b = 32 ---> Function = ADD
Function code of 32 is an ADD instruction.

## Slide 34: Decoding Machine Language
Extract the two source and destination registers identifier numbers.
See: page 154 of H&P: Computer Organization and Design
0000 0000 1010 1111 1000 0000 0010 0000
31
0
rs = 5
rt = 15
rd = 16
Rs: source #1 = 5 ---> $a1
Rt: source #2 = 15 ---> $t7
Rd: destination = 16 ---> $s0
The assembly instruction is…
add $s0, $a1, $t7

## Slide 35: Instruction Encodings
Instruction Format OP RS RT RD Shift Function Address constant
add Register 0 reg reg reg 0 32 N/A
sub Register 0 reg reg reg 0 34 N/A
lw Immediate 35 reg reg N/A N/A N/A address
sw Immediate 43 reg reg N/A N/A N/A address
See: page 119 of H&P: Computer Organization and Design

## Slide 36: Example
Assume $t1 holds the base address of array A[]. Let h = $s2.
Source code: A[300] = h + A[300];
Compiler or assembly programmer produces:
lw $t0, 1200 ($t1) # $t0 = A[300]
add $t0, $s2, $t0 # $t0 = h + A[300]
sw $t0, 1200($t1) # A[300] = $t0 the result of the computation.
What is the MIPS machine language code for these three instructions?

## Slide 37: Solution
See: pages 120-121 of H&P: Computer Organization and Design
9 8 1200
100011 01001 01000 0000010010110000
1000 1101 0010 1000 0000 0100 1011 0000
0X8D2804B0
0 18 8 8 0 32
000000 10010 01000 01000 00000 100000
0000 0010 0100 1000 0100 0000 0010 0000
0X02484020

## Slide 38: Jump Instruction Format
J 0x12000
Jump to next execute the instruction at the specified target address.
26-bits
6-bits
Op-Code
Jump target address

## Slide 39: Numeric Indices for Registers
Numerical index code Register Symbolic Name
0 $zero
1 $at # reserved for assembler
2 $v0 # function return
3 $v1
4 $a0 # function arguments
5 $a1
6 $a2
7 $a3

## Slide 40: Numeric Indices for Registers
Numerical index code Register Symbolic Name
8 $t0 # function local variables
9 $t1
10 $t2
11 $t3
12 $t4
13 $t5
14 $t6
15 $t7

## Slide 41: Numeric Indices for Registers
Numerical index code Register Symbolic Name
16 $s0 # main program variables
17 $s1
18 $s2
19 $s3
20 $s4
21 $s5
22 $s6
23 $s7
24 $t8 # function local variables
25 $t9

## Slide 42: Numeric Indices for Registers
Numerical index code Register Symbolic Name
26 $k0 # reserved for OS kernel
27 $k1
28 $gp # pointer to globals
29 $sp # stack pointer
30 $fp # frame pointer
31 $ra # function return address

## Slide 43: Assembly Process
An assembler translates a source file of instructions expressed using symbolic mnemonics for the processor instructions.
Assembler outputs a binary object code file by encoding each assembly instruction as a 32-bit binary number.

## Slide 44: Two-Pass Assembler
Pass One:
  Identify all symbolic names such as data variables or branch labels.
  Determine the memory address for each symbol.
Pass Two:
  Encode each instruction into a 32-bit binary number.
  Output the object code file.

## Slide 45: Why Two Passes?
An assembler must make two passes over the assembly source instructions because some symbols are used before they are defined.

## Slide 46: Example of Symbol Usage
# Branch if $t0 is less than zero.
bltz $t0, END_IF
addi $t0, $t0, 1
END_IF:
addi $t0, $t0, -1

## Slide 47: Symbol Used before Defined
The symbol END_IF is used in an instruction before it is defined.
The assembler cannot encode the 32-bit binary instruction because it does not yet know how the location of END_IF
bltz $t0, END_IF

## Slide 48: Symbol Used before Defined
The MIPS .data section may be listed following the code statements.
la $a0, SumString
la $a1, ProdString
.data
SumString: .asciiz “Sum is “
ProdString: .asciiz “Product is “

## Slide 49: First Pass: build Symbol Table
The assembler’s first pass builds a symbol table of all symbolic names such as variable addresses or branch labels.
Add entry to symbol table for the first time that a new symbol is encountered.
Fill-in the symbol’s address as soon as that information becomes available.

## Slide 50: Example: Branch Label
bltz $t0, END_IF
addi $t0, $t0, 1
END_IF:
addi $t0, $t0, -1
Symbol Table
END_IF

## Slide 51: Example: Branch Label
0x0000 bltz $t0, END_IF
0x0004 addi $t0, $t0, 1
END_IF:
0x0008 addi $t0, $t0, -1
Symbol Table
END_IF 0x0008

## Slide 52: Count Instruction Sizes
The assembler must keep track of the address of each instruction as it scans the assembly source code.
Since all MIPS instructions encode to 32-bits the assembler simply increments the address of each successive instruction by 4 bytes.

## Slide 53: Example: Variable Address
la $a0, SumString
la $a1, ProdString
.data
SumString: .asciiz “Sum is “
ProdString: .asciiz “Product is “
Symbol Table
SumString

## Slide 54: Example: Variable Address
la $a0, SumString
la $a1, ProdString
.data
SumString: .asciiz “Sum is “
ProdString: .asciiz “Product is “
Symbol Table
SumString
ProdString

## Slide 55: Example: Variable Address
la $a0, SumString
la $a1, ProdString
# Assume data section begins at address 0x2000
.data
SumString: .asciiz “Sum is “
ProdString: .asciiz “Product is “
Symbol Table
SumString 0x2000
ProdString

## Slide 56: Example: Variable Address
la $a0, SumString
la $a1, ProdString
# Assume data section begins at address 0x2000
.data
SumString: .asciiz “Sum is “
ProdString: .asciiz “Product is “
Symbol Table
SumString 0x2000
ProdString 0x2008

## Slide 57: Pass Two: Encode Instructions
In its second pass over the source assembly instructions, the assembly can encode each instruction into its binary equivalent.
Whenever a symbol is encountered lookup its address from the symbol table.

## Slide 58: Object File Format
For a Unix OS, the object file consists of the following six sections:
  file header: general file format information
  text segment: machine language code
  data segment: program data variables
  relocation information: identify instructions that depend on absolute addresses
  symbol table: symbols not found in this object file
  debugging data: compiler flags & options

## Slide 59: Separate Compilation
A program may be developed from two or more source code files.
Each source file may be compiled and assembled individually to generate its object file.
  Only need to re-compile & assemble the source code files that are edited.

## Slide 60: Linkers
Separate source code files can include references to symbols that are defined in other source files.
The linker resolves instruction that reference symbols defined in other files to produce a single complete executable file.

## Slide 61: Linker Example
main:
# call subroutine
jal quickSort
...
# call library function
jal printf
quickSort:
code for quick sort
printf:
code for ‘C printf
LINKER
main:
# call subroutine
jal quickSort
...
# call library function
jal printf
...
quickSort:
code for quick sort
...
printf:
code for ‘C printf
Executable File
Object File
Object File
Object File

## Slide 62: Loader
Operating system reads the binary executable from disk into main memory.
Operating system allocates a contiguous block of memory to load the program.
Address constants in code must be “relocated” to their actual memory addresses.

## Slide 63: Relative Addresses
Object code files are typically generated with the first line of code reckoned at address 0.
When the object code is loaded into main memory, simply add the base address of the allocated space to all relative addresses to form absolute addresses.

## Slide 64: Loader: Example
Address Code
0x000 li $t0, 0
0x004 li $t7, 10
0x008 la $a0, A
LOOP:
0x00C lw $t1, ($a0)
0x010 add $t0, $t0, $t1
0x014 addi $a0, $a0, 4
0x018 addi $t7, $t7, -10
0x01C bgtz $t7, LOOP
Object File
Load program into memory beginning at address 0x2000
Address Code
0x2000 li $t0, 0
0x2004 li $t7, 10
0x2008 la $a0, A
LOOP:
0x200C lw $t1, ($a0)
0x2010 add $t0, $t0, $t1
0x2014 addi $a0, $a0, 4
0x2018 addi $t7, $t7, -10
0x201C bgtz $t7, LOOP
Program in Main Memory

## Slide 65: Loader: Example
Address Code
0x000 li $t0, 0
0x004 li $t7, 10
0x008 la $a0, A
LOOP:
0x00C lw $t1, ($a0)
0x010 add $t0, $t0, $t1
0x014 addi $a0, $a0, 4
0x018 addi $t7, $t7, -10
0x01C bgtz $t7, LOOP
Object File
Address Code
0x2000 li $t0, 0
0x2004 li $t7, 10
0x2008 la $a0, 0x2100
LOOP:
0x200C lw $t1, ($a0)
0x2010 add $t0, $t0, $t1
0x2014 addi $a0, $a0, 4
0x2018 addi $t7, $t7, -10
0x201C bgtz $t7, 0x200C
Program in Main Memory
A: 0x100
LOOP: 0x00C
A: 0x2100
LOOP: 0x200C