## Slide 1: Pipelining
7/12/2013

## Slide 2: Fetch-Execute Cycle
1. Fetch next instruction from RAM[IR]
Increment IR = IR + 1
2. Decode machine instruction
3. Fetch operand(s) from memory
4. Execute
5. Store result to destination register/RAM

## Slide 3: One Clock Cycle
Instruction Fetch
Instruction Decode
Operand Fetch
Execute Instruction
Store Result
1 second
Assume that a simple CPU has a clock rate of 1 hertz or 1 cycle per second and runs at 1.0 IPC

## Slide 4: Instruction Throughput
N seconds x (1 cycle / sec) x (1 instruction / cycle) =
N instructions
10 seconds x (1 cycle / sec) x (1 instruction / cycle) =
10 instructions
In 10 seconds our simple processor completes 10 instructions

## Slide 5: Clock Speed Sells
Marketers want to boost clock speed since 1 Hz doesn’t sound so hot
Process technology prevents a die shrink (less distance for electrons to travel)
Clever idea: If we do half the job in one clock cycle, we can run the clock twice as fast

## Slide 6: 5x Faster Clock Rate
Instruction Fetch
Instruction Decode
Operand Fetch
Execute Instruction
Store Result
1 second
Increase clock rate to 5 hertz or 5 cycles / second
cycle time is 0.2 seconds but at only 0.2 IPC
1 cycle
1 cycle
1 cycle
1 cycle
1 cycle

## Slide 7: Faster Instruction Throughput?
N seconds x (5 cycle / sec) x (0.2 instruction / cycle) =
10 seconds x (5 cycle / sec) x (0.2 instruction / cycle) =
10 instructions
In 10 seconds our 5 Hz processor completes 10 instructions…same throughput as our 1 Hz processor
IPC = 10 instructions / 50 cycles = 0.2

## Slide 8: Automobile Assembly Line
1914: Henry Ford introduced the assembly line
Throughput of 1 car every 93 minutes
Versus prior best of 1 every 728 minutes
Ford produced 308,162 cars, which was more than all 299 other auto manufacturers combined
Source: http://www.emediaplan.com/admunch/Brands/ford.asp

## Slide 9: Ford’s Innovations
Divide the job into 84 small steps
Place parts on a moving assembly line bringing the work to each worker
One worker completed the same step every 6 seconds
Labor savings cut price
from $825 to $300
Source: http://www.pbs.org/wgbh/aso/databank/entries/dt13as.html
http://www.detnews.com/2003/specialreport/0306/09/f08-186919.htm

## Slide 10: Moving Assembly Line in a CPU?
How can we apply the innovations of the moving assembly line to increase instruction throughput?
  Dedicated circuitry for each of our 5 stages
  Can have 5 instructions in process at any one time
  If each stage is completed in the same amount of time we expect a 5X speedup

## Slide 11: CPU Pipeline Circuitry
Source: http://arstechnica.com/paedia/c/cpu/part-2/cpu2-1.html
Basic 4 Stage CPU Pipeline

## Slide 12: Instruction Pipeline
Time

## Slide 13: Pipelined Throughput
Takes 5 cycles to complete the first instruction on our 5 Hz 1.0 IPC CPU
Complete 1 instruction per cycle thereafter
In 10 seconds…
  1 instruction + 9 seconds x 5 cycles / sec x 1 instructions / cycle =
  1 instr + 45 instr = 46 instructions
  Pipelined IPC = 46 instructions / 50 cycles = 0.92

## Slide 14: Pipeline Latency
Pipeline latency: amount of time to pass a single instruction through the pipeline.
Pipeline latency = num stages x clock cycle

## Slide 15: Pipeline Latency: Example
An non-pipelined processor has a 25ns cycle time evenly divided into 5 stages.
Assume there is a 1 ns latch delay between adjacent pipeline stages.
What is the total latency?

## Slide 16: Pipeline Latency: Example
cycle time(p) = cycle time(un)/stages +
latch latency
cycle time = 25ns/ 5 stages + 1 ns = 6 ns
Latency = cycle time x stages = 6 ns x 5 stages
= 30 ns

## Slide 17: Pipeline Latency: Exercise
An non-pipelined processor has a 25ns cycle time evenly divided into 50 stages.
Assume there is a 1 ns latch delay between adjacent pipeline stages.
What is the total latency?

## Slide 18: Pipeline Latency: Exercise
cycle time(p) = cycle time(un)/stages +
latch latency
cycle time = 25 ns / 50 stages + 1 ns = 1.5 ns
Latency = cycle time x stages = 1.5 ns x 50 stages
= 75 ns

## Slide 19: Pipeline Latency
Observation:
  Non-pipelined latency of 25 ns
  5 stage pipeline latency of 30 ns (20% longer)
  50 stage pipeline latency of 75 ns (300% longer)

## Slide 20: Limits of Pipelining
If a five stage pipeline yields a 5X speedup, why not increase the pipeline even more?
  Physical limit of space on die would require more circuitry for additional stages
  Not all instructions are independent of one another

## Slide 21: Dependencies
Instruction 1: C = A + B
Instruction 2: if(C > 4) then D = 2 * C;
Instruction 3: else D = -2 * C;
What should the pipeline do about instructions 2 and 3?

## Slide 22: Branch Prediction
Processor can try to guess which way the branch will go
Assume that an if-then is taken and process instruction 2 into the pipeline
Statistics show such guesses are correct 90% of the time

## Slide 23: Flushing the Pipeline
Suppose instructions F, G, H, and I depend on E
By the time E completes, we’ve worked on F, G, H, and I

## Slide 24: Flushing the Pipeline
Each time a branch prediction is incorrect, we must throw away the in-progress instructions resulting in wasted work
We waste 4 stages worth of work
If a pipeline had 20 stages such as the Intel Pentium III, we would lose 19 stages of work on a missed branch prediction

## Slide 25: Flushing the Pipeline
The 10% miss rate on branch prediction for the Pentium III results in between 20-40% of wasted time
This statistic emphasizes the importance of good branch prediction heuristics and the danger of making a pipeline too long

## Slide 26: Instruction Hazards
Data dependency between instructions A and B if one instruction reads or writes to a register that is used by the other.
Four types of data dependency hazards
  RAR: Read-after-Read
  RAW: Read-after-Write
  WAR: Write-after-Read
  WAW: Write-after-Write

## Slide 27: RAR: Read-After-Read
Example in MIPS assembly:
  add $t0, $t1, $t2
  add $s0, $s1, $t2
Both instructions read register $t2
Since this dependency is read-only the pipeline stages can safely over processing of both instructions

## Slide 28: RAW: Read-After-Write
Example in MIPS assembly:
  add $t0, $t1, $t2
  add $s0, $s1, $t0
Second instruction reads modified $t0
Processing of instruction #2 cannot begin in stage 3 (load operands) until instruction #1 has completed stage 5 (write back)

## Slide 29: Pipeline Stall (Bubble)

## Slide 30: WAW: Write-After-Write
Example in MIPS assembly:
  add $t0, $t1, $t2
  add $t0, $t3, $t4
Both instructions write register $t0
Pipelined processing will perform the write-backs storing $t0 in the same order so the pipelined result left in $t0 is correct

## Slide 31: WAR: Write-After-Read
Example in MIPS assembly:
  add $s0, $t0, $t2
  add $t0, $t3, $t4
Read of $t0 followed by write to $t0
Pipelined processing will read $t0 before second instruction can re-write its value so pipelined result left in $t0 is correct

## Slide 32: Pipeline Design
The pipeline produces one result in the amount of time needed to complete its slowest stage
Must carefully balance the division of work between pipeline stages so no one stage is much slower than the rest

## Slide 33: References
Pipelining, pushing the Clockspeed Envelope by Dan Mepham
http://www.hardwarecentral.com/hardwarecentral/print/2427/
Understanding Pipelining and Superscalar Execution by Jon Stokes
http://arstechnica.com/paedia/c/cpu/part-2/cpu2-1.html