## Slide 1: Trends in Cyber Physical Systems: A Historical Perspective
Systems that Interact with the Physical World
CSE 40437/60437-Spring 2015
Prof. Dong Wang

## Slide 2: Last Lecture
Grid Computing
Bio-info
Quantum
Brain
Interfaces
Computing
Interdisciplinary
Application
Research
Internet
GIS
Infosphere
Graphics
Databases
MANET
Security
High-performance
Computing
Centralized
machines
Parallel machines
Languages
Operating
Systems
Theory
Core
Architecture
Cyber-Physical
Systems
WWW
LANs
2007-now:

## Slide 3: This Lecture
History and Origin of CPS
Two Fundamental Challenges of Traditional CPS
Real-world Examples

## Slide 4: History: The Beginnings
NSF Workshop on Cyber-Physical Systems, October 16-17, 2006, Austin, TX.
National Meeting on Beyond SCADA: Networked Embedded Control for Cyber Physical Systems, November 8-9, 2006, Pittsburgh, PA.
National Workshop on High-Confidence Software Platforms for Cyber-Physical Systems (HCSP-CPS), November 30 - December 1, 2006, Alexandria, VA.
NSF Industry Round-Table on Cyber-Physical Systems, May 17, 2007, Arlington, VA.
Joint Workshop On High-Confidence Medical Devices, Software, and Systems (HCMDSS) and Medical Device Plug-and-Play (MD PnP) Interoperability, June 25-27, 2007, Boston, MA.
National Workshop on Composable Systems Technologies for High-Confidence Cyber-Physical Systems, July 9-10, 2007, Arlington, VA.
National Workshop on High-Confidence Automotive Cyber-Physical Systems, April 3-4, 2008, Troy, MI.
CPSWeek, April 21-24, 2008, St. Louis, MO.
CPS Summit, April 25, 2008, St. Louis, MO: NSF Announces new CPS Initiative
The First International Workshop on Cyber-Physical Systems, International Conference on Distributed Computing Systems (ICDCS), June 20, 2008, Beijing, CHINA.
Workshop on CPS Applications in Smart Power Systems, Raleigh, NC, 2011

## Slide 5: History: The Beginnings
NSF Workshop on Cyber-Physical Systems, October 16-17, 2006, Austin, TX.
National Meeting on Beyond SCADA: Networked Embedded Control for Cyber Physical Systems, November 8-9, 2006, Pittsburgh, PA.
National Workshop on High-Confidence Software Platforms for Cyber-Physical Systems (HCSP-CPS), November 30 - December 1, 2006, Alexandria, VA.
NSF Industry Round-Table on Cyber-Physical Systems, May 17, 2007, Arlington, VA.
Joint Workshop On High-Confidence Medical Devices, Software, and Systems (HCMDSS) and Medical Device Plug-and-Play (MD PnP) Interoperability, June 25-27, 2007, Boston, MA.
National Workshop on Composable Systems Technologies for High-Confidence Cyber-Physical Systems, July 9-10, 2007, Arlington, VA.
National Workshop on High-Confidence Automotive Cyber-Physical Systems, April 3-4, 2008, Troy, MI.
CPSWeek, April 21-24, 2008, St. Louis, MO.
CPS Summit, April 25, 2008, St. Louis, MO: NSF Announces new CPS Initiative
The First International Workshop on Cyber-Physical Systems, International Conference on Distributed Computing Systems (ICDCS), June 20, 2008, Beijing, CHINA.
Workshop on CPS Applications in Smart Power Systems, Raleigh, NC, 2011
Technologies

## Slide 6: History: The Beginnings
NSF Workshop on Cyber-Physical Systems, October 16-17, 2006, Austin, TX.
National Meeting on Beyond SCADA: Networked Embedded Control for Cyber Physical Systems, November 8-9, 2006, Pittsburgh, PA.
National Workshop on High-Confidence Software Platforms for Cyber-Physical Systems (HCSP-CPS), November 30 - December 1, 2006, Alexandria, VA.
NSF Industry Round-Table on Cyber-Physical Systems, May 17, 2007, Arlington, VA.
Joint Workshop On High-Confidence Medical Devices, Software, and Systems (HCMDSS) and Medical Device Plug-and-Play (MD PnP) Interoperability, June 25-27, 2007, Boston, MA.
National Workshop on Composable Systems Technologies for High-Confidence Cyber-Physical Systems, July 9-10, 2007, Arlington, VA.
National Workshop on High-Confidence Automotive Cyber-Physical Systems, April 3-4, 2008, Troy, MI.
CPSWeek, April 21-24, 2008, St. Louis, MO.
CPS Summit, April 25, 2008, St. Louis, MO: NSF Announces new CPS Initiative
The First International Workshop on Cyber-Physical Systems, International Conference on Distributed Computing Systems (ICDCS), June 20, 2008, Beijing, CHINA.
Workshop on CPS Applications in Smart Power Systems, Raleigh, NC, 2011
Applications

## Slide 7: Original Focus: Mission-critical Systems
Building Timely, Predictable, Reliable Systems

## Slide 8: Two Classical Challenges
Establish Functional Correctness: How to build functionally correct systems from possibly flawed components?
Establish Temporal Correctness: What are the analytic foundation for robust timing guarantees in highly dynamic, time-critical software systems?

## Slide 9: Two Classical Challenges
Establish Functional Correctness: How to build functionally correct systems from possibly flawed components?
Establish Temporal Correctness: What are the analytic foundation for robust timing guarantees in highly dynamic, time-critical software systems?

## Slide 10: Rate of Innovation and Development Time Issues
Near the turn of the 20th century products had a 20-30 year life-span before new “versions” were developed
At present, a product is obsolete in 2-3 years
  No time to discover and “debug” all possible problems
  New problems introduced in new versions
  Component reuse generates additional problems

## Slide 11: Software: Increasingly the Primary Cause of System Failure
Arbitrary component interactions unconstrained by physical laws of nature (algorithms can do anything)
Fast error propagation (at computing device speed)
Software that interacts with the physical world is buggy!

## Slide 12: Typical Isolation Techniques
Abstraction
Separation of concerns

## Slide 13: Typical Isolation Techniques
Abstraction
Separation of concerns
Physical
Link
Network
Transport
Abstraction
Kernel
Virtualization
Separate virtual machines or protection domains

## Slide 14: Abstraction  Solution?
Complexity
 More levels of abstraction
 Narrower specialization
 More details are “abstracted away”
 Myopic view. Less knowledge of
possible adverse interactions
 More potential for interaction
or incompatibility errors

## Slide 15: The Curse of Component Re-use The Ariane 5 Explosion
On June 4, 1996, the maiden flight of the European Ariane 5 launcher crashed about 40 seconds after takeoff (0.5 Billion Dollars)

## Slide 16: The Curse of Component Re-use The Ariane 5 Explosion
On June 4, 1996, the maiden flight of the European Ariane 5 launcher crashed about 40 seconds after takeoff (0.5 Billion Dollars)
Cause of problem?
  An inertial reference software component.
    Not needed during flight. Should be stopped before takeoff but is allowed to operate for up to 50 additional seconds to avoid expensive restarts should countdown be interrupted
    Component was designed for Ariane 4. Ariane 5 was a faster system. Velocity variable overflowed.
    Overflow causes an exception that is not caught and crashes the software

## Slide 17: Example 1: Interactive Complexity in Distributed Protocols
Interactive complexity means:
  Simple individually insignificant failures interact to compound into system failures, or even…
  Sets of correctly operating components interact to produce a system failure
    Example:
      Shortest hop routing
      Adaptive rate control

## Slide 18: Example 1:
Shortest hop routing
  Find shorter path (fewer hops that are longer)
Long wireless hops  poor channel quality
Adaptive rate control
  Reduce transmission rate to improve quality
Reduced transmission rate
 Has longer transmission range

## Slide 19: Example 2: Correlated failure modes between “independent components”
Localization (determining a node’s location) fails in a correlated manner with failure to synchronize clocks. Why?
  Note: None of the two components uses the other
Localization
Clock synchronization
Tracking

## Slide 20: Example 2: Correlated failure modes between “independent components”
Localization (determining a node’s location) fails in a correlated manner with failure to synchronize clocks. Why?
  Note: None of the two components uses the other
Answer: communication problems. Both subsystems rely on distributed protocols
Localization
Clock synchronization
Tracking
Poor performance is
Compounded by two
Correlated failures

## Slide 21: Example 3: More on hidden interactions
Magnetic tracking system operates perfectly in calm weather but fails under strong wind conditions. Why?
  Wind should not change magnetic sensor reading

## Slide 22: Example 3: More on hidden interactions
Magnetic tracking system operates perfectly in calm weather but fails under strong wind conditions. Why?
  Wind should not change magnetic sensor reading
Explanation
  Wind caused node antenna to vibrate
  Moving (metal) antenna caused a lot of noise on the magnetic sensor
  Noise filter adapted noise threshold to remove background noise (and in this case the signal too)

## Slide 23: Example 4: Three Mile Island Nuclear Reactor Failure
March 28, 1979

## Slide 24: Example 4: Three Mile Island Nuclear Reactor Failure
False alarm of minor secondary system coolant leakage through seal
Stop secondary coolant flow and turbine
Heat exchange stops between primary and secondary cooling
Systems. Primary overheats.
Open emergency feed-water pumps from emergency tank to cool coolant
Failure to open valves
Valve failure indicator light turns on but is occluded by repair tag on another device
Core overheating triggers emergency shutdown
Core temperature and pressure
continue to build up
Coolant pressure relief valve opens to reduce pressure
Pressure drops. Valve is stuck open. Coolant boils off. Core temperature rises. Reaction resumes.
Core is flooded with water
Water at very high temperature oxidizes metal fuel rod coating (rusting)
Hydrogen is released and eventually leads to explosion

## Slide 25: Ensuring Software Correctness
The physical world has no “reset” button
  When failures occur, they can be costly!
Must reduce:
  Interactive complexity
    Unexpected interactions between seemingly correct components
  Coupling
    Fast propagation of effects of failure to other system components

## Slide 26: Designing Complex Systems (Example: Air-traffic control)
Reduce interactive complexity
  Air traffic is restricted to non-intersecting “corridors” that separate flight paths in the sky
Reduce coupling
  Separate aircraft by a substantial distance to reduce cascaded failure effects (think: multiple-car pile-ups in freeway accidents)

## Slide 27: Interaction Examples
Function calls
Resource sharing
  One module crashes  overwrites memory of another  second “unrelated” module crashes (analogy to physical proximity and correlated damage)
  One module is overloaded  another starves
Timing and synchronization constraints
  Precedence constraints (one module must execute before another)
  Exclusion constraints (cannot operate at the same time)
Assumptions
  I thought you submitted our paper?
  No, I thought you did?

## Slide 28: Question: How to Build Reliable Software?
Common approaches:
  Tracing, source level debugging
  Simulation/emulation
  Log and replay

## Slide 29: Candidate Approach: Formal Methods
Express safety properties (e.g., task A will never miss its deadline)
Prove that safety properties hold
  If proof fails, counter example is presented (a sequence of events that leads to failure)
Problem:
  Proofs require axioms. Axioms may make incorrect assumptions (e.g., circular sensing range)
  Interactions must be explicitly modeled. Failure to model interactions (e.g., between wind and magnetic sensor) may overlook some failure modes.

## Slide 30: Living with Buggy Systems
If errors cannot be avoided (even using formal methods), we must design systems to tolerate them
  Architectures for “living with bugs”
  Fast diagnosis and recovery
  Issues
    Problem must be observable (or else cannot diagnose)
    Observation must be in time so that recovery is possible (observing that you forgot your parachute after you jump will not help you)

## Slide 31: Simplicity to Conquer Complexity Prof. Lui Sha UIUC
Elements of a good design
  Simple safety core
  Complex enhanced mission functionality
  Formal proof of core correctness
  Well formed dependency (core may use but will not depend on any other components)
Sha, Lui. "Using simplicity to control complexity." IEEE Software 18.4 (2001): 20-28.

## Slide 32: Diagnosis: A Development-Time Data Mining Example
Run system multiple times
Log all observable interactions (messages exchanged, resources allocated, etc)
Label execution as “correct” (no observable problems) or “incorrect” (problems observed)
Separate logs into “good” data set and “bad” data set
Look for sequences of events in the “good” pile but not the “bad” pile and vice versa

## Slide 33: Two Classical Challenges
Establish Functional Correctness: How to build functionally correct systems from possibly flawed components?
Establish Temporal Correctness: What are the analytic foundation for robust timing guarantees in highly dynamic, time-critical software systems?

## Slide 34: Real-Time Overview
Deadline=Period
Deadline<Period
Rate Monotonic
EDF
Bounds
Optimality
Result
Bound
Optimality
Result
Deadline Monotonic
EDF
Bound
(Poor)
Per Task
Tests
Simple
Recursive
Processor
Demand
Classical
Hyperbolic
Aperiodic Tasks
Real-time Tasks
Fixed-Priority
Dynamic-Priority
Polling
Slack Steal.
Priority Ex.
Deferrable
Sporadic
Total B.
Sporadic
DPE
CBS
TBS+
IPE
EDL
Periodic Tasks

## Slide 35: Real-Time Workload
Job (unit of work)
  a computation, a file read, a message transmission, etc
Attributes
  Resources required to make progress
  Timing parameters
Released
Absolute deadline
Relative deadline
Execution time

## Slide 36: Real-Time Task
Task : a sequence of similar jobs
  Periodic task (p,e)
    Its jobs repeat regularly
    Period p = inter-release time (0 < p)
    Execution time e = maximum execution time (0 < e < p)
    Utilization U = e/p
5
10
15
0

## Slide 37: Deadlines: Hard vs. Soft
Hard deadline
  Disastrous or very serious consequences may occur if the deadline is missed
  Validation is essential : can all the deadlines be met, even under worst-case scenario?
  Deterministic guarantees
Soft deadline
  Ideally, the deadline should be met for maximum performance. The performance degrades in case of deadline misses.
  Best effort approaches / statistical guarantees

## Slide 38: Schedulability
Property indicating whether a real-time system (a set of real-time tasks) can meet their deadlines
(4,1)
(5,2)
(7,2)

## Slide 39: Real-Time Scheduling
Determines the order of real-time task executions
Static-priority scheduling
Dynamic-priority scheduling
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15

## Slide 40: RM (Rate Monotonic)
Optimal static-priority scheduling
It assigns priority according to period
A task with a shorter period has a higher priority
Executes a job with the shortest period
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
T1
T2
T3

## Slide 41: RM (Rate Monotonic)
Executes a job with the shortest period
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
T1
T2
T3

## Slide 42: RM (Rate Monotonic)
Executes a job with the shortest period
(4,1)
(5,2)
(7,2)
Deadline Miss !
5
5
10
10
15
15
T1
T2
T3

## Slide 43: Response Time
Response time
  Duration from released time to finish time
(4,1)
(5,2)
(10,2)
5
5
10
10
15
15
T1
T2
T3

## Slide 44: Response Time
Response time
  Duration from released time to finish time
(4,1)
(5,2)
(10,2)
Response Time
5
5
10
10
15
15
T1
T2
T3

## Slide 45: Response Time
Response Time (ri) [Audsley et al., 1993]
HP(Ti) : a set of higher-priority tasks than Ti
(4,1)
(5,2)
(10,2)
5
5
10
10
T1
T2
T3

## Slide 46: RM - Schedulability Analysis
Real-time system is schedulable under RM
if and only if ri ≤ pi for all task Ti(pi,ei)
Joseph & Pandya,
“Finding response times in a real-time system”,
The Computer Journal, 1986.

## Slide 47: RM – Utilization Bound
Real-time system is schedulable under RM if
∑Ui ≤ n (21/n-1)
Liu & Layland,
“Scheduling algorithms for multi-programming in a hard-real-time environment”, Journal of ACM, 1973.

## Slide 48: RM – Utilization Bound
Real-time system is schedulable under RM if
∑Ui ≤ n (21/n-1)
Example: T1(4,1), T2(5,1), T3(10,1),
∑Ui = 1/4 + 1/5 + 1/10
= 0.55
3 (21/3-1) ≈ 0.78
Thus, {T1, T2, T3} is schedulable under RM.

## Slide 49: RM – Utilization Bound
Real-time system is schedulable under RM if ∑Ui ≤ n (21/n-1)
Example: T1(4,1), T2(5,2), T3(7,2),
∑Ui = 1/4 + 2/5 + 2/7
≈ 0.94
3 (21/3-1) ≈ 0.78
Thus, {T1, T2, T3} is NOT schedulable under RM.

## Slide 50: RM – Utilization Bound
Real-time system is schedulable under RM if
∑Ui ≤ n (21/n-1)
Example: T1(4,1), T2(5,2), T3(10,2),
∑Ui = 1/4 + 2/5 + 2/10
= 0.85
3 (21/3-1) ≈ 0.78
However, {T1, T2, T3} is still schedulable under RM (as we just showed) even their total utilization is higher than the bound!

## Slide 51: RM – Utilization Bound
Real-time system is schedulable under RM if (but not only if) ∑Ui ≤ n (21/n-1)
The above condition is only a sufficient but not necessary condition!
  We only know tasks with utilization lower than the bound is guaranteed to be schedulable under RM.
  We know nothing about tasks with higher utilization!

## Slide 52: RM – Utilization Bound
Real-time system is schedulable under RM if
∑Ui ≤ n (21/n-1)

## Slide 53: EDF (Earliest Deadline First)
Optimal dynamic priority scheduling
A task with a shorter deadline has a higher priority
Executes a job with the earliest deadline
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
T1
T2
T3

## Slide 54: EDF (Earliest Deadline First)
Executes a job with the earliest deadline
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
T1
T2
T3

## Slide 55: EDF (Earliest Deadline First)
Executes a job with the earliest deadline
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
T1
T2
T3

## Slide 56: EDF (Earliest Deadline First)
Executes a job with the earliest deadline
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
T1
T2
T3

## Slide 57: EDF (Earliest Deadline First)
Optimal scheduling algorithm
  if there is a schedule for a set of real-time tasks,
  EDF can schedule it.
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
T1
T2
T3

## Slide 58: EDF – Utilization Bound
Real-time system is schedulable under EDF if and only if
∑Ui ≤ 1
Liu & Layland,
“Scheduling algorithms for multi-programming in a hard-real-time environment”, Journal of ACM, 1973.

## Slide 59: EDF – Overload Conditions
Domino effect during overload conditions
  Example: T1(4,3), T2(5,3), T3(6,3), T4(7,3)
T1
5
0
7
T2
T3
T4
3
6
Deadline Miss !
T1
5
0
7
T3
3
6
Better schedules :
T1
5
0
7
T4
3
6

## Slide 60: RM vs. EDF
Rate Monotonic
  Simpler implementation, even in systems without explicit support for timing constraints (periods, deadlines)
  Predictability for the highest priority tasks
EDF
  Full processor utilization
  Misbehavior during overload conditions
For more details: Buttazzo, “Rate monotonic vs. EDF: Judgement Day”, EMSOFT 2003.

## Slide 61: Real-world Example: What Happens on Mars?
Prof. Lui Sha, CS, UIUC
http://research.microsoft.com/en-us/um/people/mbj/Mars_Pathfinder/Mars_Pathfinder.html

## Slide 62: The Problem
Tasks have synchronization constraints
  Semaphores protect critical sections
Blocking can cause a higher-priority task to wait on an lower-priority one to unlock the resource
  Problem: In all previous scheduling examples, we assumed that a task can only wait for higher priority tasks not lower-priority tasks

## Slide 63: Mutual Exclusion Constraints
Tasks that lock/unlock the same semaphore are said to have a mutual exclusion constraint
Task 1
Task 2
Critical Sections (Mutually exclusive)
Lock S
Unlock S
Lock S
Unlock S

## Slide 64: Priority Inversion
Locks and priorities may be at odds. Locking results in priority inversion.
Lock S
Preempt
High-priority Task
Low-priority Task

## Slide 65: Priority Inversion
Locks and priorities may be at odds. Locking results in priority inversion.
Lock S
Preempt
Attempt to Lock S but results in blocking
Priority Inversion
High-priority Task
Low-priority Task

## Slide 66: Priority Inversion
How to account for priority inversion?
Lock S
Preempt
Attempt to Lock S but results in blocking
Priority Inversion
Unlock S
Lock S
Unlock S
High-priority Task
Low-priority Task

## Slide 67: Priority Inversion
What is the problem of this scheme? Can the high-priority task gets delayed unboundedly?
Lock S
Preempt
Attempt to Lock S but results in blocking
Priority Inversion
Unlock S
Lock S
Unlock S
High-priority Task
Low-priority Task

## Slide 68: Unbounded Priority Inversion
Consider the following: a series of intermediate priority tasks is delaying a higher-priority one
High-priority Task
Lock S
Preempt
Attempt to Lock S but results in blocking
Unlock S
Unbounded priority inversion
Low-priority Task
Intermediate-priority Task
Preempt
…..

## Slide 69: Unbounded Priority Inversion
Consider the following: a series of intermediate priority tasks is delaying a higher-priority one
High-priority Task
Lock S
Preempt
Attempt to Lock S but results in blocking
Unlock S
Unbounded priority inversion
Low-priority Task
Intermediate-priority Task
Preempt
…..
The root cause of the Mars Pathfinder restarting problem!

## Slide 70: Unbounded Priority Inversion
How to prevent unbounded priority inversion?
High-priority Task
Lock S
Preempt
Attempt to Lock S but results in blocking
Unlock S
Unbounded priority inversion
Low-priority Task
Intermediate-priority Task
Preempt
…..

## Slide 71: Priority Inheritance Protocol
Let a task inherit the priority of any higher priority task it is blocking
High-priority Task
Lock S
Preempt
Attempt to Lock S but results in blocking
Unlock S
Low-priority Task
Intermediate-priority Task
Priority Inherit

## Slide 72: Deadlocks in PIP
J1 = {..., P(S2) ..., P(S1),...,V(S1) ...,V(S2),...}
J2 = {..., P(S1) ..., P(S2),...,V(S2) ...,V(S1),...}
lock S1
time
preempt J2
lock S2
(try to lock S1)
blocked by J2
(try to lock S2)
blocked by J1
crossing nested semaphores
deadlock!

## Slide 73: Blocking Chains in PIP
J1 = {..., P(S1), ..., V(S1), ..., P(S2), ..., V(S2), ...}
J2 = {..., P(S2) , ..., V(S2), ...}
J3 = {..., P(S1) , ..., V(S1), ...}
time
preempt J3
(attempt to lock S1)
blocked by J3
complete
(attempt to lock S2)
blocked by J2
unlock
S1
unlock
S2
unlock S2
lock
S2
lock
S1
lock
S1
unlock
S1
lock
S2
t0
t1
t2
t3
t4
t5
t6
t7
t8
t9
t10
t11
t12
t13
complete
complete

## Slide 74: Priority Ceiling Protocol (PCP)
Goals:
  Solve problems of PIP.
    Prevent deadlocks and blocking chains
Basic idea:
  Priority ceiling of a semaphore:
    The priority of the highest priority task that may use the semaphore
  Additional condition for allowing a job J to start a new critical section
    only if J’s priority is higher than all priority ceilings of all the semaphores locked by jobs other than J .
Notes: The key thing of priority ceiling is to make sure nobody is using the thing you will use in your job execution. In other words, make sure the job has every semaphore it needs (not used by anyone) to finish its execution.

## Slide 75: Examples for PCP (1/2)
Prevent deadlocks
J1 = {..., P(S0) ..., V(S0),...}
J2 = {..., P(S1) ..., P(S2),...,V(S2) ...,V(S1),...}
J3 = {..., P(S2) ..., P(S1),...,V(S1) ...,V(S2),...}
lock S2
time
preempt J3
complete
complete
unlock S2
unlock S1
lock S1
lock S2
unlock S1
lock S0
(attempt to lock S1)
blocked by J3
complete
lock S1
unlock S2
preempt J3
unlock S0
nested crossing semaphores
Ceiling(S0)= H
Ceiling(S1)= M
Ceiling(S2)= M

## Slide 76: Real-Time Overview
Deadline=Period
Deadline<Period
Rate Monotonic
EDF
Bounds
Optimality
Result
Bound
Optimality
Result
Deadline Monotonic
EDF
Bound
(Poor)
Per Task
Tests
Simple
Recursive
Processor
Demand
Classical
Hyperbolic
Aperiodic Tasks
Real-time Tasks
Fixed-Priority
Dynamic-Priority
Polling
Slack Steal.
Priority Ex.
Deferrable
Sporadic
Total B.
Sporadic
DPE
CBS
TBS+
IPE
EDL
Periodic Tasks

## Slide 77: Further Reading
Buttazzo, Giorgio C. Hard real-time computing systems: predictable scheduling algorithms and applications. Vol. 24. Springer, 2011.

## Slide 78: Open Cyber-Physical Systems
Hard Real-time
Non Real-time
Safety-critical
Non-critical

## Slide 79: Open Cyber-Physical Systems
Hard Real-time
Non Real-time
Safety-critical
Non-critical
Most
Embedded
Systems
Research
Model checking
Formal verification
Worst-case analysis
Certification

## Slide 80: Open Cyber-Physical Systems
Hard Real-time
Non Real-time
Safety-critical
Non-critical
Most
Embedded
Systems
Research
A Proliferation
of Networked Open
Cyber-physical Systems
Model checking
Formal verification
Worst-case analysis
Certification

## Slide 81: Open Cyber-Physical Systems
Hard Real-time
Non Real-time
Safety-critical
Non-critical
Most
Embedded
Systems
Research
A Proliferation
of Networked Open
Cyber-physical Systems
Challenges?

## Slide 82: Open Cyber-Physical Systems
Hard Real-time
Non Real-time
Safety-critical
Non-critical
Most
Embedded
Systems
Research
A Proliferation
of Networked Open
Cyber-physical Systems
Challenges?
- Data reliability
- Large scale
- Distributed ownership
- Imprecise/Incomplete models

## Slide 83: Personalized Healthcare
Wearable and Ambient Sensors: Opportunistic Context Measurement
Implantable
Medical Devices, Biosensors
Biological
System
Biometric
Sensing
Context and
Activity Sensing,
NEAT-factor, etc.
Logging
Logging
Community/Social
Network
Direct
Control
Context Factors,
Bio-feedback
Sanitized
Community
Data
Personal Data
Services
Social
Factors
Bio-loops
Medical care
services
Care Providers,
Physicians
Comparative
Analysis
Smart Tattoos

## Slide 84: Body-Area Networks
Point of Care
Devices
Bio-feedback Sensors
Implanted Sensors
Insulin pumps, pacemakers, glucose monitors, …
Smart Spaces
Wearable Activity
and Biometric Monitoring
Micro- and Nano-sensors, Biochips
Transparent
Testing

## Slide 85: Crowd-sensing Browsing the Physical World Feng Zhao http://research.microsoft.com/en-us/projects/senseweb/

## Slide 86
Signal data
Visual data
Human data
Extract objects and linkages
Information Network
Optimize resource allocation
Sensors, witnesses, sources, …
Information
High QoI,
Quantifiable uncertainty
Prioritized
Situation-awareness
Extract objects and linkages
Feedback
to sensor and communication networks
Social networks
Military Situation Awareness Applications
Notes: 86
86
86

## Slide 87: An Architecture for Open CPS
Critical Services

## Slide 88: An Architecture for Open CPS
Critical Services
Mobiles

## Slide 89: An Architecture for Open CPS
Critical Services
Mobiles
Sensors

## Slide 90: An Architecture for Open CPS
Critical Services
Mobiles
Sensors
People

## Slide 91: Publication Venues
Cyber-physical systems
  International conference on cyber-physical systems (ICCPS)
  CPSWeek (http://www.cpsweek.org)
Real-time systems
  IEEE Real-time systems symposium (IEEE RTSS)
  IEEE Real-time applications symposium (IEEE RTAS)
  Springer Journal on Real-time Systems
Embedded systems
  International conference on embedded software (EmSoft)
  ACM Transactions on Embedded Computing Systems (ACM TECS)
Networked sensing
  ACM Sensys (http://sensys.acm.org/2014/index.html)
  ACM/IEEE IPSN (http://ipsn.acm.org/2015/)
  ACM Transactions on Sensor Networks (ACM ToSN)

## Slide 92: Publication Venues (Cont.)
Data Analytics, Mining and Processing
  ACM KDD Conference on Knowledge Discovery and Data Mining (http://www.kdd.org/kdd2015/)
  IEEE International Conference on Data Mining (ICDE) (http://icdm2014.sfu.ca/home.html)
  ACM International Conference on Web Search and Data Mining (http://www.wsdm-conference.org/2015/)
  International World Wide Web Conference (WWW) (http://www.www2015.it/ )
  IEEE Transactions on Knowledge and Data Engineering (TKDE) (http://www.computer.org/portal/web/tkde)

## Slide 93: Education Venues
Nano-Tera/Artist Summer School on Embedded System Design
  http://artist-summer-school.epfl.ch/
Georgia Tech Summer School on Cyber Physical Systems
  http://users.ece.gatech.edu/~magnus/CPSschool.html

## Slide 94: The CPS Research Landscape (An Incomplete List, Alphabetic)
Berkeley (architecture, control, automotive, sensor networks, …):
  http://chess.eecs.berkeley.edu/
CMU (real-time, automotive, …):
  http://users.ece.cmu.edu/~raj/
Notre Dame (social sensing, CPS in social space)
  http://www3.nd.edu/~dwang5/
UIUC (avionics, human-centric, medical, …)
  http://publish.illinois.edu/cpsintegrationlab/
U. of Pennsylvania (composability, medical, …)
  http://precise.seas.upenn.edu/
University of Virginia (sensor networks, real-time, …)
  http://www.cs.virginia.edu/~stankovic/rts.html
Vanderbilt (composition, control, …)
  http://www.isis.vanderbilt.edu/research/NES

## Slide 95: Pointers and Readings
"Opportunities and Obligations for Physical Computing Systems", Computer, Volume 38, Issue 11, November 2005, pages 23-31. (Report produced by a Workshop at the IEEE Real-Time Systems Symposium, December 2003).
http://repository.upenn.edu/cis_papers/222/
"High Confidence Medical Device Software and Systems (HCMDSS)" Workshop, June 2 - 3, 2005, Philadelphia, PA.
http://rtg.cis.upenn.edu/hcmdss/index.php3
National Workshop on "Aviation Software Systems: Design for Certifiably Dependable Systems", October 5-6, 2006, Alexandria, TX
http://chess.eecs.berkeley.edu/hcssas/index.html
NSF Workshop on "Cyber-Physical Systems", October 16-17, 2006, Austin, TX.
http://varma.ece.cmu.edu/CPS
National Workshop on "High-Confidence Software Platforms for Cyber-Physical Systems (HCSP-CPS)", November 30 - December 1, 2006, Alexandria, VA.
http://www.isis.vanderbilt.edu/HCSP-CPS/

## Slide 96: Pointers and Readings
"Joint Workshop On High-Confidence Medical Devices, Software, and Systems (HCMDSS) and Medical Device Plug-and-Play (MD PnP) Interoperability", June 25-27, 2007, Boston, MA.
http://rtg.cis.upenn.edu/hcmdss07/index.php3
National Workshop on "Composable and Systems Technologies for High-Confidence Cyber-Physical Systems", July 9-10, 2007, Arlington, VA.
http://www.isis.vanderbilt.edu/CST-HCCPS/
National Workshop on "High-Confidence Automotive Cyber-Physical Systems", Apr 3-4, 2008, Troy, MI.
http://varma.ece.cmu.edu/Auto-CPS/
CPSWeek, 2008-present
http://www.cpsweek.org/
CPS Summit, April 25, 2008, St. Louis, MO, USA.
http://varma.ece.cmu.edu/Summit
National Workshop on "Research on Transportation Cyber-Physical Systems: Automotive, Aviation, and Rail", November 18-20, 2008, Washington, DC (USA).
http://www.ee.washington.edu/research/nsl/aar-cps