## Slide 1
1
Y86-64 Instructions
8-byte integer operations (no floating point!)  “word” (it is considered a quad word for historical reasons, because the original architecture was 16 bit!)
Format
  - 1–10 bytes of information read from memory
    - Can determine the type of instruction from first byte
    - Can determine instruction length from first byte
Registers
  - rA or rB represent one of the registers (0-14)
  - 0xF denotes no register (when needed)
  - No partial register options (must be a byte)
Notes: No floating point registers or instructions
1

## Slide 2: Y86-64 Move Instruction
Split into four different instructions
Explicitly indicates form of source (1st char of instruction name) and destination (2nd char of instruction name)
  Immediate (i)
  Register (r)
  Memory (m) – base + displacement format
Either Source, Destination or both must be a register
rrmovq rA, rB
2
0
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D

## Slide 3: Move Operations
irmovq is used to place known numeric values (labels or numeric literals) into a register
rrmovq copies a value between registers
rmmovq stores a word in memory
mrmovq loads a word from memory
rmmovq and mrmovq are the only instructions that access memory – Y86 is a load/store architecture
Direct transfers from one memory location to another are not allowed
Transfer of immediate data to memory is not allowed

## Slide 4
Assembly Syntax
AT&T  What Y86 assembler uses
  - Immediate values preceded by $
  - Registers are prefixed with %
  - Moves and ALU operations are source, destination:
    movq $5, %rax
  - Effective address DISP(BASE)

## Slide 5
Simple Addressing Modes
5
Normal = (R) = Mem[Reg[R]]
  - Register Reg contents specify memory address
  - Example: mrmovq (%rcx),%rax
Displacement = D(R) = Mem[Reg[R]+D]
  - Register R contents specify start of memory region
  - Constant displacement D specifies offset
    -In bytes
  - Example: mrmovq 8(%rbx),%rdx

## Slide 6
6
Run Y86 program
irmovq $55,%rdx
rrmovq %rdx, %rbx
irmovq Array, %rax
rmmovq %rbx,8(%rax)
mrmovq 0(%rax),%rcx
halt
.align 8
Array:
.long 0x6f
.long 0x84
% yas y86prog1.ys
% yis y86prog1.yo
Stopped in 6 steps at PC = 0x2a.
Status 'HLT‘, CC Z=1 S=0 O=0
Changes to registers:
%rax: 0x0000000000000000 0x0000000000000030
%rcx: 0x0000000000000000 0x000000840000006f
%rdx: 0x0000000000000000 0x0000000000000037
%rbx: 0x0000000000000000 0x0000000000000037
Changes to memory:
0x0038: 0x0000000000000000 0x0000000000000037
Notes: a[1]=55
c=a[0]
6

## Slide 7
7
Run Y86 program
irmovq $55,%rdx
rrmovq %rdx, %rbx
Irmovq $0x33, %r8
irmovq Array, %rax
rmmovq %rbx,8(%rax)
rmmovq %rax,0(%rax)
mrmovq 0(%rax),%rcx
halt
.align 8
Array:
.long 0x6f
.long 0x84
.long 0x55
.long 0x44
% yas y86prog1.ys
% yis y86prog1.yo
Stopped in 8 steps at PC = 0x3e.
Status 'HLT‘, CC Z=1 S=0 O=0
Changes to registers:
%rax: 0x0000000000000000 0x0000000000000040
%rcx: 0x0000000000000000 0x0000000000000040
%rdx: 0x0000000000000000 0x0000000000000037
%rbx: 0x0000000000000000 0x0000000000000037
%r8: 0x0000000000000000 0x0000000000000033
Changes to memory:
0x0040: 0x0000840000006f 0x0000000000000040
0x0048: 0x00004400000055 0x0000000000000037
Notes: a[1]=55
c=a[0]
7

## Slide 8: Conditional Move Operation
Based on values of condition codes
All are based on the form: cmovXX, where XX can be “le”, “l” “e”, “ne”, “ge” or “g”.
All conditional moves are between 2 register locations
cmovle copies a value from the source register to a destination register when the condition codes satisfies less than or equal (SF=1 OR ZF=1)
cmovl copies a value from the source register to a destination register when the condition code satisfies less than (SF = 1 AND ZF = 0)
cmove copies a value from the source register to a destination register when the condition code satisfies equal(ZF = 1)
cmovne copies a value from the source register to a destination register when the condition code satisfies not equal (ZF = 0)
cmovge copies a value from the source register to a destination register when the condition code satisfies greater than or equal (SF = 0 OR ZF = 1)
cmovg copies a value from the source register to a destination register when the condition code satisfies greater than (SF = 0 AND ZF = 0)

## Slide 9
9
Supported ALU Operations
Arithmetic instructions
  - addq rA, rB R[rB] ← R[rB] + R[rA]
  - subq rA, rB R[rB] ← R[rB] − R[rA]
  - andq rA, rB R[rB] ← R[rB] & R[rA]
  - xorq rA, rB R[rB] ← R[rB] ^ R[rA]
# y86prog2.ys
.pos 0x0
irmovq $1, %rax
irmovq $0, %rbx
irmovq $1, %rcx
addq %rax, %rax
andq %rbx, %rbx
subq %rax, %rcx
irmovq $0x7fffffffffffffff, %rdx
addq %rdx, %rdx
halt
% yas y86prog2.ys
% yis y86prog2.yo
Stopped in 9 steps at PC = 0x2a.
Status 'HLT‘, CC Z=0 S=1 O=1
Changes to registers:
%rax: 0x0000000000000000 0x0000000000000002
%rcx: 0x0000000000000000 0xffffffffffffffff
%rdx: 0x0000000000000000 0xfffffffffffffffe
Changes to memory:
Notes: Notice & ^ are bit operations
Watch out for subl command – correct order very important!
What are the CC bits for each instruction for the example code?
9

## Slide 10: Y86-64 Instruction Set #1
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9

## Slide 11: Y86-64 Instructions
Format
  1–10 bytes of information read from memory
    Can determine instruction length from first byte
    Not as many instruction types, and simpler encoding than with x86-64
  Each accesses and modifies some part(s) of the program state

## Slide 12: Y86-64 Instruction Set #2
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovq
7
0
cmovle
7
1
cmovl
7
2
cmove
7
3
cmovne
7
4
cmovge
7
5
cmovg
7
6

## Slide 13: Y86-64 Instruction Set #3
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
addq
6
0
subq
6
1
andq
6
2
xorq
6
3

## Slide 14: Y86-64 Instruction Set #4
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 15: Encoding Registers
Each register has 4-bit ID
  Same encoding as in x86-64
Register ID 15 (0xF) indicates “no register”
  Will use this in our hardware design in multiple places
%rax
%rcx
%rdx
%rbx
0
1
2
3
%rsp
%rbp
%rsi
%rdi
4
5
6
7
%r8
%r9
%r10
%r11
8
9
A
B
%r12
%r13
%r14
No Register
C
D
E
F

## Slide 16: Instruction Example
Addition Instruction
  Add value in register rA to that in register rB
    Store result in register rB
    Note that Y86-64 only allows addition to be applied to register data
  Set condition codes based on result
  e.g., addq %rax,%rsi Encoding: 60 06
  Two-byte encoding
    First indicates instruction type
    Second gives source and destination registers
addq rA, rB
6
0
rA
rB
Encoded Representation
Generic Form

## Slide 17: Arithmetic and Logical Operations
  Refer to generically as “OPq”
  Encodings differ only by “function code”
    Low-order 4 bytes in first instruction word
  Set condition codes as side effect
addq rA, rB
6
0
rA
rB
subq rA, rB
6
1
rA
rB
andq rA, rB
6
2
rA
rB
xorq rA, rB
6
3
rA
rB
Add
Subtract (rA from rB)
And
Exclusive-Or
Instruction Code
Function Code

## Slide 18: Move Operations
  Like the x86-64 movq instruction
  Simpler format for memory addresses
  Give different names to keep them distinct
rrmovq rA, rB
2
0
Register  Register
Immediate  Register
irmovq V, rB
F
rB
3
0
V
Register  Memory
rmmovq rA, D(rB)
4
0
rA
rB
D
Memory  Register
mrmovq D(rB), rA
5
0
rA
rB
D

## Slide 19: Move Instruction Examples
irmovq $0xabcd, %rdx
movq $0xabcd, %rdx
30 82 cd ab 00 00 00 00 00 00
X86-64
Y86-64
Encoding:
rrmovq %rsp, %rbx
movq %rsp, %rbx
20 43
mrmovq -12(%rbp),%rcx
movq -12(%rbp),%rcx
50 15 f4 ff ff ff ff ff ff ff
rmmovq %rsi,0x41c(%rsp)
movq %rsi,0x41c(%rsp)
40 64 1c 04 00 00 00 00 00 00
Encoding:
Encoding:
Encoding:

## Slide 20: Conditional Move Instructions
  Refer to generically as “cmovXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Variants of rrmovq instruction
    (Conditionally) copy value from source to destination register
rrmovq rA, rB
Move Unconditionally
cmovle rA, rB
Move When Less or Equal
cmovl rA, rB
Move When Less
cmove rA, rB
Move When Equal
cmovne rA, rB
Move When Not Equal
cmovge rA, rB
Move When Greater or Equal
cmovg rA, rB
Move When Greater
2
0
rA
rB
2
1
rA
rB
2
2
rA
rB
2
3
rA
rB
2
4
rA
rB
2
5
rA
rB
2
6
rA
rB

## Slide 21: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code” fn
  Based on values of condition codes
  Same as x86-64 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in x86-64
jXX Dest
7
fn
Jump (Conditionally)
Dest

## Slide 22: Jump Instructions
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 23: Y86-64 Program Stack
  Region of memory holding program data
  Used in Y86-64 (and x86-64) for supporting procedure calls
  Stack top indicated by %rsp
    Address of top stack element
  Stack grows toward lower addresses
    Top element is at highest address in the stack
    When pushing, must first decrement stack pointer
    After popping, increment stack pointer
%rsp
•
•
•
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 24: Stack Operations
  Decrement %rsp by 8
  Store word from rA to memory at %rsp
  Like x86-64
  Read word from memory at %rsp
  Save in rA
  Increment %rsp by 8
  Like x86-64
pushq rA
A
0
rA
F
popq rA
B
0
rA
F

## Slide 25: Subroutine Call and Return
  Push address of next instruction onto stack
  Start executing instructions at Dest
  Like x86-64
  Pop value from stack
  Use as address for next instruction
  Like x86-64
call Dest
8
0
Dest
ret
9
0

## Slide 26: Miscellaneous Instructions
  Don’t do anything
  Stop executing instructions
  x86-64 has comparable instruction, but can’t execute it in user mode
  We will use it to stop the simulator
  Encoding ensures that program hitting memory initialized to zero will halt
nop
1
0
halt
0
0

## Slide 27: Status Conditions
Mnemonic | Code
ADR | 3
Mnemonic | Code
INS | 4
Mnemonic | Code
HLT | 2
Mnemonic | Code
AOK | 1
  Normal operation
  Halt instruction encountered
  Bad address (either instruction or data) encountered
  Invalid instruction encountered
Desired Behavior
  If AOK, keep going
  Otherwise, stop program execution

## Slide 28: Writing Y86-64 Code
Try to Use C Compiler as Much as Possible
  Write code in C
  Compile for x86-64 with gcc –Og –S
  Transliterate into Y86-64
  Modern compilers make this more difficult
Coding Example
  Find number of elements in null-terminated list
    int len1(int a[]);
5043
6125
7395
0
a
 3

## Slide 29: Y86-64 Code Generation Example
First Try
  Write typical array code
  Compile with gcc -Og -S
Problem
  Hard to do array indexing on Y86-64
    Since don’t have scaled addressing modes
/* Find number of elements in
null-terminated list */
long len(long a[])
{
long len;
for (len = 0; a[len]; len++)
;
return len;
}
L3:
addq $1,%rax
cmpq $0, (%rdi,%rax,8)
jne L3

## Slide 30: Y86-64 Code Generation Example #2
Second Try
  Write C code that mimics expected Y86-64 code
Result
  Compiler generates exact same code as before!
  Compiler converts both versions into same intermediate form
long len2(long *a)
{
long ip = (long) a;
long val = *(long *) ip;
long len = 0;
while (val) {
ip += sizeof(long);
len++;
val = *(long *) ip;
}
return len;
}

## Slide 31: Y86-64 Code Generation Example #3
len:
irmovq $1, %r8 # Constant 1
irmovq $8, %r9 # Constant 8
irmovq $0, %rax # len = 0
mrmovq (%rdi), %rdx # val = *a
andq %rdx, %rdx # Test val
je Done # If zero, goto Done
Loop:
addq %r8, %rax # len++
addq %r9, %rdi # a++
mrmovq (%rdi), %rdx # val = *a
andq %rdx, %rdx # Test val
jne Loop # If !0, goto Loop
Done:
ret
Register | Use
%rdi | a
%rax | len
%rdx | val
%r8 | 1
%r9 | 8

## Slide 32: Y86-64 Sample Program Structure #1
  Program starts at address 0
  Must set up stack
    Where located
    Pointer values
    Make sure don’t overwrite code!
  Must initialize data
init: # Initialization
. . .
call Main
halt
.align 8 # Program data
array:
. . .
Main: # Main function
. . .
call len . . .
len: # Length function
. . .
.pos 0x100 # Placement of stack
Stack:

## Slide 33: Y86-64 Program Structure #2
  Program starts at address 0
  Must set up stack
  Must initialize data
  Can use symbolic names
init:
# Set up stack pointer
irmovq Stack, %rsp
# Execute main program
  call Main
  # Terminate
  halt
# Array of 4 elements + terminating 0
.align 8
Array:
.quad 0x000d000d000d000d
  .quad 0x00c000c000c000c0
.quad 0x0b000b000b000b00
.quad 0xa000a000a000a000
.quad 0

## Slide 34: Y86-64 Program Structure #3
Set up call to len
  Follow x86-64 procedure conventions
  Push array address as argument
Main:
irmovq array,%rdi
# call len(array)
call len
ret

## Slide 35: Assembling Y86-64 Program
  Generates “object code” file len.yo
    Actually looks like disassembler output
  unix> yas len.ys
  0x054: | len:
  0x054: 30f80100000000000000 | irmovq $1, %r8 # Constant 1
  0x05e: 30f90800000000000000 | irmovq $8, %r9 # Constant 8
  0x068: 30f00000000000000000 | irmovq $0, %rax # len = 0
  0x072: 50270000000000000000 | mrmovq (%rdi), %rdx # val = *a
  0x07c: 6222 | andq %rdx, %rdx # Test val
  0x07e: 73a000000000000000 | je Done # If zero, goto Done
  0x087: | Loop:
  0x087: 6080 | addq %r8, %rax # len++
  0x089: 6097 | addq %r9, %rdi # a++
  0x08b: 50270000000000000000 | mrmovq (%rdi), %rdx # val = *a
  0x095: 6222 | andq %rdx, %rdx # Test val
  0x097: 748700000000000000 | jne Loop # If !0, goto Loop
  0x0a0: | Done:
  0x0a0: 90 | ret

## Slide 36: Simulating Y86-64 Program
  Instruction set simulator
    Computes effect of each instruction on processor state
    Prints changes in state from original
  unix> yis len.yo
  Stopped in 33 steps at PC = 0x13. Status 'HLT', CC Z=1 S=0 O=0
  Changes to registers:
  %rax: 0x0000000000000000 0x0000000000000004
  %rsp: 0x0000000000000000 0x0000000000000100
  %rdi: 0x0000000000000000 0x0000000000000038
  %r8: 0x0000000000000000 0x0000000000000001
  %r9: 0x0000000000000000 0x0000000000000008
  Changes to memory:
  0x00f0: 0x0000000000000000 0x0000000000000053
  0x00f8: 0x0000000000000000 0x0000000000000013

## Slide 37: CISC Instruction Sets
  Complex Instruction Set Computer
  IA32 is example
Stack-oriented instruction set
  Use stack to pass arguments, save program counter
  Explicit push and pop instructions
Arithmetic instructions can access memory
  addq %rax, 12(%rbx,%rcx,8)
    requires memory read and write
    Complex address calculation
Condition codes
  Set as side effect of arithmetic and logical instructions
Philosophy
  Add instructions to perform “typical” programming tasks

## Slide 38: RISC Instruction Sets
  Reduced Instruction Set Computer
  Internal project at IBM, later popularized by Hennessy (Stanford) and Patterson (Berkeley)
Fewer, simpler instructions
  Might take more to get given task done
  Can execute them with small and fast hardware
Register-oriented instruction set
  Many more (typically 32) registers
  Use for arguments, return pointer, temporaries
Only load and store instructions can access memory
  Similar to Y86-64 mrmovq and rmmovq
No Condition codes
  Test instructions return 0/1 in register

## Slide 39: MIPS Registers

## Slide 40: MIPS Instruction Examples
Op
Ra
Rb
Offset
Op
Ra
Rb
Rd
Fn
00000
R-R
Op
Ra
Rb
Immediate
R-I
Load/Store
addu $3,$2,$1 # Register add: $3 = $2+$1
addu $3,$2, 3145 # Immediate add: $3 = $2+3145
sll $3,$2,2 # Shift left: $3 = $2 << 2
lw $3,16($2) # Load Word: $3 = M[$2+16]
sw $3,16($2) # Store Word: M[$2+16] = $3
Op
Ra
Rb
Offset
Branch
beq $3,$2,dest # Branch when $3 = $2

## Slide 41: CISC vs. RISC
Original Debate
  Strong opinions!
  CISC proponents---easy for compiler, fewer code bytes
  RISC proponents---better for optimizing compilers, can make run fast with simple chip design
Current Status
  For desktop processors, choice of ISA not a technical issue
    With enough hardware, can make anything run fast
    Code compatibility more important
  x86-64 adopted many RISC features
    More registers; use them for argument passing
  For embedded processors, RISC makes sense
    Smaller, cheaper, less power
    Most cell phones use ARM processor

## Slide 42: Summary
Y86-64 Instruction Set Architecture
  Similar state and instructions as x86-64
  Simpler encodings
  Somewhere between CISC and RISC
How Important is ISA Design?
  Less now than before
    With enough hardware, can make almost anything go fast