## Slide 1: The link layer – Switched LANs and More
LANs and virtual LANs
MPLS
Data center networks
Slides partially based on J. Kurose and K. Ross, “Computer Networking: A Top Down Approach”, 7Ed., 2016

## Slide 2: Forwarding within a switched local area network
A set of machines within a small unit, like a lab or a department, are interconnected by a layer-2 switch
  Working at the link layer, don’t recognize network addresses (IPs)
  They switch link-layer frames rather than datagrams
  And don’t use RIP or OSPF for routing
How do they forward frames then?
  Host and routers, or rather their adapters (network i/f) have a link-layer address
  a.k.a LAN, physical or MAC address
  Link-layer switches’ interfaces don’t have a MAC, they are there to connect hosts and routers transparently
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
Adapter
LAN (wired or wireless)

## Slide 3: MAC addresses
Network layer address or IP address
  32 bits for IPv4
  Hierarchical, if the machine moves networks the address changes
MAC address
  Flat structure, used “locally” to get frame from one interface to another physically-connected interface (same network, in an IP-addressing sense)
  6 bytes burned in NIC ROM, sometimes software settable
  e.g.: 1A-23-F9-CD-0C-9B
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)

## Slide 4: MAC address and ARP [RFC 826]
To ensure no two adapters have the same, allocation administered by IEEE
  Manufacturer buys portion (24b) of MAC address space
Analogy
  MAC address ~ Passport number – same one wherever you are
  IP address ~ postal address – depends on IP subnet to which node is attached
Since we have both, we need a protocol to translate between them – Address Resolution Protocol
  Like DNS, which translates host names to IP addresses, but within the same LAN

## Slide 5: ARP: address resolution protocol
Each host and router has an ARP table in memory
  IP/MAC address mappings for some LAN nodes: < IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
  Not necessarily includes every host and router on the subnet
So, what if it doesn’t have an entry for a given destination you need?
71-65-F7-2B-08-53
IP: 137.196.7.23
IP: 137.196.7.78
IP: 137.196.7.14
IP: 137.196.7.88
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
Adapter
LAN (wired or wireless)
IP | MAC | TTL
137.196.7.78 | 1A-2F-BB-76-09-AD | 12:45:00
137.196.7.14 | 58-23-D7-FA-20-89 | 17:52:00

## Slide 6: ARP protocol (in the same LAN)
A wants to send datagram to B
  B’s MAC address not in A’s ARP table
  A broadcasts ARP query packet, containing B's IP address
    Destination MAC address = FF-FF-FF-FF-FF-FF
    All nodes on LAN receive ARP query
  B receives ARP packet, replies to A with its (B's) MAC address
    Response frame sent to A’s MAC address (unicast)
  A caches IP-to-MAC address pair in its ARP table until info is too old
ARP is “plug-and-play” – nodes create their ARP tables without intervention from net administrator
ARP logically straddles between the link and network layers
  Encapsulated within a frame, with link-layer addresses in it …
Notes: ARP logically between layers – ARP packet is encapsulated within a link-layer frame and thus lies above the link layer
However, an ARP packet has fields containing link-layer addresses and thus s a link-layer protocol …but also has network-layer addresses …

## Slide 7: Addressing: routing to another LAN
A creates IP datagram with IP source A, destination B
  Needs a MAC but can’t be that of B or the local devices won’t pick it up and pass it to their network layer
To get to B, datagram must get to router R
  A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP
Eth
Phy

## Slide 8: Addressing: routing to another LAN
Frame sent from A to R, R gets it, and passes datagram up to IP
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP
Eth
Phy

## Slide 9: Addressing: routing to another LAN
To determine the right interface to use, IP forwarding table
Pass it to the interface, creating a link layer frame with B’s MAC address as destination; the frame has A-to-B IP datagram
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A

## Slide 10: Addressing: routing to another LAN
When the frame arrives, the destination passes the datagram up
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 11: Ethernet
The dominant wired LAN technology
  Alternatives included token ring, FDDI and ATM
Some reasons for domination
  First widely used LAN technology
  Simpler, cheap
  Kept up with speed race (higher data rate was the most compelling reason to change to another LAN technology): 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch (1970s while at Xerox)

## Slide 12: Ethernet: physical topology
Initially and through the mid 90s, a bus
  All nodes in same collision domain (can collide with each other)
Late 90s a move from bus to star with a hub in the center
  Hub – physical-layer device, gets bit, recreates it, boots its energy and drops it on all interfaces
Both bus and hub-based start, broadcast
Early 2000s, a switch instead of hub
  Active, store-and-forward switch in center
  Each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)

## Slide 13: Ethernet frame structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Data (46-1,500B) – Carries the datagram
  If >1,500B – fragment, if <46B, has to be padded; all passed on to network layer which uses the length of IP datagram to remove stuffing
Destination addresses (6B) – destination MAC address
  If adapter receives frame with matching dst address, or with broadcast address FF-FF-FF-FF-FF-FF, it passes data in frame to network layer
  Otherwise, adapter discards frame
dest.
address
source
address
data (payload)
CRC
preamble
type
Notes: We have learn a lot of each protocol we covered by looking at their frame

## Slide 14: Ethernet frame structure
Source address (6B) – MAC address of the source
CRC (4B) – Cyclic redundancy check at receiver (drop on error)
Type (2B) – Indicates higher layer protocol for demultiplexing
  Mostly IP but others possible, e.g., Novell IPX, AppleTalk
  Also ARP has its own type (0806)
Preamble (8B)
  7B ‘10101010’ followed by 1 byte ‘10101011’ (Start Frame Delimiter)
  First 7B to wake up and synchronize receiver’s and sender clock rates, the SFD or its last 2 bits to announce important things are coming up
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 15: Ethernet: unreliable, connectionless
Connectionless – No handshaking between sending and receiving NICs, just send what you have
Unreliable – Receiving NIC doesn't send acks or nacks back if CRC check passes or fails
  Data in dropped frames, gaps, are recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Connectionless and unreliable → a simple and cheap Ethernet
Not one but many different Ethernet standards
  Common MAC protocol and frame format
  Different speeds: 2, 10 and 100 Mbps, 1, 10 and 40 Gbps
  Different physical layer media: fiber, cable, twisted-pair copper
10GBASE-T 10BASE-2
1000BASE-LX

## Slide 16: Ethernet switches (late 1990s–today)
Avoid broadcast and collision – relay msg to the correct port
Switches are store-and-forward devices, like routers
  More complex hardware – parallel packet processing and queueing
If packet is addressed to an unknown address, broadcast to all
Switch allows a subnet to grow very large, as packet flows are isolated from each other and can happen in parallel
No special configuration is required on nodes or in switch
  It’s entirely “plug and play”
  Switch automatically learns MACs of recent senders on each port
If a port is connected to another switch, then it will relay traffic for many MAC addresses

## Slide 17: Switches avoid collision entirely
Switch ports have output queues (like a router), so switch will wait to send a packet until the port is free
  Worst that can happen is that a packet is dropped due to a full queue
Early Ethernet on bus or hub-based start topologies
  A broadcast channel needing CSMA/CD to deal with collisions
Today’s Ethernet uses switched-base start topology
  With a store-and-forward switch
  Modern switches are full-duplex so a node and a switch can send frames to each other without interference
  No collisions – no need for a MAC protocol
  Switch isolates links from each other, so easy to mix legacy and new equipment

## Slide 18: Switches and routers
Network admins sometime have a choice, e.g. connecting departments within a university
Chooses an outbound link using packet’s dst MAC address
Forwarding rules are learned by inspecting traffic
Redundant links are not allowed
No configuration required, just “plug and play”
ARP and DCHP (broadcast) traffic must be sent to all switch ports (on all connected switches)
Chooses an outbound link using packet’s dst IP address
Forwarding rules are decided by IGP and BGP
Routing algorithm chooses shortest among multiple paths
Router must be configured to assign its IP addresses, IGP, etc
Gives adms greater control over where traffic is sent (traffic eng)
Isolates Ethernet broadcasts
Ethernet switch
Router

## Slide 19: VLANs (Virtual LANs)
A switch that supports VLANs can be divide it into multiple virtual switches
  Let large switches to be flexibly configured
  Often configured by port, can also assign MAC addresses to VLANs
Typically used to isolate private subnets for security
Traffic from one VLAN cannot flow into another VLAN
single physical switch ……
… operates as multiple virtual switches
1
2
7
8
9
10
15
16
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
…
9
10
15
16
1
2
7
8
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
…
Notes: A switch is not just a switch

## Slide 20: Multiprotocol label switching (MPLS)
Initially proposed in mid 90s to improve IP router forwarding
  Idea, use a fixed-length label rather than shortest prefix matching
MPLS routers or label-switched routers
  Exchanged labeled packets over Label Switched Paths (LSPs)
  MPLS forwarding table distinct from IP forwarding tables
  Ingress LER is a tunnel entry points, adds the label stack
  Egress LER removes the label stack and does the classic IP lookup
MPLS router
Label Switched Path
Ingress Label Edge Router
Egress Label Edge Router
Notes: A link is not just a link …
The first one is a tunnel entry point, adds the label stack
The last one, exit point, removes the label stack and routes performing the classic IP lookup (this is called Ultimate Hop Popping)

## Slide 21: MPLS headers
Labeled packets are tagged with one or more Label Stack Entries (LSEs), MPLS header, inserted between the frame header (link layer) and the IP packet (network)
PPP or Ethernet header
MPLS header
IP header
Remainder of link-layer frame
20
3
1
5
MPLS label
exp
S
TTL
Exp or service class
Same idea as IP TTL
Bottom of stack flag bit
Used for forwarding

## Slide 22: MPLS versus IP paths
IP routing: path to destination determined by dst address alone
MPLS forwarding decisions can differ from those of IP
  Use dst and src addresses to route flows to same dst differently (traffic engineering)
  Re-route flows quickly if link fails: pre-computed backup paths
R2
Entry router (R4) can use different MPLS routes to A based, e.g., on source address
R1
D
R3
R5
A
R4
R6

## Slide 23: MPLS signaling
Modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing,
  e.g., link bandwidth, amount of “reserved” link bandwidth
  Entry MPLS router uses RSVP-TE signaling protocol to set up MPLS forwarding at downstream routers
R2
D
R3
R5
A
R6
R4
R1
modified
link state
flooding
RSVP-TE

## Slide 24: MPLS forwarding tables
In label | Out label | Dest | Out i/f
 | 10 | A | 0
 | 12 | D | 0
 | 8 | A | 1
In label | Out label | Dest | Out i/f
10 | 6 | A | 1
12 | 9 | D | 0
In label | Out label | Dest | Out i/f
8 | 6 | A | 0
In label | Out label | Dest | Out i/f
6 | - | A | 0
D
R3
R5
A
R6
R4
R2
R1
0
1
0
1
0
0

## Slide 25: Data center networks
Google, Microsoft, Amazon, … building big data centers
  Housing 10s or 100s of thousands of machines
A fast and efficient DCN is key
Much work on design of DCN
  Topologies
  Routing
  Container-based modular data centers
  Reliability
Server racks
Top-of-rack switches
Tier-1 switches
Tier-2 switches
Access routers
Border routers
Internet
…
…
Load balancer

## Slide 26: A recap of sorts … visiting www.google.com?
web page
school network
165.124.160.0/20
Comcast network
68.80.0.0/13
DNS server
Google’s network
64.233.160.0/19
64.233.169.105
web server
Notes: You boot up your laptop, connect it to an Ethernet cable, and try to get to the google landing page …
The school upstream provider is comcast who also provides the DNS service for the school
First thing first, you need an IP

## Slide 27: What happens when visiting www.google.com?
Connecting laptop needs to get its own IP address, address of first-hop router, address of DNS server: use DHCP
OS creates a DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FF:FF:FF:FF:FF:FF) on LAN, received by router running DHCP server
Ethernet unpacked to get IP, unpacked to get UDP, unpacked to get DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
Notes: DHCP destination port is 67, source port is 68
UDP segment is encapsulated in an IP datagram with a broadcast IP destination 255.255.255.255 and a source IP 0.0.0.0
The IP datagram is placed within an Ethernet frame and broadcasted; source MAC address is the client’s
Switch broadcasts the incoming frame on all outgoing ports, including the one connected to the router running the DHCP server
IP datagram is extracted, destination address means it should be processed by upper layer, payload (UDP) is demultiplexed to to UDP, DHCP request is extracted

## Slide 28: Connecting to network (continued)
DHCP server creates DHCP ACK containing client’s IP address, IP address of first-hop router for client, subnet mask, & IP address of DNS server
Encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client receives DHCP ACK
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
Notes: DHCP reply is encapsulated in a UDP segment, which is put inside a IP datagram which is put inside an Ethernet frame which has a destination MAC address of the client
The self-learning switch that receives the frame has seen the MAC address of the client and know to forward only to the output port leading to the client’s machine
The client has now its IP address, that of its DNS server, the default gateway (which adds to its IP forwarding table) – any packet going to a destination outside its own subnet will go to the default gateway

## Slide 29: ARP (before DNS, before HTTP)
Before sending HTTP request, we need to send a DNS request to get IP address of www.google.com
Create DNS request, inside UDP segment, inside IP datagram, inside Ethernet frame, but we don’t yet have the MAC address of the router to set as the first-hop Ethernet destination
Client broadcasts ARP query listing the router’s IP address. Router replies with its MAC address (on that subnet)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
ARP query
Eth
Phy
ARP
ARP
ARP reply
Notes: OS creates a DNS request …
The frame containing the UDP segment containing the DNS request will be sent to the gateway router but while the client knows the IP doesn’t know the MAC of the gateway router

## Slide 30: DNS
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via switch from client to 1st hop router
… from campus network into Comcast network, routed (tables already created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
DNS server replies with IP address of www.google.com

## Slide 31: TCP
Google’s network
64.233.160.0/19
64.233.169.105
web server
To send HTTP request, client opens TCP socket to server on port 80
TCP SYN packet sent -- step 1 of 3-way handshake
Server sends SYN-ACK – step 2 of 3-way handshake
TCP connection established!
HTTP
TCP
IP
Eth
Phy
HTTP
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK

## Slide 32: HTTP request/reply
Google’s network
64.233.160.0/19
64.233.169.105
web server
HTTP request sent into TCP socket
  IP datagram containing request routed to google.com
Web server replies with HTTP response (incl. web page)
  IP datagram containing response routed back to client
HTTP
TCP
IP
Eth
Phy
HTTP
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
The End